Oil Leak Diagnosis

Meets NATEF Task:  (A8-A-4)  Inspect engine assembly for fuel, oil, coolant, and other leaks; determine necessary action.  (P-2)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

Engine oil is usually amber in color when new, but quickly becomes darker and often black when used in an engine.   Other fluid colors include the following:

- red – automatic transmission fluid (also used in some power steering units)

- green – antifreeze coolant

- orange – antifreeze coolant

- blue – antifreeze coolant or windshield washer fluid

- yellow – windshield washer fluid

- clear – condensation from the air-conditioning system (normal)

_____  1.  Raise the hood and carefully inspect the areas where oil is likely to leak including:

valve covers	                	– OK _____     NOT OK _____

intake manifold area        	– OK _____     NOT OK _____

oil pressure-sending unit 	– OK _____     NOT OK _____

_____  2.  Safely hoist the vehicle and carefully inspect the underneath of the engine.

_____  3.  Where is the highest, most forward area of the leak? (describe)  ________________

___________________________________________________________________

_____  4.  If the exact location cannot be located, lower the vehicle and add fluorescent dye to

the engine oil.  Drive the vehicle for 10 to 15 minutes and hoist the vehicle.

_____  5.  Using black light, locate the area of the leak by looking for the yellow/green areas

highlighted by the dye.  Describe the leak location:

____________________________________________________________

### _____  6.  Based on the test results, what is the necessary action? _________________________

__________________________________________________________________