Power Balance – Manual Method

Meets NATEF Task:  (A8-A-6)  Perform cylinder balance test; determine necessary action.    (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____ 1.  Check service information for the recommended method and procedures to follow for

performing a power balance test without the use of a scan tool.

_____  2.  One method uses a 2" long vacuum hose between the distributor cap (or coils) and the

spark plug wires.

_____ 3.  Connect the tachometer to the engine and record idle RPM = ____________.

_____ 4.  Using a test light, ground out one cylinder at a time by touching the tip of the grounded

test light to the section of rubber hose, and record the RPM drop:

#1 _________      #5 __________

#2 _________      #6 __________

#3 _________      #7 __________

#4 _________      #8 __________

NOTE:  50 RPM is the maximum variation between cylinders.  The cylinder that drops

the most RPM is the strongest cylinder.  The cylinder that drops RPM the least is the

weakest cylinder.

_____ 5.  Results:

RPM difference between the strongest and weakest cylinder _____________.

Which cylinder is the strongest? _____________.

Which cylinder is the weakest? _____________.

_____  6.  Based on the test results, what is the necessary action? _________________________

__________________________________________________________________