Compression Testing

Meets NATEF Task:  (A8-A-7)  Perform cylinder cranking and running compression tests; determine necessary action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Remove all spark plugs (be certain to label the spark plug wires).

_____  2.  Block open the throttle and choke (if equipped).

_____  3.  Perform compression testing during cranking (4 "puffs").

NOTE:  For accurate test results, the engine should be at

normal operating temperature.  The 1st puff should be at

least 50% of the final puff.  (A low 1st puff reading indicates

possible weak piston rings.)

RESULTS:     1st puff/final reading               1st puff/final reading

1.  ___________/__________  5.  ___________/__________

2.  ___________/__________  6.  ___________/__________

3.  ___________/__________  7.  ___________/__________

4.  ___________/__________  8.  ___________/__________

_____  4.  Perform a wet compression test on any cylinder that reads lower-than-normal on the

cranking compression test.  Add about 1 ounce of engine oil to the cylinder and repeat

the test.

Cranking Compression Reading	Wet Compression Reading

Cylinder #1	___________________________	_______________________

Cylinder #2     ___________________________	_______________________

Cylinder #3	___________________________	_______________________

Cylinder #4     ___________________________	_______________________

Cylinder #5	___________________________	_______________________

Cylinder #6     ___________________________	_______________________

Cylinder #7	___________________________	_______________________

Cylinder #8     ___________________________	_______________________

If the wet compression reading is a lot higher than the cranking compression reading,

the piston rings are worn.

_____  5.  Based on the test results, what is the necessary action?  ________________________