Running Compression Test

Meets NATEF Task:  (A8-A-7)  Perform cylinder and running compression tests; determine necessary action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Perform a normal cranking compression test to eliminate obvious engine mechanical

faults.

_____  2.  Install the spark plugs except for one.  Use a jumper wire on the one remaining spark

plug wire and connect the spark plug wire to ground to prevent damage to the coil or

the ignition control module.

_____  3.  Install the compression gauge, start the engine, and operate at idle speed (push on the

Schrader valve and release the pressure every 5 or 6 “puffs”).

_____  4.  Snap open the accelerator and note the gauge reading.  It should increase.

_____  5.  Record all cylinders for running (idle) and snap accelerator readings.

Cylinder #1    Idle _____  Snap _____      Cylinder #5   Idle _____   Snap _____

Cylinder #2    Idle _____  Snap _____      Cylinder #6   Idle _____   Snap _____

Cylinder #3 	Idle _____ Snap _____      Cylinder #7   Idle _____   Snap _____

Cylinder #4     Idle _____ Snap _____      Cylinder #8   Idle _____   Snap _____

_____  6.  Analysis:

Running compression at idle speed should be about half of the cranking

compression test (60 to 80 psi).  ____ OK    ____ NOT OK

Snap throttle compression should be about 80% of the cranking compression (100

to 130 psi).

- All cylinders should be within 10% of each other on both tests.

- If the snap throttle or idle reading is low, look for a restricted intake, worn cam lobe, bent pushrod, or defective rocker arm.

- If the snap throttle reading is higher than 80% of the cranking compression test, look for a restricted exhaust on that cylinder, such as a worn exhaust cam lobe or a collapsed lifter.  If all cylinders are high on the snap throttle test, look for a restricted catalytic converter or other restriction.

_____  7.  Based on the test results, what is the necessary action? _________________________