Verify Engine Operating Temperature

Meets NATEF Task:  (A8-A-10) Verify engine operating temperature; determine necessary

action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for specified engine operating temperature, which is

generally between the thermostat temperature rating and 20°F above the thermostat

temperature.

Thermostat temperature = ______

Normal coolant temperature range = ______

| Thermostat Temperature | Normal Operating Temperature |
| --- | --- |
| 180°F (82°C) | Between 180° and 200°F (82° and 93°C) |
| 195°F (91°C) | Between 195° and 215°F (91° and 102°C) |

_____  2.  Determine the operating temperature of the engine by as many methods as possible

including:

- Dash temperature gauge = _______

- Scan tool (ECT) = _______

- Infrared pyrometer = _______

- Other (specify) _______

_____  3.  Based on the result of the engine operating temperature measurements, what is the

necessary action?

__________________________________________________________________

__________________________________________________________________