Battery Load Test

Meets NATEF Task:  (A6-B-2)  Perform battery capacity test; confirm proper battery capacity for vehicle application; determine necessary action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Connect the carbon pile tester, such as a Sun Electric VAT-40, as per the test

equipment manufacturer's instructions.

_____  2.  Determine the correct amount of load (1/2 CCA of the battery) = _____ amps.

_____  3.  Remove the surface charge by applying load of one-half of the CCA rating of the

battery for 15 seconds.  Let the battery "recover" for 30 seconds.

_____  4.  Apply the same load again for 15 seconds.  With the load still applied, read the battery

voltage.

Battery voltage at the end of the 15-second load = ________ volts.

RESULTS:  The battery voltage should be greater than 9.6 volts at the end of 15 seconds

with the electrical load still applied.  If the battery voltage is below 9.6 volts,

recharge the battery and repeat the test.  If the second test also indicates less

than 9.6 volts, replace the battery.

OK_____   NOT OK_____

_____  5.  Based on the test results, what is the necessary

action?

__________________________________

__________________________________

__________________________________

__________________________________