Starting and Charging Tests

Meets NATEF Task:  (A6-A-7)  Demonstrate proper use of electrical test equipment.

(P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  General Voltmeter Test

a.  battery voltage    	= _______ (Remove the surface charge.)

b.  cranking voltage 	= _______ (Should be above 9.6 volts.)

c.  charging voltage 	= _______ (Should be 13.5=15.0 volts.)

_____  2.  Voltage-Drop Testing

Connect the red voltmeter lead to the most positive (+).

Connect the black voltmeter lead to the most negative (-).

Crank the engine.  (Voltage drop should not exceed .2 volt.)

Voltage drop across the positive (+) cable(s)	= ________.

Voltage drop across the negative (-) cable    	= ________.

Voltage drop across the solenoid              	= ________.

_____  3.  Battery Load Test  Load the battery to 1/2 CCA for 15 seconds.

CCA = __________.    Load to = ___________.

Terminal voltage at the end of 15 seconds = _______.  (should be above 9.6 volts)

_____4.  Starter Amperage Test

4 and 6 cylinders = 150 A. maximum.  V-6 and V-8 = 200 A. maximum.

GM V-8 = 250 A. maximum.

Cranking amps = _____________.		OK_____   NOT OK_____

_____  5.  Generator Output Test  	At 2,000 engine RPM:

_____amps tested  _____amps specifications  OK____  NOT OK___

(Results should be within 10% of specifications.)

_____  6.  Charging System Requirement Test

(Turn on all accessories, read the ammeter, add 5A.)  = ______ amps.