Optical Distributor Scope Test

Meets NATEF Task:  (A8-C-2) Inspect and test ignition primary and secondary circuit wiring and solid state components; determine  necessary action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the recommended procedures and specifications for

testing the optical distributor. _____________________________________________

_____  2.  Locate and carefully back probe the low resolution and high resolution signal wires at

a connector near the distributor.  (Refer to the service information for the correct

connector and color of the wires.)

_____  3.  Connect the scope probe lead to one of the terminals

and connect the probe ground lead to a good engine

ground.

_____  4.  Set the scope settings as follows:

Volts per Division = 2 volts DC

Time per division  = 500 (S (500 microseconds)

Trigger Level        = 1 V. (50%)

Trigger Slope        = positive (+)

_____  5.  Start the engine and observe the waveform.  The waveform should have vertical rising

and falling edges and the ground signal (horizontal bottom portion of the waveform)

should be close to zero volts.  Draw the waveform here:

_____  6.  Connect the scope to the high resolution signal wire.  Carefully verify that all rising

and falling edges are vertical and that the ground signal should be close to zero.  Draw

the waveform here:

_____  7.  Based on the test results, what is the necessary action? _________________________

_________________________________________________________________