Ignition Primary Wiring and Components

Meets NATEF Task:  (A8-C-3)  Inspect and test ignition primary circuit wiring and solid state components; test ignition coil(s); perform necessary action.  (P-3)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the recommended

testing procedures and specifications for testing and

inspecting the primary ignition circuit wiring and

components.

______________________________________

______________________________________

______________________________________

_____  2.  List the wiring and the components included in the primary ignition circuit:

a.  _________________   d.  __________________   g.  _________________

b.  _________________   e.  __________________    h.  _________________

c.  _________________   f.  __________________    j  .  _________________

_____  3.  What meter measurements are specified?  Check all that apply.

a.  Voltage input to the ignition switch.	Specification _____  Actual _____

b.  Voltage output from the ignition switch.	Specification _____  Actual _____

c.  Voltage at ignition coil(s).			Specification _____  Actual _____

d.  Voltage drop of ground circuit.		Specification _____  Actual _____

e.  Primary circuit current (amperes).		Specification _____  Actual _____

_____  4.  Based on the tests, what is the necessary action? ______________________________

__________________________________________________________________