Waste Spark Ignition Inspection and Testing

Meets NATEF Task:  (A8-C-1)  Diagnose ignition system-related problems; determine necessary action.  (P-2)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information and determine the type of waste spark-type ignition with

which you are working:

_____  GM (Magnavox - 3 coils in one unit)

_____  GM (AC Delco - individual coils)

_____  Ford

_____  DaimlerChrysler

_____  Other (specify) __________________

_____  2.  What type of triggering system is used to

signal the ignition module?

______________________________________

_____  3.  Test the coils for output by unplugging a spark plug wire and attaching a spark tester

(ST-125).  Start the engine.  The spark tester should spark continuously.

_____  4.  Repeat #3 for all cylinders.    OK _____     NOT OK _____

_____  5.  Install 2" lengths of vacuum hose between the coil terminals and

spark plug wire.  Using a test light, ground out one cylinder at a

time.

a.  Did all cylinders drop in RPM when grounded? _____

If not, which cylinder did not drop in RPM? _____

- If a cylinder RPM does not drop when the plug wire is grounded, what items

could be defective?   ____________________________________________

- By grounding out one spark plug wire, does it ground out one or two

cylinders?  _____

_____  6.  Based on the test results, what is the necessary action? _________________________