Misfire Monitor Activity

Meets NATEF Task:  (A8-B-4)  Diagnose driveability and emissions problems; determine necessary action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the details regarding how

the misfire monitor reacts to a misfire and under what

engine operating conditions.

__________________________________________

__________________________________________

_____  2.  Connect a scan tool to the data link connector (DLC) and create a misfire.  (Use a

spark tester connected to one removed spark plug wire to create an ignition misfire

without doing any harm to the vehicle.)

_____  3.  Observe the misfire monitor on the scan tool and record. _______________________

_________________________________________________________________

_____  4.  Rapidly depress the accelerator pedal to wide-open throttle (WOT) a few times.  Did

the misfire monitor change?

____ Yes   ____ No  Explain: _________________________________________

__________________________________________________________________

_____  5.  Turn the ignition key off, and then back on.  Did a misfire diagnostic trouble code

(DTC) set?

____ Yes   ____ No

_____  6.  Check freeze frame information on the scan tool.  Was freeze frame stored?

____ Yes   ____ No  Why? ___________________________________________

_____  7.  Based on this activity, what action is necessary? ______________________________

__________________________________________________________________