## Slide 1: Automatic Transmissions and Transaxles
Seventh Edition
Chapter 16
Valve Body Service

## Slide 2: FIGURE 16–1 (a) An exploded and (b) cutaway view of the valve body from a four-speed transaxle. Note the various valve groups and how they are retained in their bore.

## Slide 3: FIGURE 16–2 If the valve body is moved to a vertical position, steel valves should slide freely from the bore. Be prepared to catch the valves when making this check.

## Slide 4: FIGURE 16–3 A valve body being washed and air dried in a parts washer. It will be cleaned again when the two major parts are separated.

## Slide 5: FIGURE 16–4 A sheet of stiff paper has been folded to create this simple valve holder. Note that a valve group can be placed in order and be labeled.

## Slide 6: FIGURE 16–5 (a) Ohmmeter A is checking for a grounded solenoid coil; the reading should be infinite. Ohmmeter B is measuring the coil resistance; it should be within the specifications for this solenoid. (b) Connecting a solenoid to a 12-V battery should cause it to operate. Make sure the battery is connected using the correct polarity in case the solenoid has an internal diode.

## Slide 7: FIGURE 16–6 Air should not be able to flow through this solenoid if it is not activated. If it is connected to a 12-V battery, it should make a “click,” and air should be able to flow through it.

## Slide 8: FIGURE 16–7 Using assembly lube is a great way to keep check balls in place during the reassembly of the valve body.

## Slide 9: FIGURE 16–8 The valve body bolts should be tightened in order, starting from the center and working in an outward spiral.

## Slide 10: FIGURE 16–9 A check ball should seal off light from coming through the spacer plate. A problem is indicated if light shines through an opening alongside of the check ball.

## Slide 11: FIGURE 16–10 The manual valve is moved by the shift lever and held in position by the detent lever (cam).