Bench Bleeding the Master Cylinder

Meet NATEF Task:  (A5-B-4) Bench bleed master cylinder. (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

Before a replacement master cylinder is installed in a vehicle, most vehicle manufacturers recommend that the master cylinder be bled.

_____  1.  Clamp the ears of the master cylinder in a

suitable vise.

CAUTION:  Do not clamp the body of the master cylinder or bore distortion can occur.

_____  2.  Install tubes into the outlets of the master

cylinder and direct the tubes near the top

of the open reservoir.

_____  3.  Fill the master cylinder reservoir with clean DOT 3 brake fluid from a sealed

container.

_____  4.  Using a blunt tool, such as a rounded dowel rod or a Phillips screwdriver, slowly

stroke the master cylinder.

_____  5.  Continue stroking the master cylinder until a solid stream of brake fluid is observed

flowing out of the tubes and into the reservoir.

_____  6.  Remove the bleeding tubes and unclamp the master cylinder.  The master cylinder can

now be installed on the vehicle where additional bleeding at the outlet fitting may be

necessary.