Hydraulic System Fault Analysis

Meet NATEF Task:  (A5-B-5) Diagnose braking concerns caused by hydraulic malfunctions. (P-3)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

Poor stopping or dragging brakes or pulling can be caused by hydraulic system failure or faults.

_____  1.  Check master cylinder for proper brake fluid level and condition.

_____  2.  Verify proper operation of the base brakes.

_____  OK

_____  Pulls to the left during braking (see Step 3).

_____  Pulls to the right during braking (see Step 3).

_____  Brakes do not release fully (see Step 4).

_____  Poor stopping (see Step 5).

_____  Other brake system concerns (describe) ____________________________

_____  3.  Pulling can be caused by a stuck caliper piston on the side opposite the direction of the

pull.

If there is a pull to the right during braking, check the left side caliper.

#### OK ____   NOT OK ____

If there is a pull to the left during braking, check the right side caliper.

#### OK ____   NOT OK ____

_____  4.  Brakes that do not fully release can be caused by a fault with the flexible brake hose

and/or a stuck caliper piston

#### Visually check the flexible brake hose.     OK ____   NOT OK ____

Check that the caliper piston can be moved into the caliper bore easily.

#### OK ____   NOT OK ____

_____  5.  Poor stopping can be caused by a stuck caliper or wheel cylinder piston.  Check that

all hydraulic pistons are free.

LF = OK ____   NOT OK ____	LR = OK ____   NOT OK ____

RF = OK ____   NOT OK ____ 	RR=  OK ____   NOT OK ____