### Pressure Differential Switch Inspection

Meet NATEF Task:  (A5-B-10) Inspect, test, and/or replace metering (hold-off) proportioning (balance), pressure differential, and combination valves.  (P-3)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  A pressure-differential switch is used on all vehicles built after 1967 with dual master

cylinders to warn the driver of a loss of pressure in one of the two separate systems by

lighting the dashboard red brake warning indicator lamp.

_____  2.  The brake lines from both the front and the rear sections of the master cylinder are

sent to this switch which lights the brake warning indicator lamp in the event of a

"difference in pressure" between the two sections.

_____  3.  A failure in one part of the brake

system does not result in a failure of

the entire hydraulic system.  After

the hydraulic system has been

repaired and bled, moderate

pressure on the brake pedal will

center the piston in the switch and

turn off the warning lamp.

_____  4.  If the lamp remains on, it may be

necessary to:

A.   Apply light pressure to the brake pedal.

B.   Momentarily open the bleeder valve on the side that did not have the failure.

This procedure should center the pressure differential switch valve in those

vehicles not equipped with self-centering springs.

_____  5.  State the vehicle manufacturer’s recommended inspection, testing, and replacement

procedures:

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________