Gravity Brake Bleeding

Meets NATEF Task:  (A5-B-12) Bleed and/or flush the brake system.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check the service information for the specified brake bleeding procedure for the

vehicle being serviced.

_____  2.  Fill the master cylinder reservoir with clean brake fluid from a sealed container.

_____  3.  Hoist the vehicle safely.

_____  4.  Open the right rear bleeder valve and

wait until about a drip-per-second of

brake fluid is observed coming out of

the bleeder valve and close the bleeder

valve.

_____  5.  Repeat the bleeding procedures for the

left-rear, right-front, and then the

left-front wheel brakes.

_____  6.  After all four wheel brakes have been bled, lower the vehicle and fill the master

cylinder to the full mark.

CAUTION: Check the master cylinder reservoir frequently and refill as necessary with clean brake fluid.  Do not overfill a master cylinder reservoir.

_____  7.  Test drive the vehicle checking for proper brake operation before returning the vehicle

to the customer.