Brake Fluid Flush and Fill

Meets NATEF Task:  (A5-B-12) Bleed and/or flush brake system.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

Many vehicle manufacturers recommend the replacement of brake fluid every 2 or 3 years (24,000 - 36,000 miles or 38,000 - 58,000 km).

_____  1.   Check the service information for the specified brake

bleeding procedure for the vehicle being serviced.

____________________________________________

____________________________________________

_____  2.  Use a turkey baster or similar tool to remove most of the old

brake fluid from the master cylinder reservoir.

_____  3.  Refill the master cylinder with new brake fluid from a sealed

container.

_____  4.  Hoist the vehicle safely.

_____  5.  Bleed the brake fluid from the right rear wheel brake until clean brake fluid is

observed.

_____ 6.  Repeat the bleeding process for the left rear, right front, then the left front wheel

brakes.

NOTE:  Check the level of the brake fluid often and refill as necessary.  Do not allow the master cylinder reservoir to become empty.

_____  7.  After all the wheel brakes have been bled with clean brake fluid, lower the vehicle

and test drive checking for proper operation of the brakes before returning the vehicle

to the customer.