### Pre-Adjustment of Brake Shoes

Meets NATEF Task:  (A5-C-6) Pre-adjust brake shoes and parking brake; install brake drums or drum/hub assemblies and wheel bearings. (P-2)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

Brake shoes should be pre-adjusted to close to the working clearance between the brake shoes and the brake drum before the brake drum is installed.

_____  1.  Assemble the drum brake and verify that all parts are properly lubricated.

_____  2.  Using a brake shoe clearance gauge, insert it

into the drum and turn the lock knob to

hold the setting.

_____  3.  Install the brake shoe clearance gauge over the brake shoes and turn the adjuster until

the lining contacts the gauge.

_____  4.  Verify the pre-adjustment by installing the drum.  It should slide over the brake shoes

with little clearance.

OK _____     NOT OK _____