### Disc Brake Caliper Assembly

Meets NATEF Task:  (A5-D-6) Reassemble, lubricate and reinstall the calipers, pads, and related hardware, seat pads, and inspect for leaks. (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

### _____  1.  Check the service information for the specified procedure to follow for reassembly of

### the caliper assembly. ____________________________________________________

### _________________________________________________________________

### _____  2.  The procedure usually includes the following steps.

### A.  Thoroughly clean the caliper using

### denatured alcohol.

### B.   Install new square-cut O-rings into the

### groove in the caliper bore and coat the

### bore and seal with clean brake fluid from

### a sealed container.

### C.   Lubricate the caliper piston with clean

### brake fluid and install the caliper

### piston dust boot on the piston and then

### install the piston into the bore.

### D.   Seat the caliper piston dust seal.

E.   Seat the pads as specified by the service information.

__________________________________________

__________________________________________

__________________________________________

F.   Install the caliper on the vehicle.

### _____  3.  After installation of the caliper and pads, bleed the system.

_____  4.  Check for leaks and proper operation.