Brake Drum Measurement

Meets NATEF Task:  (A5-C-2) Remove, clean, inspect, and measure brake drums; determine necessary action. (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Wet the brake drum or use an enclosure to help

protect against asbestos exposure.

_____  2.  Remove the brake drum from the vehicle and

label the left and right to ensure that the

drum is replaced in the original location.

_____  2.  Thoroughly inspect the brake drum.

- Hot (hard) spots

OK_____    NOT OK_____ (requires replacement)

- Tap with a hammer.  The brake drum should ring like a bell if not cracked.

OK_____    NOT OK_____  (requires replacement)

_____  3.  Determine the maximum allowable inside diameter of the brake drum or the

maximum “turn to” dimension.

Maximum allowable inside diameter = ___________  (allow 0.030” for wear)

Maximum “turn to” diameter = ___________

_____  4.  Measure the drum using a drum micrometer.

Left = __________     Right = ___________

OK to machine ______   NOT OK to machine ______

_____  5.  Based on the inspection, what is the necessary action? _________________________

_________________________________________________________________