Brake Rotor Measurement

Meets NATEF Task:  (A5-D-6)Clean, inspect, and measure rotor thickness, lateral runout, and thickness variation; determine necessary action. (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Visually inspect the brake rotor for:

- hard spots		OK ____     NOT OK ____  (requires replacement)

- excessive rust        OK ____     NOT OK ____

- deep grooves (over 0.060” deep)   OK ____     NOT OK ____

_____  2.  Check the service information and determine the specifications and measurements for

thickness.

Minimum thickness = ________

Machine-to-thickness = ________

Actual thickness = _________ OK ____     NOT OK ____

_____  3.  Determine the specifications for thickness variation (parallelism).

___________________________

_____  4.  Using a micrometer, measure the thickness at four or more locations around the rotor

to determine the thickness variation (parallelism).  (Usually 0.0005" or less difference

in the readings.)

A.  ________		C.  ________		E.  ________

B.  ________		D.  ________		F.  ________

OK ____	NOT OK ____

_____  5.  Use a dial indicator and measure the runout of the rotor.

Runout = ____________ (should be less than 0.005 in.)

OK ____	NOT OK ____

______  6.  Based on the measurements and manufacturer’s

recommendations, should the rotor be replaced or machined?

Why?  __________________________________________

_______________________________________________