On-the-Vehicle Lathe

Meets NATEF Task:  (A5-D-8) Refinish rotor on the vehicle; measure final rotor thickness.

(P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Hoist the vehicle safely to the proper height according to the lathe manufacturer's

instructions.

_____  2.  Mount the on-the-vehicle lathe according to the lathe manufacturer's instructions and

calibrate the lathe as necessary.

NOTE:  On caliper mounted on-the-vehicle lathe, the disc brake caliper must be removed and supported with a wire to help prevent damage to the hydraulic flexible brake line.

_____  3.  Machine the rotor following the lathe manufacturer's instructions.

_____  4.  Use 150 grit aluminum oxide sandpaper on a block or a grinding disc to provide the

required smooth non-directional finish.

_____  5.  Thoroughly clean both disc brake rotors before installing the replacement disc brake

pads and reinstalling the disc brake caliper.

NOTE:  Be sure to install all anti-noise shims and hardware.

_____  6.  Reinstall the front wheels and tighten the lug nuts in a star pattern (tighten one, skip

one, etc.) using a torque wrench on a torque-limiting adjuster with an air impact

wrench.

_____  7.  Lower the vehicle and depress the brake pedal several times to achieve proper brake

pedal height.

### _____  8.  Test drive the vehicle before returning the vehicle to the customer.