Vacuum-Type Power Booster

Meets NATEF Task:  (A5-E-3) Inspect vacuum-type power booster unit for vacuum leaks; inspect the check valve for proper operation; determine necessary action. (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the recommended procedures to follow to determine if

a vacuum-type power brake booster has a vacuum leak.

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_____  2.  Most vacuum-type power boosters should be capable of supplying 3 or more assisted

stops with the engine off.  How many were found?    __________

_____  3.  Most vehicle manufacturers specify checking for leaks both around the outside (under

the hood), as well as in the valve area under the dash.

Under hood:

____  OK    ____  NOT OK

Valve area:

____  OK    ____  NOT OK

_____  4.  Based on the test results, what is the necessary action?  ________________________

__________________________________________________________________