Hydro-Boost Test

Meets NATEF Task:  (A5-E-4) Inspect and test hydro-boost system for leaks and proper

operation. (P-3)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check the service information for the specified Hydro-Boost testing procedure for the

vehicle being serviced.

_________________________________________________________________

_____  2.  Start the testing of a Hydro-boost power brake assist system by carefully inspecting

the following components:

Power steering fluid level			OK _____   NOT OK _____

Power steering pressure hoses for leaks	OK _____   NOT OK _____

Power steering pump drive belt		OK _____   NOT OK _____

Master cylinder brake fluid level		OK _____   NOT OK _____

Visually inspect the Hydro-boost assembly

for evidence of power steering fluid leaks	OK _____   NOT OK _____

_____  3.  Check the operation of the base hydraulic brakes by depressing the brake pedal several

times with the engine "off" until the brake pedal feels firm.  Continue to apply force to

the brake pedal.  The brake pedal should not drop.

OK _____   NOT OK _____(master cylinder or hydraulic system fault is

indicated)

_____  4.  With your foot still applying force to the brake pedal, start the engine.  If the

Hydro-boost system is functioning correctly, the brake pedal should drop.

OK _____   NOT OK _____

_____  5.  To check the power steering pump for proper operation,

connect a power steering pressure gauge or pressure and

volume gauge between the pump and the Hydro-boost

unit.  Start the engine and observe the pressure and

volume gauges.

Pressure at idle = _________

(should be less than 150 psi)

OK _____   NOT OK _____

Volume at idle = __________

(should be at least 2 gallons per minute)

OK _____   NOT OK _____