ABS Component Inspection

Meets NATEF Task:  (A5-G-1) Identify and inspect electronic brake control system components; determine needed action. (P-3)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check the brake fluid level and condition in the master

cylinder.

OK _____     NOT OK _____

Describe ____________________________

______________________________

_____  2.  Check the brake fluid level and condition in the ABS reservoir if equipped.

_____ Not equipped with an ABS brake fluid reservoir

OK _____     NOT OK _____  Describe ________________________________

_____  3.  Visually check the hydraulic control unit and accumulator for leakage or physical

damage.

OK _____     NOT OK _____  Describe ________________________________

_____  4.  Visually check all wheel speed sensors and tone wheel for damage or debris.

OK _____     NOT OK _____  Describe ________________________________

_____  5.  Visually inspect the wheel speed sensor wiring harness for damage.

OK _____     NOT OK _____  Describe ________________________________

_____  6.  Visually inspect the ABS controller for damage or corroded connection(s).

OK _____     NOT OK _____  Describe ________________________________

_____  7.  Based on the inspection, what is the necessary action? _________________________