## Slide 1: Light Vehicle Diesel Engines
First Edition
Chapter 1
Diesel Engine Operation
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
1.1 Prepare for the light Vehicle Diesel engine (A9) ASE certification test content area “A” (general Diagnosis).
1.2. Explain how a four-stroke cycle engine operates.
1.3. List the various characteristics by which vehicle engines are classified.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
1.4 Discuss how a compression ratio is calculated.
1.5 Explain how engine size is determined.
1.6 Describe how displacement is affected by the bore and stroke of the engine.

## Slide 4: ENGINES (1 of 2)
Purpose/Function of Engine
  Convert heat energy into mechanical energy
    Mechanical energy
      Propel vehicle
      Power air-conditioning & power steering
      Produce electrical power
    Chemical energy in fuel is converted to heat energy
    By burning fuel at controlled rate

## Slide 5: ENGINES (2 of 2)
Combustion
  Chemical energy converted to heat energy
  By burning diesel fuel at a controlled rate
    Convert diesel fuel energy into heat
    Within a combustion chamber
    Combustion occurs above piston
    Called internal combustion engine

## Slide 6: FOUR-STROKE CYCLE OPERATION (1 of 1)
4-Stroke Cycle
  Developed by Nikolaus Otto
Stroke
  Movement of piston from TDC to BDC
  Piston moves up and down, or
    Reciprocates (moves up and down) in a cylinder
    Piston is attached to crankshaft with connecting rod

## Slide 7: FIGURE 1–1 In diesel engine downward movement of piston draws air into cylinder through intake valve on intake stroke. On compression stroke, air is compressed by upward movement of piston with both valves closed. Fuel is injected and ignition occurs at beginning of power stroke, and combustion drives the piston downward to produce power. On exhaust stroke, upward-moving piston forces burned gases out open exhaust valve.

## Slide 8: QUESTION 1: ?
Which engine stroke brings in air?

## Slide 9: ANSWER 1:
Intake.

## Slide 10: ENGINE CONSTRUCTION OVERVIEW (1of 3)
BLOCK
  Solid frame, called an engine block
  Constructed of cast iron or aluminum
  Provides foundation for engine components & systems.

## Slide 11: FIGURE 1–2 Cutaway of a diesel engine showing the cylinder, piston, connecting rod, and crankshaft.

## Slide 12: ENGINE CONSTRUCTION OVERVIEW (2 of 3)
ROTATING ASSEMBLY
  Pistons are installed in block
  Move up and down during engine operation
  Connected to connecting rods
  Connect pistons to crankshaft
  Crankshaft converts up/down piston motion
  To rotary motion, transmitted to drive wheels

## Slide 13: FIGURE 1–3 Rotating assembly for a V-8 engine that has 8 pistons and connecting rods, and one crankshaft.

## Slide 14: ENGINE CONSTRUCTION OVERVIEW (3 of 3)
CYLINDER HEAD
  Seals top of cylinders in engine block
  Contains both intake valve that allow air & and fuel in
  Exhaust valves, which allow spent gases out
  Constructed of cast iron or aluminum
  Machined for valves

## Slide 15: FIGURE 1–4 A cylinder head with four valves per cylinder, two intake valves (larger) and two exhaust valves (smaller).

## Slide 16: DIESEL ENGINES (1 of 10)
Compression Ignition Engine
  Invented by Rudolf Diesel (1858–1913)
  Uses heat created by compression to ignite fuel
  Requires compression ratios of 16:1 & higher
  Incoming air is compressed until the temperature
    reaches about 1,000°F (540°C) heat of compression
  Piston reaches TDC, fuel is injected into cylinder
  Ignited by hot air
  As fuel burns, it expands and produces power

## Slide 17: FIGURE 1–5 Diesel combustion occurs when fuel is injected into the hot, highly compressed air in the cylinder.

## Slide 18: DIESEL ENGINES (2 of 10)
Diesel Engine Advantages
  Compared to a similar size gasoline engine:
    1. More torque output
    2. Greater fuel economy
    3. Long service life

## Slide 19: DIESEL ENGINES (3 of 10)
Diesel Engine Disadvantages
  Compared to a similar size gasoline-powered engine:
    1. Engine noise, especially when cold and/or idling
    2. Exhaust smell
    3. Hard starting in cold weather
    4. Overall weight, heavier than a gasoline engine
    5. Fuel availability
    6. Extra cost compared to a gasoline engine

## Slide 20: CHART 1-1 Comparison between a typical gasoline and a diesel engine.

## Slide 21: DIESEL ENGINES (4 of 10)
Indirect Diesel Injection (IDI)
  Fuel injected into small pre-chamber
  Connected to cylinder by narrow opening
  Initial combustion takes place in pre-chamber
  Slowing rate of combustion, reduces noise
  Requires use of a glow plug for cold starts

## Slide 22: FIGURE 1–6 indirect injection IDI diesel engine uses a prechamber and a glow plug.

## Slide 23: DIESEL ENGINES (5 of 10)
Diesel Injection (DI)
  Fuel injected directly into cylinder
  Piston has depression where initial combustion takes place
  Generally more efficient than IDI engines
  Tendency to produce greater amounts of noise

## Slide 24: FIGURE 1–7 A direct injection diesel engine injects the fuel directly into the combustion chamber. Many designs do not use a glow plug.

## Slide 25: DIESEL ENGINES (6 of 10)
Fuel Injection
  Ignition occurs by injecting fuel into air charge
  Heated by compression to about 1,000°F (538°C)
  Chemical reaction of burning fuel creates heat
  Causes gases to expand & piston to rotate crankshaft

## Slide 26: DIESEL ENGINES (7 of 10)
Three Phases of Combustion
  Ignition Delay
    Near end of compression stroke, fuel injection begins, but ignition does not begin immediately, delayed
  Rapid Combustion
    Fuel first starts to burn, creating sudden rise in pressure
    Sudden & rapid rise in combustion chamber pressure
    Causes characteristic diesel engine knock
  Controlled Combustion
    Rest of fuel in combustion chamber begins to burn & injection continues
    Process occurs near injector that contains fuel surrounded by air
    Fuel burns as it mixes with air

## Slide 27: QUESTION 2: ?
Which phase of combustion casues a sudden and rapid rise in combustion chamber pressure, which causes the characteristic diesel engine knock?

## Slide 28: ANSWER 2:
Rapid Combustion

## Slide 29: DIESEL ENGINES (8 of 10)
Valve & Camshaft Arrangements
  intake & exhaust valves controlled by camshaft
  Used to open valves
  Older diesels uses 1 intake valve & 1 exhaust valve
  Many newer engines use 2 intake & 2 exhaust valves

## Slide 30: DIESEL ENGINES (9 of 10)
Overhead Valve (OHV) Engines
  Camshaft is located in block
    Valves are operated by lifters, pushrods, &rocker arms.
  Pushrod engine
    Use pushrods to transfer motion of camshaft lobes to valves
  Cam-in-block design
    Another term used to describe overhead valve or pushrod design
  Overhead valve (OHV)
    Overhead valve engine has camshaft in block and the valves are located in cylinder head

## Slide 31: FIGURE 1–8 Cutaway of an overhead valve (OHV) V-8 engine showing the lifters, pushrods, roller rocker arms, and valves.

## Slide 32: DIESEL ENGINES (10 of 10)
Overhead Camshaft
  Camshaft in cylinder head
  Called overhead camshaft-type
  Single Overhead Camshaft (SOHC)
    One overhead camshaft used
  Double Overhead Camshaft (DOHC)
    Two overhead camshafts are used,
    One cam operating intake valve & other operating exhaust valves

## Slide 33: FIGURE 1–9 SOHC engines usually require additional components, such as a rocker arm, to operate all of the valves. DOHC engines often operate the valves directly.

## Slide 34: ENGINE SIZE (1 of 4)
BORE
  Diameter of cylinder
  Measured in inches or millimeters (mm)
  Larger the bore greater the piston head area
  Pressure is measured in units, such as PSI
  Greater area of piston head (square inches)
  Higher force exerted by pistons to rotate crankshaft

## Slide 35: FIGURE 1–10 bore and stroke of pistons are used to calculate engine displacement.

## Slide 36: ENGINE SIZE (2 of 4)
STROKE
  Distance piston travels from TDC to BDC
  Distance determined by throw of crankshaft
    Throw is distance from centerline of crankshaft
    To centerline of crankshaft rod journal
    ½ the stroke

## Slide 37: FIGURE 1–11 crankshaft determines the stroke of the engine, which is the difference between the centerline of the crankshaft journal and the centerline of the connecting rod journal. .

## Slide 38: ENGINE SIZE (3 of 4)
NOTE: Changing connecting rod length does not change stroke of an engine. Changing connecting rod only changes position of piston in the cylinder. Only crankshaft determines stroke of an engine

## Slide 39: QUESTION 3: ?
Which is the definition of engine stroke?

## Slide 40: ANSWER 3:
The distance the piston travels.

## Slide 41: ENGINE SIZE (4 of 4)
Displacement
  Cubic inch (cu. in.) cubic centimeter (cc) volume displaced
  How much air is moved by all of pistons
  A liter (L) is equal to 1,000 cubic centimeters
  Engines identified by their displacement in liters
Cubic inch displacement R2 X Stroke X Number of cylinders

## Slide 42: COMPRESSION RATIO (1of 4)
Compression Ratio
  Ratio of difference in cylinder volume
    When piston is at bottom of stroke to
    Volume in cylinder above piston when piston is at TDC
Compression Ratio

## Slide 43: FIGURE 1–12 compression of an engine is expressed as a ratio of the volume, with the piston at the bottom of the cylinder, to that volume when the piston is at the top of cylinder.

## Slide 44: Think of a 2-Liter Bottle
A two-liter bottle contains two liters of liquid. This is the volume of all four cylinders combined in a two-liter four-cylinder engine. A six-liter engine would therefore have the piston displacement of three two-liter bottles.

## Slide 45: TORQUE (1of 4)
Torque
  Rotating force that may or may not result in motion
    Amount of force multiplied by length of lever
    Through which it acts
    Force of 10 pounds applied to end of 1 foot long wrench
    To turn a bolt, a torque of 10 pound-feet (lb-ft) is achieved
    Form of Work

## Slide 46: FIGURE 1–13 Torque is a twisting force equal to distance from pivot point times force applied, expressed in units called pound-feet (lb-ft) or newton-meters (N-m).

## Slide 47: Is torque ft-lb or lb-ft?
Definition of torque is a force (lb) applied to an object times the distance from that object (ft). Therefore, based on the definition of the term, torque should be:
lb-ft (a force times a distance)
Newton-meter (N-m) (force times distance)
However, torque is commonly labeled, even on some torque wrenches, as ft-lb.

## Slide 48: POWER (1of 4)
Definition of Power
  Rate of doing work or torque
  Horsepower & Altitude
    Air density lower at high altitude
    Power reduced at high altitude
    One Horsepower =
      Power to move 550 pounds one foot in one second,
      Or 33,000 pounds one foot in one minute
      (550 lb * 60 sec = 33,000 lb)
.

## Slide 49: POWER (1 of 2)
Definition of Power
  Rate of doing work or torque
  Horsepower & Altitude
    Air density lower at high altitude
    Power reduced at high altitude
    One Horsepower =
      Power to move 550 pounds one foot in one second,
      Or 33,000 pounds one foot in one minute
      (550 lb * 60 sec = 33,000 lb)
.

## Slide 50: POWER (2 of 2)
Horsepower Formula
  Horsepower is torque times RPM divided by 5252
  Horsepower = Torque * RPM/ 5252.

## Slide 51: FIGURE 1–14 One horsepower is equal to 33,000 foot pounds (200 lbs X 165 feet) of work per minute.

## Slide 52: How to Explain the Difference between Horsepower and Torque
As Carroll Shelby, well-known race car driver and business owner said, “Horsepower sells cars, but torque wins races.” Torque determines how fast the vehicle will accelerate, and horsepower determines how fast the vehicle will go..

## Slide 53: Summary (1 of 2)
The four strokes of the four-stroke cycle are intake, compression, power, and exhaust.
Gasoline engines draw an air-fuel mixture into the combustion chamber, but only air enters a diesel engine on the intake stroke.
Engine size is called displacement and represents the volume displaced by all of the pistons.

## Slide 54: Summary (2 of 2)
There are three distinct phases or parts to the combustion in a diesel engine:
  Ignition delay
  Rapid combustion
  Controlled combustion
The term power means the rate of doing work. Power equals work divided by time. Work is achieved when a certain amount of mass (weight) is moved a certain distance by a force.