## Slide 1: Manual Drivetrains and Axles
8th Edition
Chapter 12
Drive Axles and Differentials

## Slide 2: Learning Objectives (1 of 2)
1.1 Prepare for the Manual Drivelines and Axles (A2) ASE certification test content area “C” (Transmission/Transaxle Diagnosis and Repair)
1.2 Discuss the different drive axle designs.
1.3 Explain the features of ring and pinion gears.

## Slide 3: Learning Objectives (2 of 2)
1.4 Discuss the types of differential carriers.
1.5 State the purpose of differentials and identify the parts of a differential assembly.
1.6 Identify the different types of limited slip differentials.

## Slide 4: Drive Axle Terminology
The major parts of a drive axle include:
  The ring and pinion gears
  Differential
  Axle shafts

## Slide 5: Drive Axle Assembly
Purpose and function
  Changing the direction of engine torque
  Allowing the drive wheels to rotate at different speeds
  Support the weight of the vehicle
  Drive the wheels through axles

## Slide 6: FIGURE 12–1 The differential assembly changes the direction of engine torque and increases the torque to the drive wheels.

## Slide 7: Axle Designs (1 of 2)
Axe Shafts
  Transfer the torque from the differential side gears to the drive wheels and support the weight of the vehicle
Semi-Floating Axles
  Used by all rear-wheel-drive passenger vehicles
    Retainer-plate type
    C-lock

## Slide 8: Axle Designs (2 of 2)
Full-floating Axles
  Used by all heavy trucks
Three-Quarter Axles
  Used by some older vehicles

## Slide 9: Figure 12–3 A typical retainer-plate type axle, which uses a ball bearing and uses a bearing retainer ring which is a press fit into the axle shaft

## Slide 10: Figure 12–4 A C-lock type axle uses a straight roller bearing which is lubricated by the drive axle lube

## Slide 11: Figure 12–5 In a full-floating axle the axle itself slides through the center of the wheel hub assembly and does not support the weight of the vehicle

## Slide 12: Ring and Pinion Gears (1 of 3)
The ring and pinion gears are the final drive reduction gears.
The ring and pinion gear set is a hypoid type.
After the gears have been cut, hardened, and ground to shape,…
  The ring and pinion are run against each other in a machine with abrasive compound on their teeth.
Final gear ratio

## Slide 13: Ring and Pinion Gears (2 of 3)
How are hypoid gear sets manufactured?
Hypoid gear tooth terms
  Pitch line
  Face
  Flank
  Drive side
  Backlash
  Coast side
  Float

## Slide 14: Ring and Pinion Gears (3 of 3)
Hunting, non-hunting, and partially non-hunting gear sets
Reverse-cut ring and pinion gears
ABS reluctor wheel
Gear and pinion mounting

## Slide 15: Figure 12–6 A hypoid gear set uses a drive pinion that meshes with the ring gear below the center line of the ring gear

## Slide 16: Figure 12–8 The drive side is the convex side of the ring gear except for some front axles used in four-wheel vehicles, and they often use the concave side on the drive side.

## Slide 17: Figure 12–9 (a) During a drive condition, the pinion gear is driving the ring gear and there is backlash at the coast side of the ring gear tooth. (b) During a coast condition, this action is reversed. (c) During a float condition, lash is split between both sides of the tooth.

## Slide 18: Figure 12–10 A reverse-cut gear set is a mirror image of the normal hypoid gear set.

## Slide 19: Figure 12–11 Two front drive axles. The left one has a standard-cut ring and pinion, whereas the one at the right has high-pinion, reverse-cut ring and pinion gears.

## Slide 20: Differential Carriers
What are the purpose and function of differential carriers?
Removable Carriers
  In most early trucks
Integral carriers
  Used by most rear-wheel-drive passenger vehicles and light trucks
Pinion shafts
  Overhung; straddle mounting

## Slide 21: Figure 12–14 A removal carrier such as this Ford 9 inch unit. This older design uses an axle housing that is often called a “banjo” because of the shape, which is similar to the musical instrument.

## Slide 22: Figure 12–15 An integral carrier axle assembly is the most commonly used design of drive axle

## Slide 23: Differentials
A differential…
  Splits torque equally to the drive wheels
  Allows engine torque to be applied to both drive axles
Parts must include a differential, which includes two or more differential pinion gears and two side or axle gears.
Types
  Open, limited slip, and locked

## Slide 24: Figure 12–16 When the vehicle turns a corner, the inner wheel slows and the outer wheel increases in speed to compensate. This difference in rotational speed causes the pinion gears to “walk” around the slower side gear

## Slide 25: Figure 12–17 A close-up view of the side gears and spider (pinion) gear.
Notes: Note the ridges on the gear teeth. These ridges are manufactured into the gear teeth to help retain lubricant so that no metal-to-metal contact occurs

## Slide 26: Limited Slip Differentials (1 of 2)
An open differential has a torque bias ratio (TBR) of 1:1.
Types
  Preloaded clutches
  Self-applying clutches
  Viscous couplings
  Eaton locker differential
  Hydraulic applied clutches
  Cone type

## Slide 27: Limited Slip Differentials (2 of 2)
What is a Torsen differential?
Electric locking differentials
  When the axle shaft or side gear is connected to the differential case, the differential becomes locked.
Electronic torque management
Independent rear suspension drive axles

## Slide 28: FIGURE 12–23 A friction additive needs to be added to the gear lube if using a preloaded clutch-type differential.

## Slide 29: Summary (1 of 2)
A drive axle combines the hypoid final drive gears with the differential and two axle shafts.
Hypoid ring and pinion gears must be adjusted correctly for long life and quiet operation.

## Slide 30: Summary (2 of 2)
The pinion gear and shaft are supported by two pinion bearings, and the ring gear and differential case are supported by two carrier bearings.
Differentials allow two wheels to be driven at different speeds.
Limited slip differentials increase torque bias to send more torque to the tire with good traction.