### Remove and Replace Transmission/Transaxle

Meets NATEF Task:  (Not Specified by NATEF)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

Always refer to the service information for the exact removal and installation procedures for the vehicle being serviced and adhere to all safety procedures.

_____  1.  Hoist the vehicle safely.

_____  2.  Drain the transmission/transaxle fluid.

_____  3.  Disconnect the drive shaft (RWD) or

drive axle shafts (FWD).

_____  4.  Disconnect all linkage and electrical connections.

CAUTION:  Be sure to label all electrical connections.

_____  5.  Remove the fasteners from the transmission/transaxle mounts and from the bell

housing.

_____  6.  Remove the transmission/transaxle.

_____  7.  To reinstall, follow the removal procedure in reverse.

_____  8.  Determine the proper torque specifications for all of the

fasteners.

Bell housing bolts = _______ lb-ft

Mounting bolts     =  _______ lb-ft

Others (list) =  ______________________

_____  9.  Check for proper operation.

_____ 10. Lower the vehicle and test drive before returning it  to the customer.