Measure Voltage Using a Voltmeter

Meets NATEF Task:  (A6-A-9)  Measure source voltage and perform voltage drop tests; determine necessary action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specifications for battery voltage.

__________________________________________________________________

_____  2.  Using a voltmeter, measure the voltage of the battery.  Voltage = _____________.

OK ____    NOT OK ____

_____  3.  Check service information regarding the

procedure and the specification for

performing a voltage drop test of the

cranking circuit.

__________________________

__________________________

_____  4.  Perform a voltage drop test of the cranking circuit and record the results.

A.  Power side of the circuit = ___________

B.  Ground side of the circuit = ___________

_____  5.  Based on the factory specification and the test results, what is the necessary action?

__________________________________________________________________

__________________________________________________________________

__________________________________________________________________