Four-Wheel Drive Diagnosis

Meets NATEF Task:  (A3-F-1, A3-A-2)  Diagnose noise and vibration concerns; determine necessary action.  (P-3, P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check the service manual for correct fluid and for the location for inspecting the fluid.

Recommended fluid = __________________

Inspection location = _______________________

_____  2.  Hoist the vehicle safely.

_____  3.  Inspect the fluid level and replace as

required or recommended.

____ level okay

____ level low - added fluid

____ drained and replaced the fluid

_____  4.  Check the engine and transmission/transfer

case mounts.

____ all mounts are dry and okay

____ one or more of the mounts is oil soaked

____ one or more of the mounts is collapsed or defective

____ other (describe) _____________________________________

NOTE:  A defective engine or transmission/transfer case mount can cause abnormal vibrations and noise.

_____  5.  Check the operation of the clutch by checking free play and compare to the factory

specifications.

Free play specifications (if available) = _______________

Actual measured clutch pedal free play = ______________

OK ____          NOT OK ____

_____  6.  Adjust the clutch linkage if possible.  OK ____      NOT OK ____

_____  7.  What is the necessary action?  _______________________________________________

____________________________________________________________________