## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 11
Vehicle Lifting and Hoisting
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES
11.1 Discuss the purpose of floor jacks and creepers.
11.2. Describe vehicle hoists and drive-on ramps, and discuss the proper methods for safely hoisting a vehicle.

## Slide 3: Floor Jack
A hand operated hydraulic device used for lifting vehicles or components.
Uses four casters to move easily
Not designed to hold a load
Requires the use of jack stands

## Slide 4: Figure 11.1 A hydraulic hand-operated floor jack

## Slide 5: Figure 11.2 Safety stands are being used to support the rear of this vehicle

## Slide 6: QUESTION 1: ?
What must be used after lifting a vehicle with a floor jack?

## Slide 7: ANSWER 1:
Jack Stands.

## Slide 8: CREEPERS
Use by technician to maneuver under vehicle.
Flat or concaved surface equipped with low profile casters.
Should be stored vertically against wall or toolbox to avoid trip hazards.

## Slide 9: VEHICLE HOISTS
In-ground: pneumatic/hydraulic.
Above-ground: electric/hydraulic.
Symmetrical: Equal length lift arms.
Asymmetrical: Unequal length lift arms.
Use recommended vehicle lift points.
Lower onto mechanical locks before working.
Before lowering ensure proper clearances.

## Slide 10: Figure 11.3 Most newer vehicles have a triangular symbol indicating the recommended hoisting lift points

## Slide 11: Figure 11.4 (a) Tall safety stands can be used to provide additional support for a vehicle while on a hoist. (b) A block of wood should be used to avoid the possibility of doing damage to components supported by the stand

## Slide 12: Figure 11.5 This training vehicle fell from the hoist when the pads were not set correctly. No one was hurt, but the vehicle was damaged

## Slide 13: Figure 11.6 (a) An assortment of hoist pad adapters that are often necessary to safely hoist many pickup trucks, vans, and sport utility vehicles. (b) A view from underneath a Chevrolet pickup truck showing how the pad extensions are used to attach the hoist lifting pad to contact the frame

## Slide 14: Figure 11.7 (a) In this photo, the pad arm is just contacting the rocker panel of the vehicle. (b) This photo shows what can occur if the technician places the pad too far inward underneath the vehicle. The arm of the hoist has dented in the rocker panel

## Slide 15: QUESTION 2: ?
Before working on a vehicle that is on a hoist, what must be done?

## Slide 16: ANSWER 2:
Lower the vehicle onto the mechanical locks.

## Slide 17: DRIVE-ON RAMPS
Inexpensive way to raise the front or rear of the vehicle.
Ramps store easily.
Caution must be used when placing the vehicle on the ramps.
Wheels on the ground need to be blocked to prevent movement.

## Slide 18: Figure 11.8 Drive-on-type ramps. The wheels on the ground level must be chocked (blocked) to prevent accidental movement down the ramp

## Slide 19: HOISTING THE VEHICLE

## Slide 20: The first step in hoisting a vehicle is to properly align the vehicle in the center of the stall.

## Slide 21: Most vehicles will be correctly positioned when the left front tire is centered on the tire pad.

## Slide 22: The arms can be moved in and out and most pads can be rotated to allow for many different types of vehicle construction.

## Slide 23: Most lifts are equipped with short pad extensions that are often necessary to use to allow the pad to contact the frame of a vehicle without causing the arm of the lift to hit and damage parts of the body.

## Slide 24: Tall pad extensions can also be used to gain access to the frame of a vehicle. This position is needed to safely hoist many pickup trucks, vans, and sport utility vehicles.

## Slide 25: An additional extension may be necessary to hoist a truck or van equipped with running boards to give the necessary clearance.

## Slide 26: Position the pads under the vehicle in the recommended locations.

## Slide 27: After being sure all pads are correctly positioned, use the electromechanical controls to raise the vehicle.

## Slide 28: With the vehicle raised one foot (30 cm) off the ground, push down on the vehicle to check to see if it is stable on the pads. If the vehicle rocks, lower the vehicle and reset the pads. The vehicle can be raised to any desired working level. Be sure the safety mechanism is engaged before working on or under the vehicle.

## Slide 29: If raising a vehicle without a frame, place the flat pads under the pinch weld seam to spread the load. If additional clearance is necessary, the pads can be raised as shown.

## Slide 30: When the service work is completed, the hoist should be raised slightly and the safety mechanism released before using the hydraulics to lower the vehicle.

## Slide 31: After lowering the vehicle, be sure all arms of the lift are moved out of the way before driving the vehicle out of the work stall.

## Slide 32: Copyright