## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 113
Tires and Wheels
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
113.1 Explain the purpose and functions of tires.
113.2 Identify the parts of a tire and describe how it is constructed.
113.3 Discuss tire sizes, load index, ratings, specifications, and grading.
113.4 Discuss tire conicity and vehicle handling.
113.5 Describe spare tires and run-flat tires.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
113.6 Describe tire selection considerations.
113.7 Explain the construction and sizing of steel and alloy wheels and attaching hardware.
113.8 This chapter will help prepare for ASE Suspension and Steering (A4) certification content area “E” (Wheel and Tire Diagnosis and Repair).

## Slide 4: INTRODUCTION TO TIRES
Purpose
  The friction (traction) between the tire and the road determines the handling characteristics of any vehicle.
Function
  Tires provide the following:
  Shock absorber action when driving over rough surfaces
  Friction (traction) between the wheels and the road

## Slide 5: PARTS OF A TIRE (1 OF 3)
Tread
  Tread refers to the part of the tire that contacts the ground.
Sidewall
  The sidewall is that part of the tire between the tread and the wheel.
Bead
  The bead is the foundation of the tire and is located where the tire grips the inside of the wheel rim.

## Slide 6: PARTS OF A TIRE (2 OF 3)
Body Ply
  The layers of material wrapped around both beads under the tread and sidewall rubber. This creates the main framework, or “carcass,” of the tire.
Belt
  A tire belt is two or more layers of material applied over the body plies and under the tread area only to stabilize the tread and increase tread life and handling.

## Slide 7: PARTS OF A TIRE (3 OF 3)
Inner Liner
  The inner liner is the soft rubber lining (usually a butyl rubber compound) on the inside of the tire that protects the body plies and helps provide for self-sealing of small punctures.
Major Splice
  When the tire is assembled by a craftsperson on a tire-building machine, the body plies, belts, and tread rubber are spliced together.

## Slide 8: Figure 113.1 (a) A typical tire tread depth gauge. The center movable plunger is pushed down into the groove of the tire

## Slide 9: Figure 113.1 (b) The tread depth is read at the top edge of the sleeve. In this example, the tread depth is 6/32 inch

## Slide 10: Figure 113.2 Wear indicators (wear bars) are strips of bald tread that show when the tread depth is down to 2/32 inch, which is the legal limit in many states

## Slide 11: Figure 113.3 The tire tread runs around the circumference of the tire, and its pattern helps maintain traction. The ribs provide grip, while the grooves direct any water on the road away from the surface. The sipes help the tire grip the road

## Slide 12: Figure 113.4 Hydroplaning can occur at speeds as low as 30 mph (48 km/h). If the water is deep enough and the tire tread cannot evacuate water through its grooves fast enough, the tire can be lifted off the road surface by a layer of water.

## Slide 13: Figure 113.5 Typical construction of a radial tire. Some tires have only one body ply, and some tires use more than two belt plies

## Slide 14: Figure 113.6 The major splice of a tire can often be seen and felt on the inside of the tire. The person who assembles (builds) the tire usually places a sticker near the major splice as a means of identification for quality control

## Slide 15: QUESTION 1: ?
What are the seven major parts of the tire?

## Slide 16: ANSWER 1:
The tread, sidewalls, bead, body ply, belt, inner liner, and major splice.

## Slide 17: TIRE MOLDING
After the tire has been assembled by the tire building machine, it is called a green tire.
The completed green tire is then placed in a mold where its shape, tread design, and all sidewall markings are formed
While in the mold, a steam bladder fills the inside of the tire and forces the tire against the outside of the mold.
The tire is no longer called a green tire but a cured tire

## Slide 18: Figure 113.7 Complete stage 1 (body plies, sidewall components, and beads) 2. Building drum expands in preparation to receive the belts and tread 3. Application of belt #1. 4. Application of belt #2. 5. Application of the tread 6. Drum retracts to release the completed green (uncured) tire

## Slide 19: Figure 113.8 After the entire tire has been assembled into a completed “green” tire, it is placed into a tire-molding machine where the tire is molded into shape and the rubber is changed chemically by the heat. This nonreversible chemical reaction is called vulcanization

## Slide 20: SERVICE DESCRIPTION
Tires built after 1990 use a “service description” method of sidewall information in accordance with ISO 4000 (International Standards Organization) that includes size, load, and speed rating together in one easy-to-read format.

## Slide 21: Figure 113.9 (a) Tire size designation includes cross-sectional width and aspect ratio. The aspect ratio is the proportional relationship between the width and the height of the tire expressed as a percentage. (b) Cross-sectional view of a typical tire showing the terminology

## Slide 22: HIGH-FLOTATION TIRES
High-flotation tires for light trucks are designed to give improved off-road performance on sand, mud, and soft soil and still provide acceptable hard-road surface performance. High-flotation tires have a size designation such as 33 × 12.50R × 15LT:

## Slide 23: HOW MUCH BIGGER CAN I GO?
When changing tire size, there are many factors to consider:
  The tire should be the same outside diameter as the original to maintain the proper suspension, steering, and ride height specifications.
  Tire size affects vehicle speed sensor values, ABS brake wheel sensor values that can change automatic transmission operation, and ABS operation.
  Generally, a tire that is 10 mm wider is acceptable.

## Slide 24: Figure 113.10 Notice that the overall outside diameter of the tire remains almost the same and at the same time the aspect ratio is decreased and the rim diameter is increased

## Slide 25: LOAD INDEX AND EQUIVALENT LOADS
The load index is an abbreviated method to indicate the load-carrying capabilities of a tire.
Examples:

## Slide 26: Figure 113.11 Typical sidewall markings for load index and speed rating following the tire size

## Slide 27: SPEED RATINGS
Tires are rated according to the maximum sustained speed.

## Slide 28: TIRE PRESSURE AND TRACTION
All tires should be inflated to the specifications given by the vehicle manufacturer.
Most vehicles have recommended tire inflation figures written in the owner’s manual or on a placard or sticker on the door post or glove compartment.

## Slide 29: Figure 113.12 A typical door placard used on a General Motors vehicle indicating the recommended tire inflation. Note that the information also includes the size and speed rating of the tire as well as the recommended wheel size

## Slide 30: RIM WIDTH AND TIRE SIZE
The rim width is the distance between the tire flanges sometimes called the “flange-to-flange” width.
As a general rule, for a given rim width it is best not to change tire width more than 10 mm (either wider or narrower).
Installing a tire that is too wide or too narrow will cause undesired tire wear.

## Slide 31: UNIFORM TIRE QUALITY GRADING SYSTEM (1 OF 3)
The U.S. Department of Transportation and the National Highway Traffic Safety Administration developed a system of tire grading, the Uniform Tire Quality Grading System (UTQGS), to help customers better judge the relative performance of tires.
The three areas of tire performance are tread wear, traction, and temperature resistance.

## Slide 32: UNIFORM TIRE QUALITY GRADING SYSTEM (2 OF 3)
Tread Wear
  The tread wear grade is a comparison rating based on the wear rate of a standardized tire, tested under carefully controlled conditions, which is assigned a value of 100.

## Slide 33: UNIFORM TIRE QUALITY GRADING SYSTEM (3 OF 3)
Traction
  Traction performance is rated by the letters AA, A, B, and C, with AA being the highest.
Temperature Resistance
  Temperature resistance is rated by the letters A, B, and C, with A being the highest rating.

## Slide 34: Figure 113.13 Typical “Uniform Tire Quality Grading System” (UTQGS) ratings imprinted on the tire sidewall

## Slide 35: QUESTION 2: ?
What are the three criteria used in the Uniform Tire Grading Quality system?

## Slide 36: ANSWER 2:
Wear, traction, and temperature resistance.

## Slide 37: ALL-SEASON TIRE DESIGNATION
Most all-season tires are rated and labeled as M & S, MS, or M + S, and therefore must adhere to general design features as specified by the Rubber Manufacturers Association (RMA).
  Tires labeled M & S are constructed with an aggressive tread design, as well as tread compounds and internal construction that are designed for mud and snow.
  One design feature is that the tire has at least 25% void area.
  The tread rubber used to make all-season tires is also more flexible at low temperatures.

## Slide 38: DOT TIRE CODE
Each tire that is DOT-approved has a DOT number molded into the sidewall of the tire.
  The DOT tire code requirements include resistance to tire damage that could be caused by curbs, chuckholes, and other common occurrences for a tire used on public roads.
  Starting with tires manufactured after January 1, 2000, the tire build date includes four digits rather than three digits.
  A new code such as “3406” means the 34th week of 2006.

## Slide 39: Figure 113.14 Typical DOT date code. This tire was built the 12th week of 2015

## Slide 40: TIRE CONICITY AND PLY STEER
Tire conicity can occur during the construction of any radial or belted tire when the parts of the tire are badly positioned, causing the tire to be smaller in diameter on one side.
  It can cause the vehicle to pull to one side of the road due to the cone shape of the tire.
Ply steer is another term that describes a slight pulling force on a vehicle due to tire construction.
  Ply steer is due to the angle of the cords in the belt layers.

## Slide 41: Figure 113.15 Conicity is a fault in the tire that can cause the vehicle to pull to one side due to the cone effect (shape) of the tire

## Slide 42: Figure 113.16 Notice the angle of the belt material in this worn tire. The angle of the belt fabric can cause a “ply steer” or slight pulling force toward one side of the vehicle

## Slide 43: VEHICLE HANDLING AND TIRE SLIP ANGLE
As a vehicle is turned, the wheels are moved while the tires remain in contact with the road.
These actions “twist” the carcass of the tire and create a slip angle between the direction the wheel is pointing and the direction the tread is pointing.
This movement causes a slight delay in the turning of the vehicle and causes tire wear.

## Slide 44: Figure 113.17 Slip angle is the angle between the direction the tire tread is heading and the direction it is pointed

## Slide 45: SPARE TIRES
Most vehicles today come equipped with space-saver spare tires.
Many small, space-saving spare tires use a higher-than-normal air inflation pressure, usually 60 PSI (414 kPa).
Space saver spares are designed to provide normal handling but not the same durability as full-size tires.
Space saver tires removed as soon as possible.

## Slide 46: RUN-FLAT TIRES (1 OF 2)
Run-flat tires (abbreviated RFT) are designed to operate without any air for a limited distance (usually 50 miles at 55 mph).
A typical run-flat tire (also called extended mobility tire [EMT] or zero pressure [ZP] tire) requires the use of an air pressure sensor/ transmitter and a dash-mounted receiver to warn the driver that a tire has lost pressure.

## Slide 47: RUN-FLAT TIRES (2 OF 2)
PAX Run-Flat Tires
  Michelin developed a run-flat tire that has three unique components:
  A special wheel that has two bead seats that are of different diameters.
  A urethane support ring that is designed to support the weight of the vehicle in the event of a flat tire.
  A special tire that is designed to operate without air.
Servicing a PAX Wheel/Tire assembly
  Follow the manufacturers guidelines for service.

## Slide 48: Figure 113.18 Cutaway of a run-flat tire showing the reinforced sidewalls and the required pressure sensor

## Slide 49: Figure 113.19 A conventional tire on the left and a run-flat tire on the right, showing what happens when there is no air in the tire

## Slide 50: Figure 113.20 The PAX run-flat tire system is composed of three unique components—a special asymmetrical wheel, a urethane support ring, and a special tire

## Slide 51: GENERAL MOTORS TPC RATINGS
All General Motors original equipment (OE) tires have a rating that identifies the size as well as the tread design, wear, traction, and heat resistance factors.
All of these factors are combined in a set of numbers and letters that is imprinted in the tire mold.

## Slide 52: Figure 113.21 The Tire Performance Criteria (TPC) specification number is imprinted on the sidewall of all tires used on General Motors vehicles from the factory

## Slide 53: WHEELS (1 OF 3)
Wheel Offset
  The wheel has a positive offset if the center section is outward from the wheel centerline.
  The wheel has a negative offset if the center section is inboard (or “dished”) from the wheel centerline.
Back Spacing
  Back spacing, also called rear spacing or backside setting, is the distance between the back rim edge and the wheel center section mounting pad.

## Slide 54: WHEELS (2 OF 3)
Determining Bolt Circle
  On four-lug axles and wheels, the bolt circle measurement is simply taken from center to center on opposite studs or holes
  On five-lug axles and wheels, one method is to measure from the far edge of one bolt hole to the center of the hole two over from the first.

## Slide 55: WHEELS (3 OF 3)
Steel Wheels
  A steel wheel is very strong due to its designed shape and the fact that it is work hardened during manufacturing.
  Steel wheels are formed from welded hoops that are flared and joined to stamped spiders.
Aluminum Wheels
  Forged and cast aluminum wheels are commonly used on cars and trucks.
  Forged means that the aluminum is hammered or forged under pressure into shape.

## Slide 56: Figure 113.22 The size of the wheel is usually cast or stamped into the wheel. This wheel is 7 inch wide. The letter “J” refers to the contour of the bead seat area of the wheel

## Slide 57: Figure 113.23 The wheel rim well provides a space for the tire to fit during mounting; the bead seat provides a tire-to-wheel sealing surface; the flange holds the beads in place

## Slide 58: Figure 113.24 A cross section of a wheel showing part designations

## Slide 59: Figure 113.25 Offset is the distance between the centerline of the wheel and the wheel mounting surface

## Slide 60: Figure 113.26 Back spacing (rear spacing) is the distance from the mounting pad to the edge of the rim. Most custom wheels use this measurement method to indicate the location of the mounting pad in relation to the rim

## Slide 61: Figure 113.27 Bolt circle is the diameter of a circle that can be drawn through the center of each lug hole or stud. The bolt circle is sometimes referred to as PCD for pitch circle diameter

## Slide 62: Figure 113.28 Measuring the bolt circle on a five-lug wheel is difficult, but a quick and easy way includes measuring as shown to determine the approximate bolt circle of a five-lug wheel

## Slide 63: Figure 113.29 Measure center-to-center distance and compare the distance to the figures in the chart in the text to determine the diameter for a five-lug bolt circle

## Slide 64: FREQUENTLY ASKED QUESTION

## Slide 65: Figure 113.30 A typical JWL symbol for the Japan Wheel Light Metal standard mark

## Slide 66: QUESTION 3: ?
What is wheel offset?

## Slide 67: ANSWER 3:
The location of the wheel center section relative to the centerline.

## Slide 68: TIRE VALVES
All tires use a tire valve, called a Schrader valve, to hold air in the tire.
Most tire experts agree that the valve stem (which includes the Schrader valve) should be replaced whenever tires are replaced.
Aluminum (alloy) wheels often require special metal valve stems that use a rubber washer and are actually bolted to the wheel.

## Slide 69: Figure 113.31 a) A rubber snap-in style tire valve assembly. (b) A metal clamp-type tire valve assembly used on most highpressure (over 60 PSI) tire applications such as is found on many trucks, RVs, and trailers.

## Slide 70: LUG NUTS
Lug nuts are used to hold a wheel to the brake disc, brake drum, or wheel bearing assembly.
Some vehicles use a lug bolt that is threaded into a hole in the brake drum or bearing assembly.
Typical lug nuts are tapered so that the wheel stud will center the wheel onto the vehicle
Many alloy wheels use a shank-nut-type lug nut that has straight sides without a taper
Lug Studs are pressed into the hub or axle.

## Slide 71: Figure 113.32 Various styles of lug nuts

## Slide 72: FREQUENTLY ASKED QUESTION

## Slide 73: Figure 113.33 (a) A typical knock-off-type wheel showing the large three prong wing nuts and the threads on the wheel hub

## Slide 74: Figure 113.33 (b) A lookalike knock-off wheel that looks like a knock-off but uses lug nuts

## Slide 75: TIRE INSPECTION

## Slide 76: 1. Check the tire information placard, usually located on the driver’s door or door jamb, for the specified tire size and inflation pressure.

## Slide 77: 2. Visually check the tires for abnormal wear or damage.

## Slide 78: 3. Remove the tire valve cap and visually check the condition of the valve stem.

## Slide 79: 4. Check inflation pressure by pushing the tire-pressure gauge straight onto the end of the tire valve. If a “hissing” sound is heard, then the reading will not be accurate.

## Slide 80: 5. Read the pressure and compare to specifications. Use an analog or digital gauge if possible which have been proven to be more accurate than a mechanical pencil type gauge.

## Slide 81: 6. A typical tire tread depth gauge.

## Slide 82: 7. The blade of the tire tread depth gauge is pushed down into the groove of the tire at the lowest part.

## Slide 83: 8. Remove the gauge from the tire and read the tread depth at the metal housing. Tread depth is usually measured in 1/32’s of an inch.

## Slide 84: 9. If the top of Lincoln’s head is visible, then the tread depth is lower than 2/32 inch, which is the legal limit in many states.

## Slide 85: Copyright