## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 117
Front Suspension and Service
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
117.1 Describe different front suspension types.
117.2 Diagnose short/long-arm (SLA) suspension systems and discuss strut suspension.
117.3 Explain how to perform a road test, a dry park test, and a visual inspection.
117.4 Discuss the diagnosis of ball joints and kingpins.
117.5 Discuss the diagnosis of shock absorbers and struts.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
117.6 Describe how to replace MacPherson struts.
117.7 Explain the diagnosis of stabilizer bar links and bushings.
117.8 Discuss the diagnosis of strut rod bushings, front coil springs, steering knuckles, torsion bars, and control arm bushings.
117.9 This chapter will help prepare for ASE Suspension and Steering (A4) certification content area “B” (Suspension System Diagnosis and Repair).

## Slide 4: FRONT SUSPENSION TYPES
Solid Axles
  Early cars and trucks used a solid (or straight) front axle to support the front wheels.
Kingpins
  At the end of solid axle, they allow the front wheels to rotate for steering.
Twin-I Beam
  Strong steel twin beams that cross provide independent front suspension operation with the strength of a solid front axle.

## Slide 5: Figure 117.1 Most early vehicles used single straight axles

## Slide 6: Figure 117.2 Typical kingpin used with a solid axle

## Slide 7: Figure 117.3 Twin I-beam front suspension. Rubber bushings are used to support the I-beams to the frame and help isolate road noise

## Slide 8: Tech Tip

## Slide 9: Figure 117.4 The rubber radius rod bushing absorbs road shocks and helps isolate road noise

## Slide 10: SHORT/LONG-ARM SUSPENSIONS (1 OF 2)
Terminology
  The short/long-arm suspension uses a short upper control arm and a longer lower control arm and is usually referred to as the SLA-type suspension.
Strut Rods
  A strut rod, also called a reaction rod, provides support to the axle during braking and acceleration forces.

## Slide 11: SHORT/LONG-ARM SUSPENSIONS (2 OF 2)
Coil Spring Front Suspensions
  Locating the coil spring on the lower control arm is the most common SLA-type suspension configuration.
Torsion Bar Front Suspensions
  Short/long-arm suspensions use longitudinal torsion bars, especially in trucks.

## Slide 12: Figure 117.5 The upper control arm is shorter than the lower control arm on a short/long-arm (SLA) suspension

## Slide 13: Figure 117.6 A typical SLA-front suspension using coil springs

## Slide 14: Figure 117.7 An SLA-type suspension with the coil spring placed on top of the upper control arm

## Slide 15: Figure 117.8 A torsion bar SLA suspension can use either the lower or the upper control arm

## Slide 16: FREQUENTLY ASKED QUESTION

## Slide 17: Figure 117.9 An SLA-type suspension that uses a coil-over shock assembly

## Slide 18: STRUT SUSPENSION
Parts and Operation
  A MacPherson strut includes the suspension spring that transfers the weight of the body to the wheel.
  A modified strut does not include a spring as part of the assembly.
  A multilink front suspension uses two control arms as well as a structural strut assembly.

## Slide 19: Figure 117.10 A typical MacPherson strut showing all of the components of the assembly. A strut includes the shock and the spring in one structural assembly

## Slide 20: Figure 117.11The modified strut front suspension is similar to a MacPherson strut suspension except that the coil spring is seated on the lower control arm and is not part of the strut assembly

## Slide 21: FREQUENTLY ASKED QUESTION

## Slide 22: Figure 117.12 The HiPer Strut (left) compared to the traditional MacPherson strut (right)

## Slide 23: Figure 117.13 A typical multilink front suspension system

## Slide 24: SERVICING THE SUSPENSION SYSTEM
When the driver notices that the vehicle is not riding or handling as it did, he or she brings it to a technician to repair or align the vehicle.
The smart technician should always road test any vehicle before and after servicing.

## Slide 25: ROAD TEST DIAGNOSIS (1 OF 2)
While driving, try to determine when and where the noise or problem occurs, such as the following:
  In cold or warm weather
  With cold or warm engine/vehicle
  While turning, left only, right only

## Slide 26: ROAD TEST DIAGNOSIS (2 OF 2)
A proper road test for any suspension system problem should include the following:
  Drive beside parked vehicles.
  Drive into driveways.
  Drive in reverse while turning.
  Drive over a bumpy road.

## Slide 27: DRY PARK TEST (SUSPENSION)
The dry park test is performed by having an assistant move the steering wheel side to side while feeling and observing for any free-play in the steering or suspension.
In this suspension analysis using the dry park test, the technician should observe the following for any noticeable play or unusual noise:
  Front wheel bearings.
  Control arm bushing wear or movement.
  Ball joint movement.

## Slide 28: VISUAL INSPECTION
A thorough visual inspection should include checking all of the following:
  Shock absorbers and struts.
  Springs
  Stabilizer bar links and bushings
  Upper and lower shock absorber mounting points
  Bump stops
  Body-to-chassis mounts
  Engine and transmission (transaxle) mounts
  Suspension arm bushings.

## Slide 29: Figure 117.14 A leaking strut. Either a cartridge insert or the entire strut will require replacement. If a light film of oil is seen, this is to be considered normal. If oil is dripping, then this means that the rod seal has failed

## Slide 30: Figure 117.15 This front coil spring looks as if it has been heated with a torch in an attempt to lower the ride height of the vehicle. Both front springs will require replacement

## Slide 31: Figure 117.16 It is easy to see that this worn control arm bushing needs to be replaced. The new bushing is shown next to the original

## Slide 32: QUESTION 1: ?
What is the purpose of the dry park test?

## Slide 33: ANSWER 1:
To look for play in components as the steering wheel is turned side-to-side.

## Slide 34: BALL JOINTS (1 OF 3)
Diagnosis and Inspection
Defective or worn ball joints can cause looseness in the suspension and the following common driver complaints:
  Loud popping or squeaking whenever driving over curbs, such as into a driveway
  Shimmy-type vibration felt in the steering wheel
  Vehicle wander or a tendency not to track straight
  Excessive freeplay in the steering wheel

## Slide 35: BALL JOINTS (2 OF 3)
A ball joint inspection should also be done when an alignment is performed or as part of any other comprehensive vehicle inspection.
  Always check wear-indicator-type ball joints with the wheels of the vehicle on the ground.
  To perform a proper non-indicator-type ball joint inspection, the force of the vehicle’s springs must be unloaded from the ball joint.
Follower ball joints (friction ball joints) should also be inspected while testing load-carrying ball joints.

## Slide 36: BALL JOINTS (3 OF 3)
Ball Joint Removal
  The removal procedures vary with the style of ball joint and the design of the suspension system.
  The preferred method to separate ball joints in a puller.
  Use caution so as to not damage any attaching components.
  Follow the manufacturers recommended procedures.
Many vehicles are equipped with non-replaceable ball joints, and the entire control arm must be replaced if the ball joint is worn or defective.

## Slide 37: Figure 117.17 Grease fitting projecting down from the surrounding area of a ball joint. The ball joint should be replaced when the area around the grease fitting is flush or recessed

## Slide 38: Figure 117.18 Indicator ball joints should be checked with the weight of the vehicle on the ground

## Slide 39: Figure 117.19 Typical dial indicator used to measure the suspension component movement. The locking pliers attach the gauge to a stationary part of the vehicle and the flexible coupling allows the dial indicator to be positioned at any angle

## Slide 40: Figure 117.20 If the spring is attached to the lower control arm as in this SLA suspension, the jack should be placed under the lower control arm as shown. A dial indicator should be used to measure the amount of freeplay in the ball joints.

## Slide 41: Figure 117.21 The jack should be placed under the lower control arm of this modified MacPherson-type suspension

## Slide 42: Figure 117.22 If the spring is attached to the upper control arm, the jack should be placed under the frame to check for ball joint wear

## Slide 43: Figure 117.23 A special tool or a block of wood should be inserted between the frame and the upper control arm before lifting the vehicle off the ground. This tool stops the force of the spring against the upper ball joint so that a true test can be performed on the condition of the ball joint

## Slide 44: Figure 117.24 The jacking point is under the frame for checking the play of a lower ball joint used with a MacPherson strut

## Slide 45: Figure 117.25 This worn and rusty ball joint was found by moving the wheel and looking for movement in the joint

## Slide 46: Figure 117.26 Taper breaker tool being used to separate the upper ball joint from the steering knuckle. This is especially important for vehicles equipped with aluminum alloy control arms

## Slide 47: Figure 117.27 A pinch bolt attaches the steering knuckle to the ball joint. Remove the pinch bolt by turning the nut, not the bolt

## Slide 48: Figure 117.28 If the pinch bolt is overtightened, the steering knuckle can be deformed. A deformed knuckle can cause the pinch bolt to break and the ball joint could become separated from the steering knuckle

## Slide 49: Figure 117.29 By drilling into the rivet, the holding force is released

## Slide 50: Figure 117.30 The head of the rivet can be removed by using a large-diameter drill bit as shown

## Slide 51: Figure 117.31 A punch and a hammer being used to remove a rivet after the head has been removed

## Slide 52: Figure 117.32 Press-in ball joints are best removed using a large C-clamp press, as shown

## Slide 53: QUESTION 2: ?
What are the symptoms of a defective ball joint?

## Slide 54: ANSWER 2:
Noise, shimmy, wander, and excessive freeplay in the steering.

## Slide 55: KINGPIN DIAGNOSIS AND SERVICE (1 OF 2)
Kingpins are designed to rotate inside kingpin bushings with a clearance between them of approximately 0.001 to 0.003 inch (0.025 to 0.075 mm).
Looseness in the kingpin causes looseness in the wheels and steering.
Kingpins can also gall or seize due to lack of lubrication, resulting in very hard steering.

## Slide 56: KINGPIN DIAGNOSIS AND SERVICE (2 OF 2)
To remove a typical kingpin, follow these basic steps:
  Remove the tire, brake drum, and backing plate or caliper.
  Remove the lockpin. The lockpin is usually tapered with a threaded end for the nut. Drive the lockpin out with a drift (punch).
  Remove the grease caps and drive the kingpin from the steering knuckle and axle with a hammer and a brass punch or a hydraulic press, if necessary

## Slide 57: Figure 117.33 Typical kingpin assembly

## Slide 58: Figure 117.34 Driving a kingpin out with a hammer

## Slide 59: Figure 117.35 A kingpin being removed showing the worn bushing

## Slide 60: SHOCK ABSORBERS AND STRUTS (1 OF 2)
Diagnosis
Replacement of shock absorbers may be required when any or all of the following symptoms appear:
  Ride harshness.
  Frequent bottoming out on rough roads.
  Extended vehicle movement after driving on dips or a rise in the road.
  Cuppy-type tire wear.
  Leaking hydraulic oil.

## Slide 61: SHOCK ABSORBERS AND STRUTS (2 OF 2)
Front Shock Replacement
  Most front shock absorbers can be replaced either with the vehicle still on the ground or while on a hoist.
  Special sockets and other tools are available to remove the nut from the shocks that use a single mounting stem.
  The removal of the lower mounting of most front shock absorbers usually involves the removal of two bolts.
  Reverse the removal procedure to install replacement shock absorbers.

## Slide 62: Figure 117.36 Most shock absorbers used on the front suspension can be removed from underneath the vehicle after removing the attaching bolts or nuts

## Slide 63: MACPHERSON STRUT REPLACEMENT (1 OF 2)
On most vehicles equipped with MacPherson strut suspensions, strut replacement involves the following steps.
  Hoist the vehicle, remove the wheels, and mark the attaching bolts/nuts.
  Remove the upper strut mounting bolts except for one to hold the strut until ready to remove the strut assembly.
  Remove the brake caliper or brake hose from the strut housing.

## Slide 64: MACPHERSON STRUT REPLACEMENT (2 OF 2)
Replacement Step Continued…
  After removing all lower attaching bolts, remove the final upper strut bolt and remove the strut assembly from the vehicle.
  Place the strut assembly into a strut spring compressor fixture.
  Compress the coil spring enough to relieve the tension on the strut rod nut.
  After removing the strut rod nut, remove the upper strut bearing assembly and the spring.

## Slide 65: Figure 117.37 Removing the upper strut mounting bolts. Some experts recommend leaving one of the upper strut mount nuts loosely attached to prevent the strut from falling when the lower attaching bolts are removed

## Slide 66: Figure 117.38 A brake hydraulic hose is often attached to the strut housing. Sometimes all that is required to separate the line from the strut is to remove a spring clip

## Slide 67: Figure 117.39 Use a strut spring compressor fixture to compress the spring on a MacPherson strut before removing the strut retaining nut

## Slide 68: Figure 117.40 Removing the strut rod nut. The strut shaft is being helped with one wrench while the nut is being removed with the other wrench. Notice that the spring is compressed before the nut is removed

## Slide 69: Figure 117.41 Typical MacPherson strut showing the various components

## Slide 70: Figure 117.42 After installing the replacement strut cartridge, reinstall the spring and upper bearing assembly after compressing the spring. Notice that the strut is being held in a strut spring compressor fixture

## Slide 71: Figure 117.43 Before final assembly, make sure the marks you made are aligned. Some struts are manufactured with marks to ensure proper reassembly

## Slide 72: Figure 117.44 The strut on a modified MacPherson strut assembly can be replaced by removing the upper mounting nuts

## Slide 73: STABILIZER BAR LINKS AND BUSHINGS
Diagnosis
  The most common symptom of defective stabilizer bar links or bushings is noise while turning, especially over bumps.
Replacement
  Stabilizer links are usually purchased as a kit consisting of replacement rubber bushings, retainers, a long bolt, and spacer with a nut and lock nut.
  Stabilizer bar bushing replacement involves the removal (unbolting) of the bushing retainers that surround the bushing.

## Slide 74: Figure 117.45 Stabilizer bar links should be replaced as a pair

## Slide 75: STRUT ROD BUSHINGS
Diagnosis
  When strut rod bushings fail, the lower control arm can move forward and backward during braking or when hitting bumps in the road.
Replacement
  The strut rod must be removed from the vehicle and then the replacement rubber bushings can be installed.

## Slide 76: Figure 117.46 A strut rod as viewed from the front of the vehicle

## Slide 77: Figure 117.47 Typical strut rod bushing with rubber on both sides of the frame to help isolate noise, vibration, and harshness from being transferred to the passengers

## Slide 78: FRONT COIL SPRINGS
Diagnosis
  Sagging springs can cause the vehicle to bottom out against the suspension bumpers, and cause the tires to slide laterally (side to side) across the pavement.
Replacement
  Springs should be replaced in pairs.
  Several aftermarket alternatives are available.
  Care should be exercised when compressing a spring.
  Follow manufacturers procedures when replacing springs.

## Slide 79: Figure 117.48 Notice that if the front coil springs are sagging, the resulting angle of the lower control arm causes the wheels to move from side to side as the suspension moves up and down. Note the difference between the distance at “A” with good springs and the distance at “B” with sagging springs

## Slide 80: Figure 117.49 A spring compressor is required by most vehicle manufacturers to be used whenever disassembling a coil spring suspension system

## Slide 81: Figure 117.50 The steering knuckle has been disconnected from the lower ball joint. The lower control arm and the coil spring are being held up by a floor jack

## Slide 82: Figure 117.51 A rubber mallet is being used to support the upper control arm as the lower control is being lowered using a floor jack. After all of the tension has been removed from the coil spring, it can be removed and the replacement installed

## Slide 83: Figure 117.52 Spring insulators are installed between the spring seat and the coil spring to reduce noise

## Slide 84: Figure 117.53 The holes in the lower arm are not only used to allow water to drain from the spring seat, but also used as a gauge to show the service technician that the coil spring is correctly seated

## Slide 85: QUESTION 3: ?
What are the symptoms of a failed coil spring?

## Slide 86: ANSWER 3:
Vehicle sags, suspension bottoms out and tire slide on the pavement.

## Slide 87: STEERING KNUCKLES
Diagnosis
  Unless a thorough inspection is performed during a wheel alignment, a bent steering knuckle is often overlooked.
Replacement
  If the steering knuckle is bent or damaged, it must be replaced.

## Slide 88: TORSION BARS
Adjustment
  Most torsion bar suspensions are designed with an adjustable bolt to permit the tension on the torsion bar to be increased or decreased to change the ride height.
  Adjustments are typically made during an aligment.

## Slide 89: Figure 117.54 By rotating the adjusting bolt, the vehicle can be raised or lowered

## Slide 90: CONTROL ARM BUSHINGS
Diagnosis
  Defective control arm bushings are a common source of vehicle handling and suspension noise problems.
Replacement
  To remove an old bushing from a control arm, the control arm must first be separated from the suspension and/ or frame of the vehicle.
  Bushings are typically pressed in and out of the control arm.
  Some bushings are not serviceable.

## Slide 91: Figure 117.55 An adapter and a press or large clamp are used to remove the old bushing from the control arm and to install a new bushing

## Slide 92: STRUT REPLACEMENT

## Slide 93: 1. The tools needed to replace a front strut assembly include several sockets and a ball-peen hammer, plus a strut compressor.

## Slide 94: 2. After safely hoisting the vehicle to elbow height and removing the wheel covers, remove the front tire/wheel assembly.

## Slide 95: 3. Remove the two strut retaining nuts.

## Slide 96: 4. Before using a hammer to drive the retaining bolts from the steering knuckle, thread the nut into the bolt backwards to prevent causing damage to the threads.

## Slide 97: 5. Remove the retaining bolts and separate the strut from the steering knuckle.

## Slide 98: 6. Lower the vehicle and remove the upper strut retaining fasteners.

## Slide 99: 7. Hold the strut while removing the last upper retaining nut and then remove the strut assembly.

## Slide 100: 8. After the strut has been removed from the vehicle, install the assembly into a strut compressor.

## Slide 101: 9. Position the jaws of the compressor under the bearing assembly as per the vehicle manufacturer’s instructions.

## Slide 102: 10. Turn the compressor wheel until all tension of the spring has been relieved from the upper bearing assembly.

## Slide 103: 11. Remove the strut retaining nut.

## Slide 104: 12. Remove the strut assembly.

## Slide 105: 13. Before installing the replacement strut, check the upper bearing by exerting a downward force on the bearing while rotating and check for roughness. Replace if necessary.

## Slide 106: 14. Install the strut from underneath the spring compressor fixture.

## Slide 107: 15. Install the strut retaining nut. Most vehicle manufacturers specify that the strut retaining nut be replaced and the old one discarded.

## Slide 108: 16. Before loosening the tension, check that the coil spring is correctly located at both the top and the bottom, then release the tension on the spring.

## Slide 109: 17. Remove the strut assembly from the compressor and back of the vehicle and install the upper fasteners. Do not torque to specifications until the lower fasteners have been installed.

## Slide 110: 18. Attach the lower strut to the steering knuckle using the original hardened bolts and nuts.

## Slide 111: 19. Using a torque wrench, torque all fasteners to factory specifications.

## Slide 112: 20. Install the tire/wheel assembly, lower the vehicle, and torque the lug nuts to factory specifications. Align the vehicle before returning it to the customer.

## Slide 113: Copyright