## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 120
Steering Columns and Gears
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
120.1 Describe the purpose and function of a steering wheel.
120.2 Explain how to remove a steering wheel.
120.3 Discuss steering columns and intermediate shafts.
120.4 Explain the purpose and function of conventional steering gears.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
120.5 Explain how a recirculating ball steering gear works.
120.6 Describe how a rack-and-pinion steering gear works.
120.7 This chapter will help prepare for Suspension and Steering (A4) ASE certification test content area “A” (Steering System Diagnosis and Repair).

## Slide 4: STEERING WHEELS
Purpose and Function
  The steering wheel, which consists of a rigid rim and a number of spokes connecting the rim to a center hub, attaches to the top of the steering shaft at its center.
Air Bags
  The module fits in front of the nut that secures the steering wheel to the steering shaft.
  Bolts at the back of the steering wheel fasten the airbag module to the steering wheel.

## Slide 5: Figure 120.1 A steering wheel assembly includes a driver’s side air bag module plus many also include steering wheel controls

## Slide 6: Figure 120.2 The airbag inflates at the same time the driver moves toward the steering wheel during a front-end collision and supplements the protection of the safety belt

## Slide 7: Figure 120.3 The airbag module attaches to the steering wheel and is removed as an assembly to service the steering wheel and column

## Slide 8: STEERING WHEEL REMOVAL
If the steering wheel must be removed, first disconnect the airbag wire connector at the base of the steering column.
After removal of the airbag inflator module, remove the steering wheel retaining nut.
Note the locating marks on the steering wheel and steering shaft.
Use a steering wheel puller to remove the steering wheel from the steering shaft.

## Slide 9: Figure 120.4 Most vehicles have alignment marks made at the factory on the steering shaft and steering wheel to help the service technician keep the steering wheel in the center position

## Slide 10: Figure 120.5 A puller being used to remove a steering wheel after the steering wheel retaining nut has been removed

## Slide 11: QUESTION 1: ?
How is the steering wheel typically retained on the steering shaft?

## Slide 12: ANSWER 1:
A nut holds the steering wheel on a splined and tapered shaft.

## Slide 13: STEERING COLUMNS (1 OF 4)
Purpose and Function
  The steering shaft transmits rotary motion from the steering wheel to the steering gear.
Steering Shaft
  The steering shaft extends from the steering wheel to the steering gear.
Universal Joint
  Universal joints allow changes in the angle between two rotating shafts.

## Slide 14: STEERING COLUMNS (2 OF 4)
Flexible Couplings
  A flexible coupling is a simple device made of rubber, or rubber reinforced with fabric, that is placed between two shafts to allow for a change in angle between them.
Column Cover
  To keep the wiring from the jacket-mounted switches out of sight, the part of the steering column that extends into the passenger compartment is shrouded by the column cover.

## Slide 15: STEERING COLUMNS (3 OF 4)
Collapsible Column
  Federal law requires that steering columns and shafts collapse to absorb some of the energy of the crash and lessen the danger of injury to the driver.
Tilt Mechanisms
  Allow the driver to adjust the angle of the steering wheel relative to the steering column.

## Slide 16: STEERING COLUMNS (4 OF 4)
Telescoping Steering Columns
  The top of the steering shaft and jacket can be pulled out toward the driver or pushed in toward the dashboard, and then locked into the new position.
Steering Column Construction
  The construction on the steering column varies with the design of the dash and the type of steering system used on the vehicle.
  Follow the manufacturers instructions when disassembling and reassembling the steering column.

## Slide 17: Figure 120.6 The steering shaft links the steering wheel to the steering gear while the column jacket, which surrounds part of the shaft, holds support brackets and switches. This steering shaft has a small intermediate section between the main section and the steering gear

## Slide 18: Figure 120.7 A pot joint is a flexible coupling used to join two shafts that allow plunging motion

## Slide 19: Figure 120.8 A typical intermediate steering shaft assembly showing a U-joint and related components

## Slide 20: Figure 120.9 A flexible coupling is used to isolate road noise and vibration from the steering shaft

## Slide 21: Figure 120.10 Steering column covers are often part of the interior trim

## Slide 22: Figure 120.11 Collapsible steering columns include a mesh design that crushes easily, a bearing design that allows one section of the column to slide into the other, and a breakaway device that separates the steering column from the body of the vehicle in the event of a front-end collision

## Slide 23: Figure 120.12 Tilt mechanisms vary by design and vehicle manufacturer, although most use a ratchet to position the top portion of the steering column

## Slide 24: Figure 120.13 Typical steering column showing all of the components from the steering wheel to the steering gear. Note that this column uses a column-type electric power steering system (EPS) and a tilt wheel

## Slide 25: Figure 120.14 The steering shaft splines onto the steering wheel

## Slide 26: Figure 120.15 The toe plate seals the hole from the steering shaft and helps seal out noise and moisture

## Slide 27: Figure 120.16 The upper portion of the steering column contains the combination switch, often called the multi-function switch used to control many functions

## Slide 28: Figure 120.17 The upper section of the steering column contains the steering shaft bearing

## Slide 29: Figure 120.18 The lock plate engages an ignition lock pawl to keep the steering wheel in one position when the ignition is off

## Slide 30: QUESTION 2: ?
Why does federal law require a steering column and shaft to be collapsible?

## Slide 31: ANSWER 2:
To absorb energy in a crash and reduce the risk of injury.

## Slide 32: CONVENTIONAL STEERING GEAR
Purpose and Function
  All steering gears have an input gear, which transmits rotary movement from the steering wheel into the steering gear, and an output gear, which causes the steering linkage to move laterally.
Steering Gear Ratio
  If the steering wheel is rotated 20 degrees and results in the front wheels rotating 1 degree, then the steering gear ratio is 20:1 (read as “20 to 1”).
  Most steering gears and some rack-and-pinion steering gears feature a variable ratio.

## Slide 33: Figure 120.19 As the steering wheel is turned, the nut moves up or down on the threads, shown using a bolt to represent the worm gear and the nut representing the gear nut that meshes with the teeth of the sector gear

## Slide 34: Figure 120.20 Steering gear ratio is the ratio between the number of degrees the steering wheel is rotated to the number of degrees the front wheel turns

## Slide 35: Figure 120.21 Constant-ratio steering gear sector shaft. Notice that all three gear teeth are the same size

## Slide 36: Figure 120.22 Variable-ratio steering gear sector shaft. Notice the larger center gear tooth

## Slide 37: Figure 120.23 The sector gear meshes with the gear teeth on the ball nut

## Slide 38: RECIRCULATING BALL STEERING GEAR
Parts and Operation
  The end of the steering gear input shaft, or worm shaft, splines to the steering shaft U-joint and provides rotary input to the steering gear.
  The adjuster plug at the lower end of the worm gear holds the worm gear, shaft, and bearings inside the steering gear housing.
  Steel balls roll through the tunnels formed by the ball nut grooves and the worm gear thread.

## Slide 39: Figure 120.24 A typical manual recirculating ball steering gear

## Slide 40: Figure 120.25 The sector shaft is supported by bushings, one in the housing and one in the side cover

## Slide 41: STEERING GEAR ADJUSTMENTS
Worm bearing preload is adjusted by one of two methods: turning an adjustment nut or screw or installing selectively sized shims.
Gear mesh preload (over-center adjustment) determines how sensitive the steering gear is to small steering wheel movements during straight-ahead driving.
Sector shaft endplay is a measurement of how much room the sector shaft has to slide axially.

## Slide 42: Figure 120.26 Worm bearing preload is a turning force measured in inch-pounds or Newton-meters and worm endplay is axial movement measured in fractions of an inch or millimeters

## Slide 43: Figure 120.27 The first step to adjust worm gear freeplay is to bottom the worm gear nut, using a spanner wrench designed to fit into the two holes in the nut

## Slide 44: Figure 120.28 After the worm gear nut has been tightened, measure 1/2 inch (13 mm) and mark the case. Using the spanner wrench, rotate the worm gear nut counterclockwise 1/2 inch, align the marks, and then tighten the retaining nut. This procedure gives the proper worm gear endplay

## Slide 45: Figure 120.29 After the worm bearing preload procedure has been completed, use the torque wrench to measure the rotating torque, which should be 6- to 15 inch-pounds. If the rotating torque is within the specified range, adjust the overcenter adjustment screw until you achieve 6- to 10 inch-pounds more rotating torque and then tighten the retaining nut

## Slide 46: Figure 120.30 Sector shaft endplay is the measurement of how far the sector shaft can move axially and is measured in fractions of an inch or millimeters

## Slide 47: RACK AND PINION STEERING GEAR
Parts and Operation
  The pinion gear teeth mesh with the teeth on the rack so that when the pinion gear turns, it pushes the rack from side to side.
  The rack connects directly to the tie rod in the steering linkage to move the linkage back and forth in a straight line.
  Most rack-and-pinion units use a small metal tube running along the outside of the housing to connect the two boots and transfer air from one to the other.

## Slide 48: Figure 120.31 Rack-and-pinion steering gear operation is simple, direct, and the rack is in a straight line to the front wheels

## Slide 49: Figure 120.32 A typical manual rack-and-pinion steering gear used in a small front-wheel-drive vehicle

## Slide 50: Figure 120.33 The spring-loaded rack support positions the rack to keep it from rubbing against the housing and establishes the pinion torque

## Slide 51: Figure 120.34 A small air tube is used to transfer air between the boots as they extend and compress during turns

## Slide 52: Figure 120.35 This manual rack-and pinion steering gear mounts to the bulkhead (firewall), whereas others mount to the engine cradle or frame of the vehicle

## Slide 53: RACK AND PINION ADJUSTMENTS
Pinion torque is a measurement of how much turning force is needed at the input shaft for the pinion to overcome the resistance of the rack and move it.
To provide adjustable pinion bearing preload, there may be a threaded adjustment mechanism or selectively sized shims that install behind a shim cover.

## Slide 54: Figure 120.36 Pinion torque is a turning torque force measured in inch-pounds or Newton-meters. Tightening the rack support against the rack increases the pinion torque

## Slide 55: Figure 120.37 Pinion bearing preload is a measurement of the turning force required to overcome the resistance of the pinion shaft bearings

## Slide 56: Figure 120.38 To adjust the rack-and-pinion gear preload, loosen the retaining nut and tighten the adjuster nut until it bottoms. Then loosen 60 degrees (one “flat” of the six-sided retainer). Tighten retaining nut

## Slide 57: QUESTION 3: ?
What steering gear adjustments are possible on a typical rackand-
pinion steering gear?

## Slide 58: ANSWER 3:
Pinion bearing preload.

## Slide 59: Copyright