## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 19
Diesel Engine Operation and Diagnosis
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
19.1 State the characteristics of diesel engines.
19.2. Describe the fuel tank, lift pump, injection pump, and engine-driven vacuum pump.
19.3. Explain the HEUI system.
19.4 Discuss the purpose of glow plugs, diesel fuel heaters, diesel injector nozzles, and accelerator pedal position sensors.
19.5 Explain the purpose of diesel engine turbochargers.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
19.6 Discuss the purpose of the exhaust gas recirculation system, selective catalytic reduction, and diesel oxidation catalysts.
19.7 Explain diesel particulate matter, and discuss the function of diesel exhaust particulate filters and selective catalytic reduction.
19.8 Discuss diesel exhaust smoke diagnosis and performance diagnosis.
19.9 Discuss compression testing, glow plug resistance balance test, injector pop testing, and diesel emission testing.

## Slide 4: DIESEL ENGINES (1 of 3)
Fundamentals
  1892: Rudolf Diesel perfects the compression ignition engine.
  16:1 compression ratio to generate heat of compression.
  Fuel burns and gasses expands creating power.
Advantages/Disadvantages
  More torque, greater fuel economy, long service life.
  Engine noise, exhaust smell, cold weather startability.

## Slide 5: DIESEL ENGINES (2 of 3)
Construction
  Heavier than gasoline engine.
  Torque much greater than same size gasoline engine.
Air-Fuel Ratios
  Varies from 85:1 (very lean) to 20:1 (rich)
  Higher air fuel ratio leads to increased efficiency.

## Slide 6: DIESEL ENGINES (3 of 3)
Indirect Injection
  Fuel is injected into a prechamber.
Direct Injection
  Fuel is injected directly into the cylinder.
Diesel Fuel Ignition
  Intake stroke fills cylinder with air.
  Compression stroke raises cylinder pressure.
  Fuel injected near TDC on compression stroke.
  Power stroke a result of fuel ignition.
  Exhaust stroke starts flow of gasses out of cylinder.

## Slide 7: Figure 19.1 Diesel combustion occurs when fuel is injected into the hot, highly compressed air in the cylinder

## Slide 8: Figure 19.2 A typical high-pressure common rail (HPCR)-type diesel fuel system

## Slide 9: Chart 19-1: Comparison between a typical gasoline and a diesel engine.

## Slide 10: Figure 19.3 A Cummins diesel engine as found in a Dodge (Ram) pickup truck. A high-pressure pump (up to 30,000 PSI) is used to supply diesel fuel to this common rail, which has tubes running to each injector. Note the thick cylinder walls and heavy duty construction

## Slide 11: Figure 19.4 A rod/piston assembly from a 5.9 liter Cummins diesel engine used in a Ram pickup truck

## Slide 12: Figure 19.5 An indirect injection diesel engine uses a prechamber and a glow plug

## Slide 13: Figure 19.6 A direct injection diesel engine injects the fuel directly into the combustion chamber. Many designs do not use a glow plug

## Slide 14: QUESTION 1: ?
What is the difference between direct injection and indirect
injection?

## Slide 15: ANSWER 1:
Fuel is injected into a prechamber in an indirect injection system and directly into the cylinder in a direct injection system.

## Slide 16: THREE PHASES OF COMBUSTION
Ignition Delay: Fuel injection begins but ignition does not occur immediately.
Rapid Combustion: The fuel first starts to burn creating a sudden rise in cylinder pressure.
Controlled Combustion: The burning of fuel after rapid combustion and the continued injection of fuel.

## Slide 17: FUEL TANK AND LIFT PUMP
Filler Neck: Larger neck for diesel fuel (24 mm for diesel versus 21 mm for gasoline)
No evaporative emission devices.
Lift Pump: Typically an in-tank low-pressure fuel pump.
Water-Fuel Separator: Separates the heavier water from the diesel fuel.
Fuel Temperature Sensor: Adjust fuel delivery based on density of fuel.

## Slide 18: Figure 19.7 A fuel temperature sensor is being tested using an ice bath

## Slide 19: INJECTION PUMP
The Need for High-Pressure Fuel Pump: Increase fuel pressure to the extremely high pressures needed for injection.
Distributor Injection Pump: Provide high pressure fuel to each individual injector.
High-Pressure Common Rail: High pressure fuel is feed to common rail. Computer controlled injectors use this fuel source for injection.

## Slide 20: Figure 19.8 A typical distributor-type diesel injection pump showing the pump, lines, and fuel filter

## Slide 21: Figure 19.9 A schematic of a Stanadyne diesel fuel–injection pump assembly showing all of the related components

## Slide 22: Figure 19.10 Overview of a computer-controlled high-pressure common rail V-8 diesel engine

## Slide 23: ENGINE-DRIVEN VACUUM PUMP
Diesel engines create little or no vacuum.
Engine driven vacuum pump supplies vacuum to components that need it to operate.

## Slide 24: HEUI SYSTEM
Operation
  The engine oil is pressurized to provide an opening pressure strong enough to overcome the fuel pressure when the solenoid is commanded to open by the PCM.
  The injectors, which are hydraulically actuated by engine oil pressure from the high-pressure oil pump, are then fired by the powertrain control module (PCM).

## Slide 25: Figure 19.11 A HEUI injector from a Ford Power Stroke diesel engine. The O-ring grooves indicate the location of the O-rings that seal the fuel section of the injector from coolant and from the engine oil

## Slide 26: DIESEL INJECTOR NOZZLES
Diesel injector nozzles are spring-loaded closed valves that spray fuel directly into the combustion chamber or pre-combustion chamber when the injector is opened.
  Heat Shield
  Injector Body
  Diesel Injector Needle Valve
  Injector Pressure Chamber

## Slide 27: Figure 19.12 Typical computer-controlled diesel engine fuel injectors

## Slide 28: Figure 19.13 A Duramax injector showing all the internal parts

## Slide 29: GLOW PLUGS
Equipped on both indirect and direct injection fuel systems.
Used to provide heat to help ignite the fuel.
As glow plug heats its resistance increases.
Operation controlled by Powertrain Control Module (PCM)
May be operated after vehicle start-up to reduce white smoke.

## Slide 30: Figure 19.14 A glow plug assortment showing the various types and sizes of glow plugs used. Always use the specified glow plugs

## Slide 31: Figure 19.15 A schematic of a typical glow plug circuit. Notice that the glow plug relay and intake air heater relay are both computer controlled

## Slide 32: Figure 19.16 The intake heater grid is used to warm the intake air and increase pre-ignition temperatures. The heater may continue to be cycled to decrease the amount of time needed to warm the engine

## Slide 33: QUESTION 2: ?
Why are glow plugs kept working after the engine starts?

## Slide 34: ANSWER 2:
To reduce white tailpipe smoke.

## Slide 35: DIESEL FUEL HEATERS
Diesel fuel heaters help prevent power loss and stalling in cold weather.
The heater is placed in the fuel line between the tank and the primary filter.
Some fuel heaters are thermostatically controlled, which allows fuel to bypass the heater once it has reached operating temperature.

## Slide 36: ACCELERATOR PEDAL POSITION SENSOR
Instead of a mechanical link from the accelerator pedal to the diesel injection pump, a throttle-by-wire system uses an accelerator pedal position (APP) sensor.
To ensure safety, it consists of (up too) three separate sensors that change in voltage as the accelerator pedal is depressed.
The computer checks for errors by comparing the voltage output of each of the three sensors

## Slide 37: Figure 19.17 A typical accelerator pedal position (APP) sensor uses three different sensors in one package with each creating a different voltage as the accelerator is moved

## Slide 38: DIESEL ENGINE TURBOCHARGERS
Turbocharged Diesels
  A turbocharger greatly increases engine power by pumping additional compressed air into the combustion chambers.
Air Charge Cooler
  Cooler air entering the engine means more power can be produced by the engine.
Variable Turbocharger
  The variable vanes allow for optimal flow at all engine RPMs.

## Slide 39: Figure 19.18 A Cummins diesel turbocharger is used to increase the power and torque of the engine

## Slide 40: Figure 19.19 An air charge cooler is used to cool the compressed air

## Slide 41: Figure 19.20 A variable vane turbocharger allows the boost to be controlled without the need of a wastegate

## Slide 42: EXHAUST GAS RECIRCULATION
The EGR system recycles some exhaust gas back into the intake stream to cool combustion, which reduces oxides of nitrogen (NOx) emissions.
EGR System Components
  EGR Valve
  EGR Cooler
  EGR Pipes

## Slide 43: Figure 19.21 A cutaway showing the exhaust cooler. The cooler the exhaust is, the more effective it is in controlling NOx emissions

## Slide 44: DIESEL PARTICULATE MATTER
Particulates are generally categorized as follows:
  Total suspended particulate (TSP). Refers to all particles between 0.1 and 50 microns.
  PM10. Refers to particulate matter of 10 microns or less (approximately 1/6 the diameter of a human hair).
  PM2.5. Refers to particulate matter of 2.5 microns or less (approximately 1/20 the diameter of a human hair), also called “fine” particles.
Soot Categories
  Fine. Less than 2.5 microns
  Ultrafine. Less than 0.1 micron, and make up 80% to 95% of soot

## Slide 45: Figure 19.22 Relative size of particulate matter to a human hair

## Slide 46: DIESEL OXIDATION CATALYST
Purpose and Function
  Diesel oxidation catalysts (DOC) are used in all light-duty diesel engines, since 2007.
  The main function of the DOC is to start a regeneration event by converting the fuel-rich exhaust gases to heat.
  The DOC reduces Carbon Monoxide (CO) and Hydrocarbons (HC) as well as odor-causing componds.

## Slide 47: Figure 19.23 Chemical reaction within the DOC

## Slide 48: DIESEL EXHAUST PARTICULATE FILTER (1 OF 2)
Purpose and Function
  The diesel particulate filter is a wall flow design filter designed to capture and hold particulate matter and allow exhaust gases to flow through the system.
Operation
  Over time, the trapped particulate matter will begin to clog the filter. The filter must therefore be purged periodically to remove accumulated soot particles. The process of purging soot from the DPF is described as regeneration.

## Slide 49: DIESEL EXHAUST PARTICULATE FILTER (2 OF 2)
Exhaust Gas Temperature Sensors
  Exhaust gas temperature sensors are used to help the PCM control the DPF.
DPF Differential Pressure Sensor
  Measures the level of restriction in the filter assembly.
DPF Regeneration
  Passive Regeneration
  Active Regeneration
Ash Loading
  To service the ash load, most DPF units are replaced.

## Slide 50: Figure 19.24 After-treatment of diesel exhaust is handled by the DOC and DPF

## Slide 51: Figure 19.25 The soot is trapped in the passages of the DPF. The exhaust has to flow through the sides of the trap and exit

## Slide 52: Figure 19.26 EGT 1 and EGT 2 are used by the PCM to help control after-treatment system operation

## Slide 53: Figure 19.27 Regeneration burns the soot and renews the DPF

## Slide 54: FREQUENTLY ASKED QUESTION

## Slide 55: Figure 19.28 The post-injection pulse occurs to create the heat needed for regeneration

## Slide 56: FREQUENTLY ASKED QUESTION

## Slide 57: Figure 19.29 The exhaust is split into two outlets and has slits to help draw outside air in as the exhaust leaves the tailpipe. The end result is cooler exhaust gases exiting the tailpipe

## Slide 58: SELECTIVE CATALYST REDUCTION
Purpose and Function
  Selective catalytic reduction (SCR) is a method used to reduce NOx emissions by injecting urea into the exhaust stream.
Advantages of SCR
  Potential higher engine power output for the same size engine and reduced NOx emissions up to 90%.
Disadvantages of SCR
  Onboard storage tank required for the urea, and increased customer costs due to refilling.

## Slide 59: Figure 19.30 Diesel exhaust fluid is housed in a separate container that holds from 5 to 10 gallons, or enough to last until the next scheduled oil change, in most diesel vehicles that use SCR

## Slide 60: Figure 19.31 Urea (diesel exhaust fluid) injection is used to reduce NOx exhaust emissions. It is injected after the diesel oxidation catalyst (DOC) and before the diesel particulate filter (DPF) on this 6.7 liter Ford diesel engine

## Slide 61: DIESEL EXHAUST SMOKE DIAGNOSIS
Black Smoke
  Incomplete combustion because of a lack of air or a fault in the injection system.
White Smoke
  Occurs most often during cold engine starts because the smoke is usually condensed fuel droplets.
Blue or Gray Smoke
  Is usually due to oil consumption caused by worn piston rings, scored cylinder walls, or defective valve stem seals.

## Slide 62: DIESEL PERFORMANCE DIAGNOSIS
Begin by checking the oil
  High oil level may indicate fuel in the crankcase.
Scan data is used to find common faults:
  Hard starting
  No start
  Extended cranking before start
  Low Power

## Slide 63: Chart 19-2: Cummins 5.9 and 6.7 liter. The values can be obtained by using a scan tool and basic test equipment. Always follow the vehicle manufacturer’s recommended procedures.

## Slide 64: Chart 19-2: GM Duramax. The values can be obtained by using a scan tool and basic test equipment. Always follow the vehicle manufacturer’s recommended procedures.

## Slide 65: Chart 19-2: Ford Power Stroke. The values can be obtained by using a scan tool and basic test equipment. Always follow the vehicle manufacturer’s recommended procedures.

## Slide 66: Figure 19.32 A pressure gauge checking the fuel pressure from the lift pump on a Cummins 6.7 liter diesel

## Slide 67: COMPRESSION TESTING
A compression test is fundamental for determining the mechanical condition of a diesel engine.
To perform a compression test the following will have to done:
  Remove the glow plug (if equipped) or the injector.
  Use a diesel compression gauge, as the compression is too high to use a gasoline engine compression gauge.

## Slide 68: Figure 19.33 A compression gauge that is designed for the higher compression ratio of a diesel engine should be used when checking the compression

## Slide 69: GLOW PLUG RESISTANCE BALANCE TEST
Glow plugs increase in resistance as their temperature increases.
All glow plugs should have about the same resistance when checked with an ohmmeter.
A similar test of the resistance of the glow plugs can be used to detect a weak cylinder.
A weak cylinder will generate less heat and the resistance of the glow plug will be different.

## Slide 70: INJECTOR POP TESTING
A pop tester is a device used for checking a diesel injector nozzle for proper spray pattern.
The spray pattern should be a hollow cone, but will vary depending on design.
The nozzle should also be tested for leakage (dripping of the nozzle) while under pressure.

## Slide 71: Figure 19.34 A typical pop tester used to check the spray pattern of a diesel engine injector

## Slide 72: DIESEL EMISSION TESTING
Opacity Test
  Opacity means the percentage of light that is blocked by the exhaust smoke.
Snap Acceleration Test
  White smoke emissions are measure during a rapid acceleration of the engine.
Rolling Acceleration Test
  White smoke emissions are measured in low gear on acceleration.
Stall Acceleration Test
  Opacity measured during an engine stall test.

## Slide 73: Chart 19-3: An opacity test is sometimes used during a state emission test on diesel engines.

## Slide 74: Tech Tip

## Slide 75: Figure 19.35 The letters on the side of this injector on a Cummins 6.7 liter diesel indicate the calibration number for the injector

## Slide 76: QUESTION 3: ?
What is the purpose of the letters and numbers on the side of a common rail injector?

## Slide 77: ANSWER 3:
They represent the calibration code.

## Slide 78: Copyright