## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 26
Engine Condition Diagnosis
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
26.1 Discuss typical engine-related complaints and engine smoke diagnosis.
26.2 Discuss the importance of the driver’s description and visual checks.
26.3 Discuss engine noise diagnosis.
26.4 Explain oil pressure testing and the purpose of oil pressure warning lamps.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
26.5 Explain compression testing, and compare wet and running compression tests.
26.6 Describe cylinder leakage test and cylinder power balance test.
26.7 Explain the vacuum test and exhaust restriction test.
26.8 Explain how to test back pressure with a vacuum gauge and a pressure gauge, and how to diagnose head gasket failure.
26.9 Discuss the operation of dash warning lights.

## Slide 4: TYPICAL ENGINE-RELATED COMPLAINTS
Excessive oil consumption
Engine misfiring
Loss of power
Smoke from the engine or exhaust
Engine noise

## Slide 5: ENGINE SMOKE DIAGNOSIS
Blue: Indicates the engine is burning oil.
Black: Indicates excessive fuel in the combustion chamber.
White (steam): Indicates water (coolant) in the combustion chamber.

## Slide 6: Figure 26.1 Blowby gases coming out of the crankcase vent hose. As seen on this old high-mileage engine, excessive amounts of combustion gases flow past the piston rings and into the crankcase

## Slide 7: Figure 26.2 White steam is usually an indication of a blown (defective) cylinder head gasket that allows engine coolant to flow into the combustion chamber where it is turned into steam

## Slide 8: QUESTION 1: ?
What does blue exhaust smoke indicate?

## Slide 9: ANSWER 1:
The engine has an oil consumption concern.

## Slide 10: THE DRIVER IS YOUR BEST RESOURCE
Ask the following questions:
When did the problem first occur?
Under what conditions does it occur?
  Cold or hot?
  Acceleration, cruise, deceleration?
  How far was it driven?
  What recent repairs have been performed?

## Slide 11: Tech Tip

## Slide 12: VISUAL CHECKS
Oil level and condition
Coolant level and condition
Oil leaks

## Slide 13: Figure 26.3 What looks like an oil pan gasket leak can be a rocker cover gasket leak. Always look for the highest and most forward place you see oil leaking; that should be repaired first

## Slide 14: Figure 26.4 The transmission and flexplate (flywheel) were removed to check the exact location of this oil leak. The rear main seal and/or the oil pan gasket could be the cause of this leak

## Slide 15: Figure 26.5 Using a black light to spot leaks after adding dye to the oil

## Slide 16: ENGINE NOISE DAIGNOSIS
Engine noises are often difficult to diagnose. Several items that can cause an engine noise include:
  Valves clicking
  Torque converter
  Cracked flex plate
  Loose or defective drive belts or tensioners.
  Piston pin knock
  Timing chain noise
  Rod or main bearing noise

## Slide 17: Figure 26.6 An accessory belt tensioner. Most tensioners have a mark that indicates normal operating location. If the belt has stretched, this indicator mark will be outside of the normal range. Anything wrong with the belt or tensioner can cause noise

## Slide 18: Figure 26.7 A cracked exhaust manifold on a Ford V-8

## Slide 19: OIL PRESSURE TESTING
Proper oil pressure is very important for the operation of any engine.
Low oil pressure can cause engine wear, and engine wear can cause low oil pressure.
Other issues include:
  Low oil level
  Diluted oil
  Stuck oil pressure relief valve
The oil pressure warning lamp will illuminate when pressures drop below 4-7 PSI.
.

## Slide 20: Figure 26.8 To measure engine oil pressure, remove the oil pressure sending (sender) unit usually located near the oil filter. Screw the pressure gauge into the oil pressure sending unit hole

## Slide 21: TECH TIP

## Slide 22: Figure 26.9 A Tech 2 scan tool display showing a fault with cylinder 3. Once the cylinder has been identified, then more detailed tests can be performed to determine the root cause, which could be an ignition, fuel or mechanical issue

## Slide 23: Figure 26.10 The Ford IDS scan tool has a graph function that allows the technician to view the data on the cylinder contribution test visually, making diagnosis easier. In this example, the cylinders on bank 2 on a Ford V-8 (cylinders 7, 6, 5, and 8) are weak

## Slide 24: TECH TIP

## Slide 25: Figure 26.11 The paper test involves holding a piece of paper near the tailpipe of an idling engine. A good engine should produce even, outward puffs of exhaust. If the paper is sucked in toward the tailpipe, a burned valve is a possibility

## Slide 26: COMPRESSION TEST
Cranking compression test
  Dry
  Wet
Running (dynamic) compression test
Relative compression test
Cylinder leakage test

## Slide 27: Figure 26.12 A two-piece compression gauge set. The threaded hose is screwed into the spark plug hole after removing the spark plug. The gauge part is then snapped onto the end of the hose

## Slide 28: TECH TIP

## Slide 29: Figure 26.13 Use a vacuum or fuel line hose over the spark plug to install it without danger of cross-threading the cylinder head

## Slide 30: Figure 26.14 Badly burned exhaust valve. A compression test could have detected a problem, and a cylinder leakage test (leakdown test) could have been used to determine the exact problem

## Slide 31: Figure 26.15 (a) A relative compression test using an amp clamp around the starter motor power cable and a Pico scope. (b) The result is a waveform that displays the current needed for each cylinder is the same, indicating that all cylinders have the same relative compression

## Slide 32: Figure 26.16 A typical handheld cylinder leakage tester

## Slide 33: Figure 26.17 A whistle stop used to find top dead center. Remove the spark plug and install the whistle stop, then rotate the engine by hand. When the whistle stops making a sound, the piston is at the top

## Slide 34: QUESTION 2: ?
What the three types of compression test?

## Slide 35: ANSWER 2:
Cranking, running and relative compression tests.

## Slide 36: CYLINDER BALANCE TEST
The purpose of a cylinder power balance test is to determine if all cylinders are contributing power equally.
The acceptable method of canceling cylinders, which will work on all types of ignition systems, including distributorless, is to ground the secondary current for each cylinder.

## Slide 37: Figure 26.18 Using a vacuum hose and a test light to ground one cylinder at a time on a distributorless ignition system.

## Slide 38: VACUUM TESTS
Vacuum is pressure below atmospheric pressure and is measured in inches (or millimeters) of mercury (Hg).
Cranking Vacuum Test
Idle Vacuum Test
Low and Steady Vacuum
Fluctuating Vacuum

## Slide 39: Figure 26.19 An engine in good mechanical condition should produce 17 to 21 inch Hg of vacuum at idle at sea level

## Slide 40: Figure 26.20 A steady but low reading could indicate retarded valve or ignition timing

## Slide 41: Figure 26.21 A gauge reading with the needle fluctuating 3 to 9 inch Hg below normal often indicates a vacuum leak in the intake system

## Slide 42: Figure 26.22 A leaking head gasket can cause the needle to vibrate as it moves through a range from below to above normal

## Slide 43: Figure 26.23 An oscillating needle 1 or 2 inch Hg below normal could indicate an incorrect air-fuel mixture (either too rich or too lean)

## Slide 44: Figure 26.24 A rapidly vibrating needle at idle that becomes steady as engine speed is increased indicates worn valve guides

## Slide 45: Figure 26.25 If the needle drops 1 or 2 inch Hg from the normal reading, one of the engine valves is burned or not seating properly

## Slide 46: Figure 26.26 Weak valve springs will produce a normal reading at idle, but as engine speed increases, the needle will fluctuate rapidly between 12 and 24 inch Hg

## Slide 47: Figure 26.27 A steady needle reading that drops 2 or 3 inch Hg when the engine speed is increased slightly above idle indicates that the ignition timing is retarded

## Slide 48: Figure 26.28 A steady needle reading that rises 2 or 3 inch Hg when the engine speed is increased slightly above idle indicates that the ignition timing is advanced

## Slide 49: Figure 26.29 A needle that drops to near zero when the engine is accelerated rapidly and then rises slightly to a reading below normal indicates an exhaust restriction

## Slide 50: QUESTION 3: ?
What does a fluctuating vacuum gauge indicate?

## Slide 51: ANSWER 3:
A vacuum leak in the intake system.

## Slide 52: EXHAUST RESTRICTION TEST
Common causes of restricted exhaust include the following:
  Clogged catalytic converter
  Clogged or restricted muffler
  Damaged or defective piping
Test back pressure:
  With a vacuum gauge
  With a pressure gauge

## Slide 53: Figure 26.30 A technician-made adapter used to test exhaust system back pressure

## Slide 54: DIAGNOSING HEAD GASKET FAILURE
Several items can be used to help diagnose a head gasket failure.
  Exhaust gas analyzer
  Chemical test
  Bubbles in coolant
  Excessive exhaust steam

## Slide 55: Figure 26.31 A tester that uses a blue liquid to check for exhaust gases in the exhaust, which would indicate a head gasket leak problem

## Slide 56: COMPRESSION TEST

## Slide 57: 1. The tools and equipment needed to perform a compression test include a compression gauge, an air nozzle, and the socket ratchets and extensions that may be necessary to remove the spark plugs from the engine.

## Slide 58: 2. To prevent ignition and fuel-injection operation while the engine is being cranked, remove both the fuel injection fuse and the ignition fuse.

## Slide 59: 3. Block open the throttle (and choke, if the engine is equipped with a carburetor). Keeping the throttle open ensures that enough air will be drawn into the engine so that the compression test results will be accurate.

## Slide 60: 4. Before removing the spark plugs, use an air nozzle to blow away any dirt that may be around the spark plug.

## Slide 61: 5. Remove all of the spark plugs. Be sure to mark the spark plug wires so that they can be reinstalled onto the correct spark plugs after the compression test has been performed.

## Slide 62: 6. Select the proper adapter for the compression gauge. The threads on the adapter should match those on the spark plug.

## Slide 63: 7. If necessary, connect a battery charger to the battery before starting the compression test. It is important that consistent cranking speed be available for each cylinder being tested.

## Slide 64: 8. Make a note of the reading on the gauge after the first “puff,” which indicates the first compression stroke that occurred on that cylinder as the engine was being rotated.

## Slide 65: 9. After the engine has been cranked for four “puffs,” stop cranking the engine and observe the compression gauge.

## Slide 66: 10. Record the first puff and this final reading for each cylinder. The final readings should all be within 20% of each other.

## Slide 67: 11. If a cylinder(s) is lower than most of the others, use an oil can and squirt two squirts of engine oil into the cylinder and repeat the compression test.

## Slide 68: 12. If the gauge reading is now much higher than the first test results, then the cause of the low compression is due to worn or defective piston rings.

## Slide 69: Copyright