## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 29
Engine Cleaning and Crack Detection
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES
29.1 Explain the mechanical cleaning procedure of engines.
29.2 Discuss chemical cleaners.
29.3 Compare spray and steam washing, thermal cleaning, tank and vapor cleaning, and ultrasonic and vibratory cleaning.
29.4 Explain crack detection and crack repair.

## Slide 3: MECHANICAL CLEANING
Scraping
  The scraper most frequently used is a putty knife, or a plastic card.
Abrasive Pads or Discs
  White: Finest grit size
  Yellow: Course Grit
  Green: Cast-iron Only
Media Blasting
  Media blasting with baking soda is the cleaning method of choice for most shops.

## Slide 4: Figure 29.1 Plastic razor blades are available and make an excellent tool to clean gasket surfaces without causing any harm to the engine surfaces

## Slide 5: Figure 29.2 An air-powered grinder attached to a bristle pad being used to clean the gasket surface of a cylinder head.

## Slide 6: Figure 29.3 An abrasive disc commonly called by its trade name, Scotch Brite™ pad

## Slide 7: Figure 29.4 Using baking soda is the recommended way to clean engine parts because any soda that is left on or in the part is dissolved in oil or water, unlike either sand or glass beads, which can be engine damaging

## Slide 8: Figure 29.5 Small engine parts can be blasted clean in a sealed cabinet

## Slide 9: Tech Tip

## Slide 10: QUESTION 1: ?
What is the purpose of mechanical cleaning?

## Slide 11: ANSWER 1:
The purpose of mechanical cleaning is to remove heavy deposits.

## Slide 12: CHEMICAL CLEANERS
pH
  Indicates the amount of chemical activity in the soap.
Solvent-Based Cleaning
  A deposit is said to be soluble when it can be dissolved with a chemical or solvent.
Water-Base (aqueous) Chemical Cleaning
  Used because of environmental concerns.
  Most aqueous-type chemicals are silicate–based and are mixed with water.

## Slide 13: SPRAY AND STEAM WASHING
Spray Washing
  A spray washer directs streams of liquid through numerous high-pressure nozzles to dislodge dirt and grime on an engine surface.
Steam Cleaning
  Steam vapor is mixed with high-pressure water and sprayed on the parts.

## Slide 14: Figure 29.6 A pressure jet washer is similar to a large industrial-sized dishwasher. Each part is then rinsed with water to remove chemicals or debris that may remain there while it is still in the tank

## Slide 15: THERMAL CLEANING
Temperatures Involved:
  600°F (315°C) to 800°F (425°C)
Advantages:
  Cleans the inside as well as the outside
  The waste generated is nonhazardous
Microbial Cleaning:
  uses microbes (living organisms [single-celled bacteria]) that literally “eat” the hydrocarbons (grease and oils) off of the parts being cleaned.
Pyrolytic Oven:
  A high-temperature oven cleans engine parts by decomposing dirt, grease, and gaskets.

## Slide 16: Figure 29.7 A microbial cleaning tank uses microbes to clean grease and oil from parts

## Slide 17: Figure 29.8 (a) A pyrolytic (high-temperature) oven cleans by baking the engine parts. After the parts have been cleaned, they are placed into an airless blaster. This unit uses a paddle to scoop stainless steel shot from a reservoir and forces it against the engine part.

## Slide 18: Figure 29.8 (b) This cleaned engine block has been baked and shot blasted

## Slide 19: TANK AND VAPOR CLEANING
Cold Tank Cleaning
  The cold soak tank is used to remove grease and carbon.
Hot Tank Cleaning
  The hot soak tank is used for cleaning heavy organic deposits and rust from iron and steel parts.
Vapor Cleaning
  The parts to be cleaned are suspended in hot vapors above a perchloroethylene solution.

## Slide 20: ULTRASONIC AND VIBRATORY CLEANING
Ultrasonic Cleaning
  The disassembled parts are placed in a tank of cleaning solution that is then vibrated at ultrasonic speeds to loosen all the soil from the parts.
Vibratory Cleaning
  A vibrating bin with small odd-shaped ceramic or steel pieces, called media, with a cleaning solution of mineral spirits or water-based detergents are used to clean the small parts.
.

## Slide 21: Figure 29.9 An ultrasonic cleaner is used to clean fuel injectors

## Slide 22: CRACK DETECTION
Visual Inspection
  After cleaning, the parts are reexamined for cracks.
Magnetic Crack Detection
  Uses a magnetic field that is commonly referred to by the brand name Magnafluxing.
Fluorescent-Penetrant Detection
  A dark red penetrating chemical is sprayed on the component and tested with a black light.
Pressure Testing
  The head or block is pressurized and then lowered into water, where air bubbles indicate a leak.

## Slide 23: Figure 29.10 The top deck surface of a block is being tested using magnetic crack inspection equipment

## Slide 24: Figure 29.11 If the lines of force are interrupted by a break (crack) in the casting, then two magnetic fields are created and the powder will lodge in the crack

## Slide 25: Figure 29.12 This crack in a vintage Ford 289, V-8 block was likely caused by the technician using excessive force trying to remove the plug from the block.

## Slide 26: Figure 29.13 To make sure that the mark observed in the cylinder wall was a crack, compressed air was forced into the water jacket while soapy water was sprayed on the cylinder wall. Bubbles confirmed that the mark was indeed a crack

## Slide 27: Figure 29.14 A cylinder head is under water and being pressure tested using compressed air. Note that the air bubbles indicate a crack

## Slide 28: QUESTION 2: ?
When id the dye-penetrant testing method most commonly used?

## Slide 29: ANSWER 2:
On parts constructed of aluminum or other nonmagnetic material.

## Slide 30: CRACK REPAIR (1 OF 2)
Crack Concerns
  Cracks in the engine block can cause coolant to flow into the oil or oil into the coolant.
Stop Drilling
  A hole can be drilled at each end of the crack to keep it from extending further.
Crack-Welding Cast Iron
  A highly skilled welding technique that is typically only successful when the entire cast-part is heated red-hot.

## Slide 31: CRACK REPAIR (2 OF 2)
Crack-Welding Aluminum
  Cracks in aluminum can be welded using a Heli-arc® or similar welder that is specially designed to weld aluminum.
Crack Plugging
  In the process of crack plugging, a crack is closed using interlocking tapered plugs. This process can be used on cast-iron or aluminum components.

## Slide 32: Figure 29.15 (a) Before welding, the crack is ground out using a carbide grinder

## Slide 33: Figure 29.15 (b) Here the technician is practicing using the special cast-iron welding torch before welding the cracked cylinder head

## Slide 34: Figure 29.15 (c) This is the finished welded crack before final machining

## Slide 35: Figure 29.15 (d) Note the finished cylinder head after the crack has been repaired using welding

## Slide 36: Figure 29.16 Reaming a hole for a tapered plug

## Slide 37: Figure 29.17 Tapping a tapered hole for a plug

## Slide 38: Figure 29.18 Screwing a tapered plug in the hole

## Slide 39: Figure 29.19 Cutting the plug with a hacksaw

## Slide 40: Figure 29.20 Interlocking plugs

## Slide 41: Figure 29.21 (a) A hole is drilled and tapped for the plugs

## Slide 42: Figure 29.21 (b) The plugs are installed

## Slide 43: Figure 29.21 (c) After final machining, the cylinder head can be returned to useful service

## Slide 44: QUESTION 3: ?
What is the purpose of stop drilling?

## Slide 45: ANSWER 3:
To prevent the crack from extending any further.

## Slide 46: Copyright