## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 34
Engine Blocks
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
34.1 Explain the construction of engine blocks.
34.2 Explain the procedure for engine block service.
34.3 Explain block preparation for assembly.

## Slide 3: ENGINE BLOCKS (1 OF 3)
Construction
  Gray Cast Iron
  Cast Aluminum
  Die-Cast Aluminum Alloy
Block Manufacturing
  Cast-iron cylinder block sand casting technology continues to be improved.
Aluminum Blocks
  Styrofoam is often used as a core when casting an aluminum block

## Slide 4: ENGINE BLOCKS (2 OF 3)
Bedplate Design Blocks
  A bedplate is a structural member that attaches to the bottom of the block and supports the crankshaft.
Casting Numbers
  Casting numbers can be used to check dimensions, such as the cubic inch displacement, and other information, such as year of manufacture.
Block Deck
  The cylinder head is fastened to the top surface of the block, know as the block deck.

## Slide 5: ENGINE BLOCKS (3 OF 3)
Cooling Passages
  In most cylinder designs, the cooling passages extend nearly to the bottom of the cylinder.
Lubricating Passages
  Carry lubricating oil to the required locations. This is accomplished through oil drilled galleries and oil gallery plugs.
Main Bearing Caps
  The main bearing caps are cast or manufactured from sintered or billeted materials, separately from the block.

## Slide 6: QUESTION 1: ?
What is the purpose of a bedplate?

## Slide 7: ANSWER 1:
To support the crankshaft and provide the block with structural support.

## Slide 8: Figure 34.1 The cylinder block usually extends from the oil pan rails at the bottom to the deck surface at the top

## Slide 9: Figure 34.2 An expansion (core) plug is used to block the opening in the cylinder head or block the holes where the core sand was removed after the part was cast

## Slide 10: Figure 34.3 A Styrofoam casting mold used to make the five cylinder engine blocks for the Chevrolet Colorado and the Hummer H3.

## Slide 11: Figure 34.4 Cast-iron dry sleeves are used in aluminium blocks to provide a hard surface for the rings

## Slide 12: Figure 34.5 A dry sleeve is supported by the surrounding cylinder block. A wet sleeve must be thicker to be able to withstand combustion pressures without total support from the block

## Slide 13: Figure 34.6 A bedplate is a structural part of the engine, which is attached between the block and the oil pan and supports the crankshaft

## Slide 14: Figure 34.7 Casting numbers identify the block

## Slide 15: Figure 34.8 The deck is the machined top surface of the block

## Slide 16: Figure 34.9 Cutaway of a Chevrolet V-8 block showing all of the internal passages

## Slide 17: Figure 34.10 Typical oil gallery plugs on the rear of a Chevrolet small block V-8 engine

## Slide 18: Figure 34.11 Small block Chevrolet block. Note the left-hand dipstick hole and a pad cast for a right-hand dipstick

## Slide 19: Figure 34.12 Two-bolt main bearing caps provide adequate bottom end strength for most engines

## Slide 20: Figure 34.13 High-performance and truck engines often use four-bolt main bearing caps for greater durability

## Slide 21: Figure 34.14 Some engines add to the strength of a four-bolt main bearing cap by also using cross bolts through the bolt on the sides of the main bearing caps

## Slide 22: Figure 34.15 A girdle is used to tie all of the main bearing caps together

## Slide 23: ENGINE BLOCK SERVICE (1 OF 4)
Procedures
  OPERATION 1: Main bearing housing bore alignment.
  OPERATION 2 Machining of the block deck surface.
  OPERATION 3 Cylinder boring and honing.
Main Bearing Housing Bore Alignment
  The main bearing journals of a straight crankshaft are in alignment. If not, the crankshaft tends to bend as it rotates.

## Slide 24: ENGINE BLOCK SERVICE (2 OF 4)
Arbor Check Method
  The arbor is installed, then all main caps are tightened to specifications. After tightening, the arbor is checked to make sure it rotates freely, indicating a true centerline.
Machining The Deck Surface Of A Block
  The block deck must be resurfaced in a surfacing machine that can control the amount of metal removed when it is necessary to match the size of the combustion chambers.

## Slide 25: ENGINE BLOCK SERVICE (3 OF 4)
Deck Surface Finishing
  60 to 100 Ra (65 to 110 RMS) for cast iron
  50 to 60 Ra (55 to 65 RMS) for aluminum block decks to be assured of a proper head gasket surface
Cylinder Boring
  Cylinders should be measured across the engine (perpendicular to the crankshaft), where the greatest wear occurs.

## Slide 26: ENGINE BLOCK SERVICE (4 OF 4)
Sleeving the Cylinder
  Cylinder blocks with deep gouges may be able to be salvaged by sleeving the cylinder.
Cylinder Honing
  Honing the cylinder provides the proper surface finish on the cylinder wall for the rings to seat against.
Chamfering the Cylinder Bore
  Removing the top edge of the cylinder bores have sharp edges.

## Slide 27: QUESTION 2: ?
Why is it important to check main bore alignment?

## Slide 28: ANSWER 2:
A crankshaft will tend to bend as it turns if the alignment is not correct.

## Slide 29: Figure 34.16 The main bearing bores of a warped block usually bend into a bowed shape. The greatest distortion is in the center bores

## Slide 30: Figure 34.17 When the main bearing caps bow downward, they also pinch in at the parting line

## Slide 31: Figure 34.18 The main bearing bore alignment can be checked using a precision straightedge and a feeler gauge

## Slide 32: Figure 34.19 (a) A precision arbor can be used to check the main bearing bore alignment. (b) If the sleeve can be inserted into all of the main bearing bores, then they are aligned

## Slide 33: Figure 34.20 (a) Checking the flatness of the block deck surface using a straightedge and a feeler gauge. (b) To be sure that the top of the block is flat, check the block in six locations as shown

## Slide 34: Figure 34.21 Grinding the deck surface of the block

## Slide 35: Figure 34.22 Cylinders wear in a taper, with most of the wear occurring at the top of the cylinder where the greatest amount of heat and pressure are created. The ridge is formed because the very top part of the cylinder is not contacted by the rings

## Slide 36: Figure 34.23 Adjust a dial bore gauge as per the gauge’s instructions and then measure the bore diameter at the top just below the ridge (maximum wear section) and at the bottom below the ring travel (minimum wear section).

## Slide 37: Figure 34.24 A cylinder boring machine is used to enlarge cylinder bore diameter so a replacement oversize piston can be used to restore a worn engine to useful service, or to increase the displacement of the engine in an attempt to increase power output

## Slide 38: Figure 34.25 A dry cylinder sleeve can also be installed in a cast-iron block to repair a worn or cracked cylinder

## Slide 39: Figure 34.26 An assortment of ball-type deglazing hones. This type of hone does not straighten wavy cylinder walls

## Slide 40: Figure 34.27 After boring, the cylinder surface is rough, pitted, and fractured to a depth of about 0.001 inch

## Slide 41: Figure 34.28 Honing enlarges the cylinder bore to the final size and leaves a plateau surface finish that retains oil

## Slide 42: Figure 34.29 A torque plate being used during a cylinder honing operation. The thick piece of metal is bolted to the block and simulates the forces exerted on the block by the head bolts when the cylinder head is attached

## Slide 43: Figure 34.30 The crosshatched pattern holds oil to keep the rings from wearing excessively, and also keeps the rings against the cylinder wall for a gas-tight fit

## Slide 44: Chart 34-1 Grit size numbers and their dimensions in inches and millimeters.

## Slide 45: Figure 34.31 (a) The surface finish tool is being held against the cylinder wall. (b) The reading indicates the Ra roughness of the cylinder. More work is needed if moly piston rings are to be used

## Slide 46: Figure 34.32 Using a tapered sanding cone to remove the sharp edges at the top of the cylinders created when the block was machined

## Slide 47: BLOCK PREPARATION FOR ASSEMBLY
Block Cleaning
  The block is scrubbed until it is absolutely clean. This can be determined by wiping the cylinder wall with a clean lint-free cloth. The cloth will pick up no soil when the cylinder wall is clean.
Block Detailing
  1. All oil passages (galleries) should be cleaned
  2. All tapped holes should be cleaned with the correct thread chaser.
  3. Coat the newly cleaned block with fogging oil to prevent rust.

## Slide 48: QUESTION 3: ?
Why is detailing a block important?

## Slide 49: ANSWER 3:
To remove any unwanted dirt and grit that would cause abnormal wear.

## Slide 50: Tech Tip

## Slide 51: Figure 34.33 High-performance engine builders often install bronze sleeves in the lifter bores

## Slide 52: Figure 34.34 Notice on this cutaway engine block that some of the head bolt holes do not extend too far into the block and dead end. Debris can accumulate at the bottom of these holes and it must be cleaned out before final assembly

## Slide 53: Figure 34.35 A tread chaser or bottoming tap should be used in all threaded holes before assembling the engine

## Slide 54: Copyright