## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 35
Crankshafts, Balance Shafts, and Bearings
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
35.1 Explain the purpose of crankshaft, crankshaft construction, and crankshaft oiling holes.
35.2. Discuss the different engine crankshaft types.
35.3. Explain the purpose and function of counterweights.
35.4 Explain externally and internally balanced engines, and primary and secondary engine balance.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
35.5 Explain the purpose of balance shafts.
35.6 Discuss crankshaft service.
35.7 Describe engine bearings and discuss the importance of bearing clearance.
35.8 Discuss camshaft bearings.

## Slide 4: CRANKSHAFT (1 OF 2)
Purpose and Function
  Power from expanding gases in the combustion chamber is delivered to the crankshaft through the piston, piston pin, and connecting rod.
Main Bearing Journals
  The main bearings support the crankshaft and allow it to rotate easily without excessive wear.
Rod Bearing Journals
  Also called crank pins, offset from the centerline of the crank, provide a mounting location for the rod.

## Slide 5: CRANKSHAFT (2 OF 2)
Surface Finish
  Surface finish is measured in micro-inches; and the smaller the number, the smoother the surface.
Journal Hardness
  Case Hardening
  Nitriding
  Tuftriding

## Slide 6: Figure 35.1 Typical crankshaft with main journals that are supported by main bearings in the block. Rod journals are offset from the crankshaft centerline

## Slide 7: Figure 35.2 The crankshaft rotates on main bearings. Longitudinal (end-to-end) movement is controlled by the thrust bearing.

## Slide 8: Figure 35.3 A ground surface on one of the crankshaft cheeks next to a main bearing supports thrust loads on the crank

## Slide 9: Figure 35.4 The distance from the crankpin centerline to the centerline of the crankshaft determines the stroke, which is the leverage available to turn the crankshaft

## Slide 10: QUESTION 1: ?
What is the main job of the crankshaft bearings?

## Slide 11: ANSWER 1:
Support the crankshaft.

## Slide 12: CRANKSHAFT CONSTRUCTION
Forged
  Forged crankshafts are stronger than the cast crankshaft, but they are more expensive.
Cast Crankshafts
  Casting materials and techniques have improved cast crankshaft quality so that cast crankshafts are used in most production automotive engines.
Billet Crankshafts
  A billet crankshaft is machined from a solid piece of forged steel called a billet.

## Slide 13: Figure 35.5 Wide separation lines of a forged crankshaft

## Slide 14: Figure 35.6 Cast crankshaft showing the bearing journal overlap and a straight, narrow cast mold parting line. The amount of overlap determines the strength of the crankshaft

## Slide 15: Figure 35.7 A billet crankshaft showing how it is machined from a solid chuck of steel, usually 4340 steel, at the right and the finished crankshaft on the left

## Slide 16: CRANKSHAFT OILING HOLES
Purpose and Function
  The crankshaft is drilled to allow oil from the main bearing oil groove to be directed to the connecting rod bearings.
  The oil on the bearings forms a hydrodynamic oil film to support bearing loads.

## Slide 17: Figure 35.8 Crankshaft sawed in half, showing drilled oil passages between the main and rod bearing journals

## Slide 18: Figure 35.9 Typical chamfered hole in a crankshaft bearing journal

## Slide 19: ENGINE CRANKSHAFT TYPES (1 OF 3)
V-8 Engine Arrangement
  The V-8 engine crankshaft has two planes, so there is one throw every 90 degrees.
Four Cylinder Engine Crankshafts
  The crankshaft used on four-cylinder inline engines has four throws on a single plane.
Five Cylinder Engine Crankshafts
  The inline five-cylinder engine has a five-throw crankshaft with one throw at each 72 degrees.

## Slide 20: ENGINE CRANKSHAFT TYPES (2 OF 3)
Three Cylinder Engine Crankshafts
  A three-cylinder engine uses a 120-degree three-throw crankshaft with four main bearings.
Inline Six Cylinder Crankshafts
  Inline six-cylinder engine crankshafts ride on four or seven main bearings and use six crank throws in three planes 120 degrees apart.

## Slide 21: ENGINE CRANKSHAFT TYPES (3 OF 3)
90 Degree V-6 Engine Crankshafts
  The crank throws for an even-firing V-6 engine are split, making separate crankpins for each cylinder.
60 Degree V-6 Engine Crankshafts
  The adjacent pairs of crankpins on the crankshaft used in the 60-degree V-6 engine have a splay angle of 60 degrees.

## Slide 22: FREQUENTLY ASKED QUESTION

## Slide 23: Figure 35.10 A cross-drilled crankshaft is used on some production engines and is a common racing modification

## Slide 24: Figure 35.11 A splayed crankshaft design is used to create an even-firing 90-degree V-6

## Slide 25: COUNTERWEIGHTS
Purpose and Function
  Crankshafts are balanced by counterweights, which are cast, forged, or machined as part of the crankshaft.
Vibration Damage
  The crankshaft must be rigid enough to keep the deflection forces to a minimum.
  If vibrations are too great the crankshaft may fail.
  Harmful crankshaft twisting vibrations are dampened with a torsional vibration damper.

## Slide 26: Figure 35.12 A fully counterweighted four-cylinder crankshaft

## Slide 27: FREQUENTLY ASKED QUESTION

## Slide 28: Figure 35.13 The crank throw is halfway down on the power stroke. The piston on the left without an offset crankshaft has a sharper angle than the engine on the right with an offset crankshaft

## Slide 29: Figure 35.14 A crankshaft broken as a result of using the wrong torsional vibration damper

## Slide 30: Figure 35.15 The hub of the harmonic balancer is attached to the front of the crankshaft. The elastomer (rubber) between the inertia ring and the center hub allows the absorption of crankshaft firing impulses

## Slide 31: Tech Tip

## Slide 32: Figure 35.16 A General Motors high-performance balancer used on a race engine

## Slide 33: EXTERNALLY AND INTERNALLY BALANCED ENGINES
Externally Balanced
  Weight is added to the harmonic balancer (vibration damper) and flywheel or the flexplate.
Internally Balanced
  All rotating parts of the engine are individually balanced, including the harmonic balancer and flywheel (flexplate).

## Slide 34: PRIMARY AND SECONDARY ENGINE BALANCE
Primary Balance
  When pistons move up and down in the cylinders, they create a primary vibration
  A counterweight on the crankshaft opposite the piston/rod assembly helps reduce this vibration.
Secondary Balance
  A vibration at twice engine speed
  A weak high-frequency vibration caused by a slight difference in the inertia of the pistons at top dead center, compared to bottom dead center

## Slide 35: Figure 35.17 In a four-cylinder engine, the two outside pistons move upward at the same time as the inner pistons move downward, which reduces primary unbalance

## Slide 36: Figure 35.18 Primary and secondary vibrations in relation to piston position

## Slide 37: BALANCE SHAFTS
Purpose and Function
  Some engines use balance shafts to dampen normal engine vibrations.
Balance Shaft Applications
  Most four-cylinder engines larger than 2.2 liters
  Many 90 V-6 engines

## Slide 38: Figure 35.19 Two counter-rotating balance shafts used to counter-balance the vibrations of a four-cylinder engine

## Slide 39: Figure 35.20 This General Motors four-cylinder engine uses two balance shafts driven by a chain at the rear of the crankshaft

## Slide 40: Figure 35.21 Many 90-degree V-6 engines use a balance shaft to reduce vibrations and effectively cancel a rocking motion (rocking couple) that causes the engine to rock front to back

## Slide 41: QUESTION 2: ?
What are the two methods of balancing an engine?

## Slide 42: ANSWER 2:
Externally and internally.

## Slide 43: CRANKSHAFT SERVICE (1 OF 3)
Visual Inspection
  Inspection for wear, cracks, thread damage, warpage, and damaged seal surfaces.
Measuring the Crankshaft
  Checked for size, taper, and out-of-round condition.
Crankshaft Grinding
  Grind the journal to an undersize with a smooth surface finish.

## Slide 44: CRANKSHAFT SERVICE (2 OF 3)
Crankshaft Polishing
  The journal is polished after grinding, using a 320-grit polishing cloth and oil to remove the fine metal “fuzz” remaining on the journal.
Welding a Crankshaft
  Salvage a crankshaft by building up a bearing journal and then grinding it to the original journal size.

## Slide 45: CRANKSHAFT SERVICE (3 OF 3)
Stress Relieving the Crankshaft
  Stress relief is achieved by shot peening the fillet area of the journals with #320 steel shot.
Storing Crankshafts
  All crankshafts should be coated with oil to keep them from rusting, and stored vertically until time for engine assembly.

## Slide 46: Figure 35.22 Scored connecting rod bearing journal

## Slide 47: Figure 35.23 All crankshaft journals should be measured for diameter, as well as taper and out-of-round

## Slide 48: Figure 35.24 Check each journal for taper and out-of-round

## Slide 49: Figure 35.25 The rounded fillet area of the crankshaft is formed by the corners of the grinding stone

## Slide 50: Figure 35.26 An excessively worn crankshaft can be restored to useful service by welding the journals, and then machining them back to the original size

## Slide 51: Figure 35.27 All crankshafts should be polished after grinding. Both the crankshaft and the polishing cloth are being revolved

## Slide 52: Figure 35.28 Crankshafts should be stored vertically to prevent possible damage or warpage. This clever bench-mounted tray for crankshafts not only provides a safe place to store crankshafts, but is also out of the way and cannot be accidentally tipped

## Slide 53: ENGINE BEARINGS (1 Of 4)
Introduction
  Engine bearings are the main supports for the major moving parts of any engine.
Types of Bearings
  Plain Bearings
  Sleeve Bearings
Bearing Materials
  Babbitt
  Cooper-lead Alloy
  Aluminum

## Slide 54: ENGINE BEARINGS (2 OF 4)
Bearing Sizes
  Bearings are usually available in standard (std.) size, and in measurements 0.010, 0.020, and 0.030 inch undersize.
Bearing Loads
  The forces on the engine bearings vary with engine speed and load.

## Slide 55: ENGINE BEARINGS (3 OF 4)
Bearing Fatigue
  Bearing metals, like other metals, tend to fatigue and break after being flexed or bent a number of times.
Bearing Conformability
  The ability of bearing materials to creep or flow slightly to match shaft variations is called conformability.

## Slide 56: ENGINE BEARINGS (4 OF 4)
Bearing Embedability
  The bearings must be capable of embedding small particles into the bearing surface so that they will not score the shaft.
Bearing Damage Resistance
  Bearings have a characteristic called score resistance. It prevents the bearing materials from seizing to the shaft during oil film breakdown.

## Slide 57: Figure 35.29 The two halves of a plain bearing meet at the parting faces

## Slide 58: Figure 35.30 Bearing wall thickness is not the same from the center to the parting line. This is called eccentricity and is used to help create an oil wedge between the journal and the bearing

## Slide 59: Figure 35.31 Typical two- and three-layer engine bearing inserts showing the relative thickness of the various materials

## Slide 60: Figure 35.32 Typical bearing shell types found in modern engines: (a) half-shell thrust bearing, (b) upper main bearing insert, (c) lower main bearing insert, (d) full round-type camshaft bearing

## Slide 61: Figure 35.33 Bearings are often marked with an undersize dimension. This bearing is used on a crankshaft with a ground journal that is 0.020 inch (0.76 mm) smaller in diameter than the stock size

## Slide 62: Figure 35.34 Work hardened bearing material becomes brittle and cracks, leading to bearing failure

## Slide 63: Figure 35.35 Bearing material covers foreign material (such as dirt) as it embeds into the bearing

## Slide 64: BEARING CLEARANCE (1 OF 2)
Importance
  Doubling the journal clearance will allow more than four times more oil to flow from the edges of the bearing.
Checking Bearing Clearance
  Plastigauge®
  Measure journal and inside of bearing, then subtract. The difference is the clearance.

## Slide 65: BEARING CLEARANCE (2 OF 2)
Bearing Spread and Crush
  Spread holds the bearing shell in the housing while the engine is being assembled.
  Crush is when the bearing cap is tightened, the ends of the two bearing shells touch and are forced together.
Bearing Tang
  A tang or lip helps locate the bearing shell in the housing.

## Slide 66: Figure 35.36 Bearing spread and crush

## Slide 67: Figure 35.37 Bearings are thinner at the parting line faces to provide crush relief

## Slide 68: Figure 35.38 Spun bearing. The lower cap bearing has rotated under the upper rod bearing

## Slide 69: Figure 35.39 The tang (lug) and slot help index the bearing in the bore

## Slide 70: Figure 35.40 Many bearings are manufactured with a groove down the middle to improve the oil flow around the main journal

## Slide 71: CAMSHAFT BEARINGS
Types of Camshaft Bearings
  Full round bearings
  Split-type (half shell) bearings
Camshaft Bearing Installation
  In many engines, each cam bearing is a different size.
  The cam bearing journal size must be checked.
  The location of each new cam bearing can be marked.
  Many vehicle manufacturers specify that the cam bearings should be installed “dry”

## Slide 72: Figure 35.41 Cam-in-block engines support the camshaft with sleeve-type bearings

## Slide 73: Figure 35.42 Camshaft bearings must be installed correctly so that oil passages are not blocked

## Slide 74: Figure 35.43 Some overhead camshaft engines use split bearing inserts

## Slide 75: QUESTION 3: ?
What is the purpose of bearing spread?

## Slide 76: ANSWER 3:
Hold the bearing in place during installation.

## Slide 77: Copyright