## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 36
Gaskets and Sealants
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
36.1 Discuss the need for gaskets and sealants.
36.2 Describe head gaskets and the types of head gaskets.
36.3 Discuss cover gasket materials and gasket failures.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
36.4 Discuss the purpose and function of oil seals.
36.5 Discuss the purpose and function of assembly sealants.

## Slide 4: PURPOSE AND FUNCTION
Need for Gaskets and Sealants
  Gaskets and sealants are used in engines to seal gaps and potential gaps between two or more parts.
Gasket and Sealant Requirements
  Withstand normal engine temperatures
  Withstand normal engine vibrations
  Withstand acids and chemicals normally found
  Expand and contract at different rates

## Slide 5: Figure 36.1 Gaskets are used in many locations in the engine

## Slide 6: QUESTION 1: ?
What is the purpose of a gasket?

## Slide 7: ANSWER 1:
Seal gaps and potential gaps between two or more parts.

## Slide 8: HEAD GASKETS
Requirements Needed
  High clamping loads
  Wide operating temperature range
Types of Head Gaskets
  Perforated steel core gaskets
  Multilayered steel gaskets (MLS)

## Slide 9: Figure 36.2 Gaskets help prevent leaks between two surfaces

## Slide 10: Figure 36.3 A typical perforated steel core head gasket with a graphite or composite facing material

## Slide 11: Figure 36.4 A solid steel core head gasket with a nonstick coating, which allows some movement between the block and the head

## Slide 12: Figure 36.5 The armor ring can be made from steel or copper

## Slide 13: Figure 36.6 Multilayer steel (MLS) gaskets are used on many newer all-aluminum engines, as well as on engines that use a cast block with aluminum cylinder heads.

## Slide 14: QUESTION 2: ?
Why is armor used in head gaskets?

## Slide 15: ANSWER 2:
So the head gasket can withstand high cylinder pressures.

## Slide 16: COVER GASKET MATERIALS (1 OF 2)
Cover Gasket Requirements
  The gasket must be impermeable to the fluids it is designed to seal in or out.
  The gasket must conform to the shape of the surface, and it must be resilient, or elastic, to maintain the sealing force as it is compressed.

## Slide 17: COVER GASKET MATERIALS (2 OF 2)
Types of Gaskets
  Cork gaskets
  Fiber gaskets
  Synthetic rubber gaskets
  Rubber-coated metal gaskets
  Formed in place gaskets
  Plastic/rubber gaskets

## Slide 18: Figure 36.7 Left to right: Cork-rubber, paper, composite, and synthetic rubber (elastomer) gaskets

## Slide 19: Figure 36.8 Rubber-coated steel gaskets have replaced many oil pan gaskets that once had separate side rail gaskets and end seals

## Slide 20: Figure 36.9 Formed in place gaskets often use silicone rubber and are applied at the factory using a robot.

## Slide 21: Figure 36.10 A typical intake manifold gasket showing the metal washer at each fastener location, which keeps the gasket from being compressed too much

## Slide 22: GASKET FAILURES
Causes of Gasket Failures
  Detonation (spark knock or ping) may cause extreme pressure
  A plugged PCV system can increase crankcase pressure
  Improper installation, such as incorrect torqueing sequence

## Slide 23: Figure 36.11 This intake manifold gasket was damaged due to fretting. Newer designs allow for more movement between the intake manifold and the cylinder head

## Slide 24: Tech Tip

## Slide 25: OIL SEALS
Purpose and Function
  Oil seals allow the shaft to rotate and seal the area around the shaft to prevent oil or coolant from leaking.
Seal Materials
  Buna-N
  Viton® (fluorocarbon)
  Teflon® (polytetrafluorethylene, also called PTFE)

## Slide 26: Figure 36.12 A rear main seal has to be designed to seal oil from leaking around the crankshaft under all temperature conditions

## Slide 27: ASSEMBLY SEALANTS
RTV Silicone
Anaerobic Sealers
Non-hardening Sealers
Anti-seize Compounds

## Slide 28: Figure 36.13 Room-temperature vulcanization (RTV) is designed to be a gasket substitute on non-machined surfaces.

## Slide 29: Figure 36.14 Anaerobic sealer is used to seal machined surfaces. Always follow the instructions on the tube for best results

## Slide 30: Figure 36.15 The strength of the thread locker depends on whether the fastener is to be removed by hand (blue). High strength thread locker (red) can only be removed if heated

## Slide 31: Figure 36.16 Applying anti-seize compound to the threads of a bolt helps prevent the threads from galling or rusting

## Slide 32: Chart 36-1 Summary chart showing where sealants are used and their common trade names.

## Slide 33: QUESTION 3: ?
What is needed for an anaerobic sealer to cure?

## Slide 34: ANSWER 3:
The absence of air.

## Slide 35: Copyright