## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 40
Electrical Circuits and Ohm’s Law
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
40.1 Identify the parts of a complete circuit.
40.2 Describe the characteristics of different types of circuit.
40.3 Explain Ohm’s law as it applies to automotive circuits.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
40.4 Explain Watt’s law as it applies to automotive circuits.
40.5 This chapter will help you prepare for the ASE Electrical/Electronic Systems (A6) certification test content area “A” (General Electrical/Electronic System Diagnosis).

## Slide 4: CIRCUITS
Definition
  A circuit is a complete path that electrons travel from a power source (such as a battery) through a load, such as a lightbulb, and back to the power source.
Parts of a Complete Circuit
  Power source
  Protection
  Power path
  Electrical load
  Return path

## Slide 5: Figure 40.1 All complete circuits must have a power source, a power path, protection (fuse), an electrical load (lightbulb in this case), and a return path back to the power source

## Slide 6: Figure 40.2 The return path back to the battery can be any electrical conductor, such as a copper wire or the metal frame or body of the vehicle

## Slide 7: Figure 40.3 An electrical switch opens the circuit and no current flows. The switch could also be on the return (ground) path wire

## Slide 8: QUESTION 1: ?
What is included in a complete electrical circuit?

## Slide 9: ANSWER 1:
  A power source, circuit protection, power path, electrical load, and a return path.

## Slide 10: CIRCUIT FAULT TYPES (1 OF 2)
Open Circuit
  An open circuit is any circuit that is not complete, or that lacks continuity.
Short-to-Voltage
  A short-to-voltage occurs when the power side of one circuit is electrically connected to the power side of another circuit.

## Slide 11: CIRCUIT FAULT TYPES (2 OF 2)
Short-to-Ground
  A short-to-ground is a type of short circuit that occurs when the current bypasses part of the normal circuit and flows directly to ground.
High Resistance
  High resistance in a circuit is caused by an unwanted load.

## Slide 12: Figure 40.4 Examples of common causes of open circuits. Some of these causes are often difficult to find

## Slide 13: Figure 40.5 A short circuit permits electrical current to bypass some or all of the resistance in the circuit

## Slide 14: Figure 40.6 A fuse or circuit breaker opens the circuit to prevent possible overheating damage in the event of a short circuit

## Slide 15: Figure 40.7 A short-to-ground affects the power side of the circuit. Current flows directly to the ground return, bypassing some or all of the electrical loads in the circuit.

## Slide 16: QUESTION 2: ?
What is the difference between a short-to-voltage and a short-to-ground?

## Slide 17: ANSWER 2:
A short to voltage is when the power of one circuit is unintentionally connected to another circuit. A short to ground is when part of a circuit is bypassed to ground.

## Slide 18: Tech Tip

## Slide 19: Figure 40.8 Electrical flow through a circuit is similar to water flowing over a waterwheel. The more water (amperes in electricity), the greater the amount of work (waterwheel).

## Slide 20: OHM’S LAW
Definition
  It requires 1 volt to push 1 ampere through 1 ohm of resistance.
Formulas
  Ohm’s law can also be stated as a simple formula used to calculate one value of an electrical circuit if the other two are known.

## Slide 21: Figure 40.9 To calculate one unit of electricity when the other two are known, simply use your finger and cover the unit you do not know.

## Slide 22: Figure 40.10 This closed circuit includes a power source, power-side wire, circuit protection (fuse), resistance (bulb), and return path wire. In this circuit, if the battery has 12 volts and the electrical load has 4 ohms, then the current through the circuit is 3 amperes

## Slide 23: WATT’S LAW
Background
  A watt is a unit of electrical power represented by a current of 1 ampere through a circuit with a potential difference of 1 volt.
Formulas
  The symbol for a watt is the capital letter W. The formula for watts is: W = I x E
Magic Circle
  The formulas for calculating any combination of electrical units are shown in the magic circle.

## Slide 24: Figure 40.11 To calculate one unit when the other two are known, simply cover the unknown unit to see what unit needs to be divided or multiplied to arrive at the solution

## Slide 25: Figure 40.12 “Magic circle” of most formulas for problems involving Ohm’s law. Each quarter of the “pie” has formulas used to solve for a particular unknown value

## Slide 26: QUESTION 3: ?
What is Ohm’s law?

## Slide 27: ANSWER 3:
  It requires 1 volt to push 1 ampere through 1 ohm of resistance.

## Slide 28: Copyright