## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 45
Wiring Schematics and Circuit Testing
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
45.1 Interpret wiring schematics and explain the procedure to identify relay terminals.
45.2 Locate shorts, grounds, opens, and resistance problems in electrical circuits, and determine necessary action.
45.3 Explain the different methods to locate a short circuit, and the procedure to troubleshoot an electrical problem.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
45.4 This chapter will help you prepare for the ASE Electrical/Electronic Systems (A6) certification test content area “A” (General Electrical/Electronic System Diagnosis).

## Slide 4: WIRING SCHEMATICS AND SYMBOLS (1 OF 2)
Terminology
  A wiring schematic, sometimes called a diagram, shows electrical components and wiring using symbols and lines to represent components and wires.
All circuit schematics or diagrams include:
  Power-side of wiring, splices, connectors, wire size, wire color, trace color, circuit number, electrical components, ground path returns, fuses and switches

## Slide 5: WIRING SCHEMATICS AND SYMBOLS (2 OF 2)
Circuit Information
  The first color or color abbreviation is the color of the wire insulation.
  The second color (if mentioned) is the color of the stripe or tracer on the base color.
Wire Size
  Wire size is shown on all schematics.
  Metric wire gauge size in square millimeters (mm2)
  Standard wire using the AWG standard

## Slide 6: Figure 45.1 The center wire is a solid color wire, meaning that the wire has no other identifying tracer or stripe color. The two end wires could be labeled “BLU/WHT,” indicating a blue wire with a white tracer or stripe

## Slide 7: Chart 45-1 Typical abbreviations used on schematics to show wire color. Some vehicle manufacturers use two letters to represent a wire color. Check service information for the color abbreviations used.

## Slide 8: Figure 45.2 Typical section of a wiring diagram. Notice that the wire color changes at connection C210. The “0.8” represents the metric wire size in square millimeters

## Slide 9: Figure 45.3 Typical electrical and electronic symbols used in automotive wiring and circuit diagrams. Both the conventional and the global symbols are shown side-by-side to make reading schematics easier.

## Slide 10: QUESTION 1: ?
What are the two ways the wire size may be displayed on the schematic?

## Slide 11: ANSWER 1:
mm2 or AWG Standard.

## Slide 12: SCHEMATIC SYMBOLS (1 OF 4)
Battery
  The plates of a battery are represented by long and short lines.
Wiring
  Electrical wiring is shown as straight lines and with a few numbers and/or letters to indicate the wire size, circuit number, wire color, splices, connectors and location.

## Slide 13: SCHEMATIC SYMBOLS (2 OF 4)
Electrical Components
  Most electrical components have their own unique symbol that shows the basic function or parts.
Electric Motors
  An electric motor symbol shows a circle with the letter M in the center and two electrical connections, one at the top and the other at the bottom.

## Slide 14: SCHEMATIC SYMBOLS (3 OF 4)
Resistors
  A resistor symbol is a jagged line representing resistance to current flow.
Capacitors
  If one of the lines is curved, this indicates that the capacitor being used has a polarity.
Electrically Heated Unit
  The grid-like symbol represents an electrically heated element.

## Slide 15: SCHEMATIC SYMBOLS (4 OF 4)
Boxed Components
  A solid line, the box is the entire component.
  Dashed lines, it represents part of a component.
Switches
  Normally open
  Normally closed
  Momentary contact

## Slide 16: Tech Tip

## Slide 17: Figure 45.4 In this typical connector, note that the positive terminal is usually a female connector

## Slide 18: Figure 45.5 The symbol for a battery. The positive plate of a battery is represented by the longer line and the negative plate by the shorter line.

## Slide 19: Figure 45.6 The ground symbol on the left represents an earth ground. The ground symbol on the right represents a chassis ground

## Slide 20: Figure 45.7 Starting at the top, the wire from the ignition switch is attached to terminal B of connector C2, the wire is 0.5 mm2 (20- gauge AWG), and is yellow. The circuit number is 5. The wire enters connector C202 at terminal B3

## Slide 21: Figure 45.8 The electrical terminals are usually labeled with a letter or number

## Slide 22: Figure 45.9 Two wires that cross at the dot indicate that the two are electrically connected

## Slide 23: Figure 45.10 Wires that cross, but do not electrically contact each other, are shown with one wire bridging over the other

## Slide 24: Figure 45.11 Connectors (C), grounds (G), and splices (S) are followed by a number, generally indicating the location in the vehicle. G209 is under the dash.

## Slide 25: Figure 45.12 The ground for the battery is labeled G305, indicating the ground connector is located in the passenger compartment of the vehicle.

## Slide 26: Figure 45.13 The symbol for lightbulbs shows the filament inside a circle, which represents the glass ampoule of the bulb

## Slide 27: Figure 45.14 An electric motor symbol shows a circle with the letter M in the center and two black sections that represent the brushes of the motor.

## Slide 28: Figure 45.15 Resistor symbols vary, depending on the type of resistor

## Slide 29: Figure 45.16 A rheostat uses only two wires—one is connected to a voltage source and the other is attached to the movable arm

## Slide 30: Figure 45.17 Symbols used to represent capacitors. If one of the lines is curved, this indicates that the capacitor being used has a polarity.

## Slide 31: Figure 45.18 The grid-like symbol represents an electrically heated element

## Slide 32: Figure 45.19 A dashed outline represents a portion (part) of a component

## Slide 33: Figure 45.20 A solid box represents an entire component

## Slide 34: Figure 45.21 This symbol represents a component that is case grounded

## Slide 35: Figure 45.22 (a) A symbol for a single-pole, single-throw (SPST) switch. This type of switch is normally open (N.O.) because nothing is connected to the terminal that the switch is contacting in its normal position. (b) A single-pole, double-throw (SPDT) switch has three terminals.

## Slide 36: Figure 45.22(c) A double-pole, single-throw (DPST) switch has two positions (off and on) and can control two separate circuits. (d) A double-pole, double-throw (DPDT) switch has six terminals—three for each pole.

## Slide 37: Figure 45.23 (a) A symbol for a normally open (N.O.) momentary switch

## Slide 38: Figure 45.23 (b) A symbol for a normally closed (N.C.) momentary switch

## Slide 39: TECH TIP

## Slide 40: Figure 45.24 (a) A typical headlight circuit showing the colors of the wires

## Slide 41: Figure 45.24 (b) A more complex circuit using colored pencils to indicate where there is voltage in the circuit will help diagnosis the system if there is a fault

## Slide 42: QUESTION 2: ?
How is an electrical motor identified on a schematic?

## Slide 43: ANSWER 2:
An electric motor symbol shows a circle with the letter M in the center and two black sections that represent the brushes of the motor.

## Slide 44: RELAY TERMINAL IDENTIFICATION
A relay is a magnetic switch that uses a movable armature to control a high-amperage circuit by using a low amperage electrical switch.
ISO Relay Terminal Identification
  Coil (Terminals 85 and 86)
  Load (Terminals 30, 87 and 87a)
Relay Spike Control
  To reduce the induced voltage, some relays contain a diode connected across the coil.

## Slide 45: Figure 45.25 A relay uses a movable arm to complete a circuit whenever there is a power at terminal 86 and a ground at terminal 85.

## Slide 46: Figure 45.26 A cross-sectional view of a typical four-terminal relay. Current flowing through the coil (terminals 86 and 85) causes the movable arm (called the armature) to be drawn toward the coil magnet.

## Slide 47: Figure 45.27 A typical relay showing the schematic of the wiring in the relay

## Slide 48: Figure 45.28 All schematics are shown in their normal, non-energized position

## Slide 49: Figure 45.29 A horn circuit. Note that the relay contacts supply the heavy current to operate the horn when the horn switch simply completes a low-current circuit to ground, causing the relay contacts to close.

## Slide 50: Figure 45.30 When the relay or solenoid coil current is turned off, the stored energy in the coil flows through the clamping diode and effectively reduces voltage spike.

## Slide 51: Figure 45.31 A resistor used in parallel with the coil windings is a common spike reduction method used in many relays

## Slide 52: LOCATING AN OPEN CIRCUIT
The typical procedure for locating an open circuit involves the following steps.
  Perform a thorough visual inspection.
  Print out the schematic.
  Check everything that does and does not work.
  Check for voltage.

## Slide 53: COMMON POWER OR GROUND
When diagnosing an electrical problem that affects more than one component or system, check the electrical schematic for a common power source or a common ground.
Example:
  Under-hood light
  Inside lighted mirrors
  Dome light
  Left-side courtesy light
  Right-side courtesy light

## Slide 54: Figure 45.32 A typical wiring diagram showing multiple switches and bulbs powered by one fuse

## Slide 55: TECH TIP

## Slide 56: Figure 45.33 To add additional lighting, simply tap into an existing light wire and connect a relay. Whenever the existing light is turned on, the coil of the relay is energized.

## Slide 57: CIRCUIT TROUBLESHOOTING PROCEDURE
Example: Backup lights are inoperative
  Verify the malfunction
  Check for everything else that does not operate correctly
  Check fuse for backup lights
  Check for voltage at the backup light socket

## Slide 58: Figure 45.34 Always check the simple things first. Check the fuse for the circuit you are testing.

## Slide 59: LOCATING A SHORT CIRCUIT (1 OF 3)
Definition
  A short circuit is an electrical connection to another wire or to ground before the current flows through some or all of the resistance in the circuit.
Fuse Replacement Method
  Disconnect one component at a time and then replace the fuse. Not the preferred method.
Circuit Breaker Method
  The circuit breaker alternately opens and closes the circuit, protecting the wiring from overheating.

## Slide 60: LOCATING A SHORT CIRCUIT (2 OF 3)
Test Light Method
  Remove the blown fuse and connect a test light to the terminals of the fuse holder (polarity does not matter).
Buzzer Method
  The buzzer method is similar to the test light method, but uses a buzzer to replace a fuse and act as an electrical load.
Ohmmeter Method
  Remove power from the circuit and measure continuity to ground.

## Slide 61: LOCATING A SHORT CIRCUIT (3 OF 3)
Gauss Method
  A Gauss gauge is a handheld meter that responds to weak magnetic fields.
Circuit Tracer
  The tone is generated as long as there is a continuous electrical path along the circuit.

## Slide 62: Figure 45.35 (a) After removing the blown fuse, a pulsing circuit breaker is connected to the terminals of the fuse

## Slide 63: Figure 45.35 (b) The circuit breaker causes current to flow, then stop, then flow again, through the circuit up to the point of the short-to-ground.

## Slide 64: Figure 45.36 A Gauss gauge can be used to determine the location of a short circuit even behind a metal panel

## Slide 65: Figure 45.37 A tone generator–type tester used to locate open circuits and circuits that are shorted-to-ground.

## Slide 66: Figure 45.38 To check for a short-to-ground using a tone generator, connect the black transmitter lead to a good chassis ground and the red lead to the load side of the fuse terminal.

## Slide 67: QUESTION 3: ?
How can a tone generator be used to locate a short circuit?

## Slide 68: ANSWER 3:
When the circuit is shorted the generator will emit a tone.

## Slide 69: ELECTRICAL TROUBLESHOOTING GUIDE
When troubleshooting any electrical component, remember the following hints to identify the problem faster and more easily.
  For a device to work, it must have power and ground.
  If there is no power to a device, an open power side (blown fuse, etc.) is indicated.
  If there is power on both sides of a device, an open ground is indicated.
  If a fuse blows immediately, a grounded power-side wire is indicated.

## Slide 70: STEP-BY-STEP TROUBLESHOOTING
Determine the customer concern
Verify the customer’s concern
Perform a thorough visual inspection
Check for technical service bulletins (TSBs)
Locate the wiring schematic
Check the factory service information
Determine the root cause and repair the vehicle
Verify the repair

## Slide 71: CASE STUDY

## Slide 72: Figure 45.39 Anti-static spray can be used by customers to prevent being shocked when they touch a metal object like the door handle

## Slide 73: Copyright