## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 47
Magnetism and Electromagnetism
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
47.1 Define magnetism and explain the concepts of magnetic induction, permeability, and reluctance.
47.2 Explain how an electromagnet works.
47.3 Explain how electromagnetism is used in relays and solenoids.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
47.4 Explain how magnetism and voltage are related.
47.5 Describe how an ignition coil works.
47.6 Describe ways to reduce electromagnetic interference.
47.7 This chapter will help you prepare for the ASE Electrical/Electronic Systems (A6) certification test content area “A” (General Electrical/ Electronic System Diagnosis).

## Slide 4: FUNDAMENTALS OF MAGNETISM (1 OF 4)
Definition
  Magnetism is a form of energy that is caused by the motion of electrons in some materials.
  Like electricity, magnetism cannot be seen.
  Magnetite is the most naturally occurring magnet.
  Many other materials can be artificially magnetized to some degree, depending on their atomic structure.

## Slide 5: FUNDAMENTALS OF MAGNETISM (2 OF 4)
Lines of Force
  The lines that create a field of force around a magnet are believed to be caused by the way groups of atoms are aligned in the magnetic material.
Magnetic Induction
  If a piece of iron or steel is placed in a magnetic field, it also becomes magnetized.

## Slide 6: FUNDAMENTALS OF MAGNETISM (3 OF 4)
Attracting or Repelling
  When unlike poles are placed close together, the lines exit from one magnet and enter the other.
  If like poles are placed close together, the curving flux lines meet head-on, forcing the magnets apart.

## Slide 7: FUNDAMENTALS OF MAGNETISM (4 OF 4)
Permeability
  The degree that some materials allow the magnetic force to pass through more easily than others.
Reluctance
  The degree that certain materials resist the passage of magnetic force.

## Slide 8: Figure 47.1 A freely suspended natural magnet (lodestone) points toward the magnetic north pole

## Slide 9: Tech Tip

## Slide 10: Figure 47.2 If a magnet breaks or is cracked, it becomes two weaker magnets

## Slide 11: Figure 47.3 Magnetic lines of force leave the north pole and return to the south pole of a bar magnet

## Slide 12: QUESTION 1: ?
What is the result if a magnet cracks?

## Slide 13: ANSWER 1:
Two weaker magnets are created.

## Slide 14: ELECTROMAGNETISM (1 OF 3)
Definition
  A current carrying conductor surrounded by a magnetic field, many time stronger than a conventional magnet.
Creating an Electromagnet
  Wrap a nail with 20 turns of insulated wire and connect the ends to the terminals of a 1.5 volt dry cell battery.
Straight Conductor
  The magnetic field surrounding a straight, current-carrying conductor consists of several concentric cylinders of flux that are the length of the wire.

## Slide 15: ELECTROMAGNETISM (2 OF 3)
Left-Hand and Right-Hand Rules
  The left-hand rule for magnetic field direction is used with the electron flow theory.
  The right-hand rule for magnetic field direction is used with the conventional theory of electron flow.
Field Interaction
  Conductors with opposing magnetic fields move apart into weaker fields.
Motor Principle
  Use the magnetic field interaction to convert electrical energy into mechanical energy.

## Slide 16: ELECTROMAGNETISM (3 OF 3)
Coil Conductor
  If several loops of wire are made into a coil, then the magnetic flux density is strengthened.
Electromagnetic Strength
  The magnetic field can be strengthened (increased) in three ways.
    Place a soft iron core in the center of the coil.
    Increase the number of turns of wire in the coil.
    Increase the current flow through the coil windings.

## Slide 17: Figure 47.4 Iron filings and a compass can be used to observe the magnetic lines of force

## Slide 18: Figure 47.5 (a) Magnetic lines of force spread out from around an isolated magnet. (b) Opposite poles attract. (c) Similar poles repel

## Slide 19: Figure 47.6 A crankshaft position sensor and reluctor (notched wheel)

## Slide 20: Figure 47.7 A magnetic field surrounds a straight, current-carrying conductor

## Slide 21: Figure 47.8 The left-hand rule for magnetic field direction is used with the electron flow theory

## Slide 22: Figure 47.9 The right-hand rule for magnetic field direction is used with the conventional theory of electron flow

## Slide 23: Figure 47.10 Conductors with opposing magnetic fields move apart into weaker fields

## Slide 24: Figure 47.11 Electric motors use the interaction of magnetic fields to produce mechanical energy

## Slide 25: Figure 47.12 The magnetic lines of flux surrounding a coil look like those surrounding a bar magnet

## Slide 26: Figure 47.13 The left-hand rule for coils is shown

## Slide 27: Figure 47.14 An iron core concentrates the magnetic lines of force surrounding a coil

## Slide 28: USE OF ELECTROMAGNETISM
Relays
  A simple relay contains an electromagnetic coil in series with a battery and a switch.
Solenoid
  A solenoid is an example of an electromagnetic switch that uses a moveable core.

## Slide 29: Figure 47.15 An electromagnetic switch that has a movable arm is referred to as a relay

## Slide 30: FREQUENTLY ASKED QUESTION

## Slide 31: Chart 47-1 Comparison between a relay and a solenoid.

## Slide 32: Figure 47.16 (a) A starter with attached solenoid. All the current needed by the starter flows through the two large terminals of the solenoid and through the solenoid contacts inside

## Slide 33: Figure 47.16 (b) A relay is designed to carry lower current, compared to a solenoid, and uses a movable arm

## Slide 34: ELECTROMAGNETIC INDUCTION (1 OF 2)
Principles Involved
  Electricity can be produced by using the relative movement of an electrical conductor and a magnetic field.
Voltage Intensity
  The amount of the voltage depends on the rate at which the flux lines are broken.
Lenz’s Law
  An induced current moves so that its magnetic field opposes the motion that induced the current.

## Slide 35: ELECTROMAGNETIC INDUCTION (2 OF 2)
Self-Induction
  As current increases, the flux lines continue to expand, cutting across the wires of the coil and actually inducing another voltage within the same coil.
Mutual Induction
  When two coils are close together, energy may be transferred from one to the other by magnetic coupling.

## Slide 36: Figure 47.17 Voltage can be induced by the relative motion between a conductor and magnetic lines of force

## Slide 37: Figure 47.18 Maximum voltage is induced when conductors cut across the magnetic lines of force (flux lines) at a 90-degree angle

## Slide 38: QUESTION 2: ?
What is the difference between mutual induction and self-induction?

## Slide 39: ANSWER 2:
In mutual induction there are two coils, in self-induction there is a single coil.

## Slide 40: IGNITION COILS
Ignition Coil Windings
  Ignition coils use two windings and are wound on the same iron core.
Ignition Coil Construction
  A core of laminated soft iron is surrounded by the secondary windings. The secondary windings are surrounded by the primary windings.
Ignition Coil Operation
  The coil is fed battery voltage when the key is on and the ground is controlled by an ignition module.

## Slide 41: Figure 47.19 Mutual induction occurs when the expansion or collapse of a magnetic field around one coil induces a voltage in a second coil

## Slide 42: Figure 47.20 Some ignition coils are electrically connected, called “married” (left figure), whereas others use separated primary and secondary windings, called “divorced” (right figure)

## Slide 43: Figure 47.21 A GM waste-spark ignition coil showing the section of laminations that is shaped like the letter E. These mild steel laminations improve the efficiency of the coil

## Slide 44: Figure 47.22 The coil-on-plug (COP) design typically uses a bobbin-type coil

## Slide 45: ELECTROMAGNETIC INTERFERENCE
Definition
  Electrical interference caused by radio frequency or electromagnetic fields.
How is EMI Created
  When the current in a conductor is turned on/off fast enough, a high-frequency signal wave is created.
EMI Suppression Devices
  Capacitors, coils, shielding, and ground wires or cables

## Slide 46: Figure 47.23 To help prevent underhood electromagnetic devices from interfering with the antenna input, it is important that all ground wires, including the one from this power antenna, be properly grounded

## Slide 47: QUESTION 3: ?
How can EMI be reduced or controlled?

## Slide 48: ANSWER 3:
  Capacitors, coils, shielding, and ground wires or cables.

## Slide 49: Copyright