## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 52
Cranking System
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
52.1 Describe the parts and operation of a cranking circuit and explain computer-controlled starting.
52.2 Discuss how a starter motor converts electrical power into mechanical power.
52.3 List the different types of starters motors.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
52.4 Describe gear reduction starters.
52.5 Describe the function of starter drives and solenoids.
52.6 This chapter will help prepare for the ASE Electrical/Electronic Systems (A6) certification test content area “C” (Starting System Diagnosis and Repair).

## Slide 4: CRANKING CIRCUIT
Parts Involved
  Starter Motor
  Battery
  Starter Solenoid or Relay
  Starter Drive
  Ignition Switch
Control Circuit Parts and Operation
  The ignition switch does not operate the starter unless the automatic transmission is in neutral or park, or the clutch pedal is depressed on manual transmission/transaxle vehicles

## Slide 5: Figure 52.1 A typical solenoid-operated starter

## Slide 6: Figure 52.2 The lock cylinder is often a separate part from the electrical ignition switch and operates it directly or uses a link between two components

## Slide 7: Figure 52.3 To prevent the engine from cranking, an electrical switch is usually installed to open the circuit between the ignition switch and the starter solenoid

## Slide 8: QUESTION 1: ?
What are the parts in a typical cranking circuit?

## Slide 9: ANSWER 1:
  Starter Motor, Battery, Starter Solenoid or Relay, Starter Drive, and Ignition Switch

## Slide 10: COMPUTER-CONTROLLED STARTING
Operation
  The ignition switch start position on the push-to-start button is used as an input signal to the powertrain control module (PCM).
Remote Starting
  Allows the driver to start the engine of the vehicle from a distance of about 200 ft (65 m).
  The doors remain locked to reduce the possibility of theft.

## Slide 11: Figure 52.4 Instead of using an ignition key to start the engine, some vehicles are using a start button, which is also used to stop the engine, as shown on this Jaguar

## Slide 12: Figure 52.5 The top button on this key fob is the remote start button

## Slide 13: STARTER MOTOR OPERATION (1 OF 2)
Principles
  A starter motor uses electromagnetic principles to convert electrical energy from the battery (up to 300 amperes) to mechanical power (up to 8 horsepower [6 kilowatts]) to crank the engine.
Series Motors
  A series motor develops its maximum torque at the initial start (0 RPM) and develops less torque as the speed increases.

## Slide 14: STARTER MOTOR OPERATION (2 OF 2)
Shunt Motors
  Shunt-type electric motors have the field coils in parallel (or shunt) across the armature.
Permanent Magnet Motors
  Permanent magnet starters use gear reduction to multiply starter motor torque.
Compound Motors
  Some of the field coils are connected to the armature in series and some are connected directly to the battery in parallel (shunt) with the armature.

## Slide 15: Figure 52.6 This series-wound electric motor shows the basic operation with only two brushes: one hot brush and one ground brush.

## Slide 16: Figure 52.7 The interaction of the magnetic fields of the armature loops and field coils creates a stronger magnetic field on the right side of the conductor, causing the armature loop to move toward the left

## Slide 17: Figure 52.8 The armature loops rotate due to the difference in the strength of the magnetic field. The loops move from a strong magnetic field strength toward a weaker magnetic field strength

## Slide 18: Figure 52.9 Magnetic lines of force in a four-pole motor

## Slide 19: Figure 52.10 A pole shoe and field winding

## Slide 20: Figure 52.11 This wiring diagram illustrates the construction of a series-wound electric motor. Notice that all current flows through the field coils, then through the armature (in series) before reaching ground

## Slide 21: Figure 52.12 This wiring diagram illustrates the construction of a shunt-type electric motor and shows the field coils in parallel (or shunt) across the armature

## Slide 22: Figure 52.13 A compound motor is a combination of series and shunt types, using part of the field coils connected electrically in series with the armature and part in parallel (shunt)

## Slide 23: HOW THE STARTER MOTOR WORKS
Parts Involved
  Field Coils
  Armature
  Field Housing
Starter Brushes
  To supply the proper current to the armature, a four-pole motor must have four brushes riding on the commutator.
Permanent Magnet Fields
  Used in place of the electromagnetic field coils.

## Slide 24: Figure 52.14 A typical starter motor showing the drive-end housing

## Slide 25: Figure 52.15 Pole shoes and field windings installed in the housing

## Slide 26: Figure 52.16 A typical starter motor armature. The armature core is made from thin sheet metal sections assembled on the armature shaft, which is used to increase the magnetic field strength

## Slide 27: Figure 52.17 An armature showing how its copper wire loops are connected to the commutator

## Slide 28: Figure 52.18 A cutaway of a typical starter motor showing the commutator, brushes, and brush spring

## Slide 29: Tech Tip

## Slide 30: Figure 52.19 This starter permanent magnet field housing was ruined when someone used a hammer on the field housing in an attempt to “fix” a starter that did not work. A total replacement is the only solution in this case

## Slide 31: GEAR-REDUCTION STARTERS
Purpose and Function
  The purpose of the gear reduction (typically 2:1 to 4:1) is to increase starter motor speed and provide the torque multiplication necessary to crank an engine.
  Produces the necessary cranking power with reduced starter amperage requirements
  Uses a planetary gear set (a type of gear reduction) to provide the necessary torque for starting

## Slide 32: Figure 52.20 A typical gear-reduction starter

## Slide 33: STARTER DRIVES (1 Of 2)
Purpose and Function
  A starter drive includes small pinion gears that mesh with and rotate the larger gear on the engine flywheel or flex plate for starting.
Starter Drive Gear Ratio
  The engine ring gear to starter pinion ratio is between 15:1 and 20:1.

## Slide 34: STARTER DRIVES (2 OF 2)
Starter Drive Operation
  Uses a type of one-way clutch that allows the starter to rotate the engine, but then turns freely if the engine speed is greater than the starter motor speed.
Failure Mode
  The major wear occurs in the overrunning clutch section of the starter drive unit.
  The entire starter drive is replaced as a unit.

## Slide 35: Figure 52.21 A cutaway of a typical starter drive showing all of the internal parts

## Slide 36: Figure 52.22 The ring gear to pinion gear ratio is usually 15:1 to 20:1

## Slide 37: Figure 52.23 Operation of the overrunning clutch. (a) Starter motor is driving the starter pinion and cranking the engine. The rollers are wedged against spring force into their slots. (b) The engine has started and is rotating faster than the starter armature. Spring force pushes the rollers so they can rotate freely

## Slide 38: QUESTION 2: ?
What is the typical engine ring rear to starter pinion ratio?

## Slide 39: ANSWER 2:
15:1 to 20:1

## Slide 40: STARTER SOLENOIDS
Solenoid Operation
  A starter solenoid is an electromagnetic switch containing two separate, but connected, electromagnetic windings.
Solenoid Windings
  The two internal windings contain approximately the same number of turns but are made from different-gauge wire.

## Slide 41: Figure 52.24 Wiring diagram of a typical starter solenoid. Notice that both the pull-in winding and the hold-in winding are energized when the ignition switch is first turned to the “start” position.

## Slide 42: Figure 52.25 A palm-size starter armature

## Slide 43: FREQUENTLY ASKED QUESTION

## Slide 44: START-STOP SYSTEMS (1 OF 2)
Purpose and Function
  Stop-start systems are designed to increase fuel economy and reduce exhaust emissions.
Conditions for Start-Stop to Occur
  Accelerator pedal not depressed
  Vehicle speed is low or zero
  Battery state-of-charge above threshold
  Hood is closed

## Slide 45: START-STOP SYSTEMS (2 OF 2)
Start-Stop System Components
  An AGM or ELA battery
  Battery Sensor
  Low Engine Speeds
  Hood Switch
  HVAC Control Unit
Starter Motor Design
  Advanced Engagement (AE) Starter
  Tandem Solenoid (TS) Starter

## Slide 46: Figure 52.26 A Buick Auto Stop system lets the driver know when the engine is stopped

## Slide 47: Figure 52.27 Using two solenoids allows independent control of the pinion gear and motor energization

## Slide 48: FREQUENTLY ASKED QUESTION

## Slide 49: Figure 52.28 The stop-start system on this Ford F-150 pickup truck can be turned off using a switch on the dash

## Slide 50: QUESTION 3: ?
What are the main advantages of a start-stop system?

## Slide 51: ANSWER 3:
Improved fuel economy and reduced tailpipe emissions.

## Slide 52: Copyright