## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 63
Heating and Air-Conditioning Components and Operation
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
63.1 Describe how an automotive heating, ventilation, and air-conditioning system works.
63.2 Describe the parts and operation of the heating system.
63.3 Explain the air-conditioning refrigeration cycle.
63.4 Describe the operation of expansion valve systems, orifice tube systems, and thermostatic control systems.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
63.5 Discuss the refrigerants used and their impact on the environment.
63.6 Explain the function of refrigerant oils, condensers, and evaporators.
63.7 Explain the function of receiver-dryers, accumulators, refrigerant lines and hoses, thermostatic expansion valves, and fixed-orifice tubes.
63.8 Explain the operation of a compressor and its controls.

## Slide 4: HVAC PURPOSE AND FUNCTION (1 Of 4)
Principles Involved
  All matter is found in one of three different phases or states: solid, liquid, or vapor (gas).
Changes of State
  A solid is a substance that cannot be compressed and has strong resistance to flow.
  A liquid is a substance that cannot be compressed.
  A vapor is a substance that can be easily compressed, has no resistance to flow, and no fixed volume.

## Slide 5: HVAC PURPOSE AND FUNCTION (2 OF 4)
Heat and Temperature
  Molecules in a substance tend to vibrate rapidly in all directions, and this disorganized energy is called heat.
  Temperature is measured in degrees. Heat is measured in calories (c).
  Heat is also measured in British Thermal Units (BTU).
Latent Heat
  Latent heat is the “extra” heat that is needed to transform a substance from one state to another.

## Slide 6: HVAC PURPOSE AND FUNCTION (3 OF 4)
Temperature, Volume, and Pressure of Vapor
  A vapor has no fixed volume.
  Increasing the temperature of a vapor, while keeping the volume confined in the same space, increases the pressure.
  Increasing the pressure by compressing a vapor increases the temperature.

## Slide 7: HVAC PURPOSE AND FUNCTION (4 OF 4)
Pressure-Temperature Relationships
  The temperature at which a liquid boils (and vapor condenses) rises and falls with the pressure.
  Pressure in a sealed system that contains both liquid and vapor rises and falls with the temperature.
Humidity
  Refers to water vapor present in the air.
  Absolute humidity is the measurement of the weight of the water vapor in a given volume of air.
  Relative humidity is the percentage of moisture in the air compared to how much moisture air is capable of.

## Slide 8: Figure 63.1 Water is a substance that can be found naturally in solid, liquid, and vapor states

## Slide 9: Figure 63.2 The extra heat required to change a standard amount of water at its boiling point to a vapor is called latent heat of vaporization

## Slide 10: Figure 63.3 The latent heat of vaporization that water vapor stores is given off when the vapor condenses to a liquid. The temperature stays the same

## Slide 11: Figure 63.4 A sling psychrometer is used to measure relative humidity. A digital meter that reads both temperature and humidly is a low cost tool that are usually used when servicing air conditioning systems

## Slide 12: HEATING SYSTEM
Purpose and Function
  The heater system is designed to provide passenger comfort and the heat needed to defrost windshield and front side windows in many vehicles.
Parts and Operation
  Heater hose
  Heater Core
  Heater valve
  Blower motor

## Slide 13: Figure 63.5 Typical flow of air through an automotive heat, ventilation, and air conditioning system when placed in the heat position

## Slide 14: Figure 63.6 A typical heater core as installed in an HVAC housing

## Slide 15: AIR CONDITIONING REFRIGERATION CYCLE
  1. The liquid refrigerant evaporates in a small radiator-type unit called the evaporator.
  2. The compressor compresses the low-pressure refrigerant gas into a high-pressure gas and forces the refrigerant through the system.
  3. This high-pressure gas flows into the condenser. The high-pressure gas changes to form a high-pressure liquid as the heat is removed.
  4. The high-pressure liquid then flows through a device that meters the flow into the evaporator. When the high pressure of the liquid drops, it causes the refrigerant to vaporize.
  5. Air is blown through the evaporator by the blower motor. The air is cooled as heat is removed from the air and transferred to the refrigerant in the evaporator.

## Slide 16: Figure 63.7 The compressor provides the mechanical force needed to pressurize the refrigerant

## Slide 17: Figure 63.8 The evaporator removes heat from the air that enters a vehicle by transferring it to the vaporizing refrigerant

## Slide 18: Figure 63.9 The condenser changes the refrigerant vapor into a liquid by transferring heat from the refrigerant to the air stream that flows between the condenser fins

## Slide 19: EXPANSION VALVE SYSTEMS
An expansion valve is attached to the inlet to the evaporator and controls the amount of refrigerant flow into the evaporator.
The expansion valve varies the flow of the refrigerant based on the temperature at the outlet of the evaporator.
This type of system is called the thermostatic expansion valve system— usually abbreviated TEV or TXV

## Slide 20: Figure 63.10 A typical air-conditioning system that uses an expansion valve. A temperature sensor bulb is attached to the outlet of the evaporator to control the amount of refrigerant allowed to flow into the evaporator

## Slide 21: ORFICE TUBE SYSTEMS
Many air-conditioning systems today use a fixed-orifice tube at the inlet to the evaporator.
Refrigerant flow is controlled by the cycling the compressor on and off based on the input from a low pressure switch.
This type of system is commonly called a cycling clutch orifice tube (or CCOT) system.

## Slide 22: Figure 63.11 A typical automotive air-conditioning system that uses a cycling clutch and an orifice tube

## Slide 23: Figure 63.12 Typical orifice tube

## Slide 24: ANSWER 1:
To separate the high and low pressure sides of the refrigeration system.

## Slide 25: QUESTION 1: ?
What is the purpose of the fixed-orifice tube, and the thermal expansion valve.

## Slide 26: THERMOSTATIC CONTROL
A commonly used method to control evaporator temperature is to use a thermostat to control the compressor.
Air-conditioning compressors use an electromagnetic clutch.
When the thermostat senses that the temperature is near freezing, 32°F (0°C), the switch opens the electrical circuit to the compressor.

## Slide 27: Figure 63.13 A cutaway of an air-conditioning compressor electromagnetic clutch

## Slide 28: REFRIGERANTS
One of the first refrigerants was CFC-12, commonly referred to as R-12 or by its brand name Freon.
HFC-134a, also called R-134a, has been selected by vehicle manufacturers to replace the ozone-harming CFC.
HFC-134a is a smaller molecule than CFC-12. Therefore, HFC-134a can more easily leak out through small holes or openings in the system.

## Slide 29: Figure 63.14 R-134a is available in 12-oz cans, as well as larger 30-lb containers

## Slide 30: REFRIGERANTS AND THE ENVIRONMENT
Montreal Protocol
  A conference was held in Montreal, Canada, in 1987, where the United States and 22 other countries agreed to limit the production of ozone-depleting refrigerants.
Section 609 of the Clean Air Act required the following:
  Technicians who work on air conditioning to be trained and certified.
  Recovery and recycling equipment must be used.
  Each shop must comply with EPA relues.

## Slide 31: Figure 63.15 A depletion of the ozone layer allows more ultraviolet radiation from the sun to reach Earth’s surface

## Slide 32: Figure 63.16 Chlorofluorocarbon molecules break apart in the atmosphere

## Slide 33: HFO-1234YF
Description
  Also called R1234yf is the refrigerant required in all vehicles starting in MY 2021.
Ozone Depletion and Global Warming Potential
  R1234yf does not deplete the ozone layer, but is believed to have the potential to cause climate change.
Flammability
  R-1234yf is mildly flammable.
  Do not smoke or have an open flame while working on or servicing a vehicle equipped with R-1234yf.

## Slide 34: Figure 63.17 Due to the cost of R-1234yf, most shops will purchase 10 or 20 pound containers compared to the normal 30 pound container that most shops purchased for R-134a

## Slide 35: REFRIGERANT OILS
The oil carried by the refrigerant through the various components is often the only source of lubrication for the compressor.
HFC-134a and HFO-1234yf systems must use synthetic polyalkyline glycol, usually referred to as PAG oil.
Viscosity of PAG oil varies.
Always use the type and viscosity of oil specified by the manufacturer.

## Slide 36: Figure 63.18 PAG oil used in Chrysler vehicles equipped with HFC-134a refrigerant. Notice that different oils are used for different systems, depending primarily on the manufacturer of the compressor.

## Slide 37: Figure 63.19 Ester refrigerant oils are often specified for use when retrofitting an R-12 system to R-134a by companies who supply refit kits.

## Slide 38: CONDENSER
A condenser is like a radiator because it is designed to radiate heat from the refrigerant to the outside air.
As the heat travels into the air, the high-pressure gas refrigerant changes state and becomes a high-pressure liquid.
To help in the heat transfer, most vehicles are equipped with cooling fans.

## Slide 39: Figure 63.20 The condenser serves the same function for both the orifice-tube and the expansion valve–type air-conditioning system

## Slide 40: Tech Tip

## Slide 41: Figure 63.21 A repaired condenser refrigerant line

## Slide 42: EVAPORATOR
The purpose of the evaporator is to transfer heat from the air to the refrigerant flowing through it.
A blower motor equipped with a squirrel cage–type fan circulates air through the evaporator and forces the cooler air into the passenger compartment.
Because the evaporator is cold (usually just above the freezing point of 32°F [0°C]), any moisture in the air is removed, lowering the relative humidity.

## Slide 43: Figure 63.22 The evaporator allows the liquid refrigerant to evaporate and absorb heat from the passenger compartment

## Slide 44: RECEIVER-DRIER
A receiver–drier is used on an air-conditioning system that uses an expansion valve.
The receiver–drier is located between the condenser and the evaporator.
The purpose of the receiver is to provide temporary storage for the liquid refrigerant and it also usually includes a filter to trap debris and a desiccant to remove moisture.

## Slide 45: Figure 63.23 Expansion-valve systems store excess refrigerant in a receiver–drier, which is located in the high-side liquid section of the system.

## Slide 46: ACCUMULATOR
An accumulator is used on systems that use an orifice tube.
It is located between the evaporator and the compressor.
It prevents liquid refrigerant from entering the compressor, removes moisture and traps debis.

## Slide 47: Figure 63.24 A typical accumulator used on a cycling clutch orifice-tube (CCOT) system

## Slide 48: QUESTION 2: ?
Why is desiccant needed in automotive air-conditioning systems.

## Slide 49: ANSWER 2:
To absorb unwanted moisture in the system.

## Slide 50: REFRIGERANT LINES AND HOSES
Aluminum tubing is used to connect many stationary items together, like the condenser to the receiver–drier and the receiver–drier to the evaporator.
Rubber lines are usually used to and from the compressor.
Most hoses use a non-permeable inside layer of material that prevents the loss of refrigerant through the hose itself.

## Slide 51: Figure 63.25 Rigid lines and flexible hoses are used throughout the air-conditioning system. The line to and from the compressor must be flexible because it is attached to the engine.

## Slide 52: THERMOSTATIC EXPANSION VALVES
Thermostatic expansion valve (TXV) systems use a temperature-sensitive bulb located on the evaporator outlet tube.
A pressure sensitive diaphragm inside the TXV body to control the size of the variable orifice.
This regulates the rate at which liquid refrigerant flows into the evaporator.

## Slide 53: Figure 63.26 A typical expansion valve, which uses an inlet and outlet attachment for the evaporator, and a temperature-sensing bulb that is attached to the evaporator outlet tube

## Slide 54: Figure 63.27 A slot cut in the ball seat inside the expansion valve permits a small amount of refrigerant and oil to pass through at all times, even when the valve is closed. This flow of oil through the system is necessary to make sure the compressor receives the oil it needs for lubrication

## Slide 55: Figure 63.28 The sensing bulb is attached to the evaporator outlet tube. Refrigerant inside the bulb expands or contracts in response to the evaporator temperature

## Slide 56: Figure 63.29 Pressure from the capillary tube pushes on the spring-loaded diaphragm to open the expansion valve. As the pressure in the capillary tube contracts, the reduced pressure on the diaphragm allows the valve to close

## Slide 57: Figure 63.30 An H-valve (H-block) combines the temperature-sensing and pressure-regulating functions into a single assembly

## Slide 58: Figure 63.31 An H-valve as used on a Chrysler minivan

## Slide 59: Figure 63.32 In this Chrysler system, a low-pressure cutoff switch and a cycling-clutch switch are mounted on the H-valve

## Slide 60: FIXED-ORFICE TUBES
The fixed-orifice tubes provide a restriction that separates the high-pressure from the low-pressure side of the system.
AT the fixed-orifice tube the refrigerant undergoes rapid expansion and changes from a warm, high-pressure liquid to a cold, low-pressure liquid.
The orifice tube, located between the condenser and the evaporator inlet.

## Slide 61: Figure 63.33 The orifice tube is usually located at the inlet tube to the evaporator

## Slide 62: COMPRESSORS (1 OF 2)
The compressor performs the following functions:
  Compresses the low-pressure gas refrigerant from the evaporator into a high-pressure gas.
  Raises the temperature of the gas.
  Acts as the pump used to circulate the refrigerant.
  Is the major reason why there is refrigerant oil in the system.

## Slide 63: COMPRESSORS (2 OF 2)
Positive-Displacement Compressors
  Displaces a constant, uniform volume of refrigerant for each revolution or operating cycle.
Variable Displacement Compressors
  As the swash plate changes its angle, the stroke of the piston is increased for more cooling or decreased to reduce the amount of cooling by varying the volume of refrigerant.

## Slide 64: Figure 63.34 In a positive-displacement compressor, the descending piston creates a drop in pressure inside the cylinder. The resulting pressure differential allows low-side pressure to force the suction valve open.

## Slide 65: Figure 63.35 A reed valve is a one-way check valve that flaps away from the valve plate to open, and toward the valve plate to close

## Slide 66: Figure 63.36 The swash plate, attached to the crankshaft at an angle, converts the pulley’s rotary motion to axial motion, which drives the pistons in a reciprocating motion

## Slide 67: Figure 63.37 A V-5 variable displacement compressor. Internal pressures act on the swash plate, which changes the stroke of the piston and then displacement based on the pressures in the system

## Slide 68: COMPRESSOR CONTROLS
Low Pressure Switch
  This switch also prevents the air-conditioning compressor from being engaged when the temperature/Pressures are too low.
High Pressure Switch
  If the pressure exceeds a certain level (typically 375 PSI [2,600 kPa]), the pressure switch opens, thereby preventing possible damage to the system.
Power Steering Switch
  Opens the compressor circuit when the steering wheel is turned to reduce engine load.

## Slide 69: Figure 63.38 Typical air-conditioning pressure switches. A service manual is needed to determine the function of each switch. One switch could be the low-pressure switch and the other a high-pressure switch

## Slide 70: QUESTION 3: ?
What is the purpose and function of the low pressure and high
pressure switches?

## Slide 71: ANSWER 3:
To prevent the system from operating when damage may occur.

## Slide 72: Copyright