## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 97
Brake Principles and Friction Materials
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES
97.1 Discuss the energy principles that apply to brakes.
97.2 Discuss the friction principles that apply to brakes.
97.3 Describe how brakes can fade due to excessive heat.
97.4 Describe how deceleration rates are measured.
97.5 Discuss friction materials used in brake systems.

## Slide 3: ENERGY AND WORK
Energy
  Energy is the ability to do work.
Work
  Work is the transfer of energy from one physical system to another.
Kinetic Energy
  Is the energy of mass in motion.

## Slide 4: Figure 97.1 Energy, which is the ability to perform work, exists in many forms

## Slide 5: Figure 97.2 Kinetic energy increases in direct proportion to the weight of the vehicle

## Slide 6: Figure 97.3 Kinetic energy increases as the square of any increase in vehicle speed

## Slide 7: QUESTION 1: ?
What is kinetic energy?

## Slide 8: ANSWER 1:
The energy of a mass in motion.

## Slide 9: INERTIA (1 OF 2)
Definition
  Inertia is a body at rest tends to remain at rest, and a body in motion tends to remain in motion in a straight line unless acted upon by an outside force.
Weight Transfer
  When the brakes are applied at the wheel friction assemblies, only the wheels and tires begin to slow immediately.
  The rest of the vehicle, all of the weight carried by the suspension, attempts to remain in forward motion.

## Slide 10: INERTIA (2 OF 2)
Weight Bias
  The total weight of the vehicle does not change during a brake application, only the amount supported by each axle.
  Front-wheel-drive (FWD) vehicles, in particular, have a forward weight bias.
  To deal with the extra load, the front brakes are much more powerful than the rear brakes.

## Slide 11: Figure 97.4 Inertia creates weight transfer that requires the front brakes to provide most of the braking force

## Slide 12: Figure 97.5 Front-wheel-drive vehicles have most of their weight over the front wheels

## Slide 13: COEFFICIENT OF FRICTION
Definition
  The amount of friction between two objects or surfaces is commonly expressed as a value called the coefficient of friction.
Static and Kinetic Friction
  The static value is the coefficient of friction with the two friction surfaces at rest.
  The kinetic value is the coefficient of friction while the two surfaces are sliding against one another.

## Slide 14: Figure 97.6 The static coefficient of friction of an object at rest is higher than the kinetic (dynamic) friction coefficient once in motion

## Slide 15: QUESTION 2: ?
What is coefficient of friction?

## Slide 16: ANSWER 2:
The amount of friction between two surfaces.

## Slide 17: BRAKE FADE (1 OF 2)
Definition
  If repeated hard stops are performed, the brake system components can overheat and lose effectiveness, or possibly fail altogether.
Mechanical Fade
  Mechanical fade occurs when a brake drum overheats and expands away from the brake lining.
Lining Fade
  The friction material overheats to the point where its coefficient of friction drops off.

## Slide 18: BRAKE FADE (2 OF 2)
Gas Fade
  Under very hard braking when a thin layer of hot gases and dust particles builds up between the brake drum or rotor and linings.
Water Fade
  Occurs when water gets between the brake drum and the linings.

## Slide 19: Figure 97.7 Some heat increases the coefficient of friction, but too much heat can cause it to drop off sharply

## Slide 20: Figure 97.8 One cause of brake fade occurs when the phenolic resin, a part of the friction material, gets so hot that it vaporizes. The vaporized gas from the disc brake pads gets between the rotor (disc) and the friction pad. Because the friction pad is no longer in contact with the rotor, no additional braking force is possible

## Slide 21: Tech Tip

## Slide 22: Figure 97.9 The gear selector is often called the “PRNDL,” pronounced “prindle,” regardless of the actual letters or numbers used

## Slide 23: DECELERATION RATES
Terminology
  Deceleration rates are measured in units of “feet per second per second”.
Typical Deceleration Rates
  Comfortable deceleration is about 8.5 ft/sec2 (3 m/sec2).
  Loose items in the vehicle “fly” above 11 ft/sec2 (3.5 m/sec2).
Brake temperature
  1,300°F (700°C) or higher during normal driving

## Slide 24: Figure 97.10 Rapid braking causes the brake friction material to wear more compared to gentle, less aggressive, braking

## Slide 25: BRAKE FRICTION MATERIALS
Brake friction materials are composed of relatively soft, but tough, and heat-resistant material to provide the friction between the moveable part of the braking system (drum or rotor) and the stationary part of the braking system.

## Slide 26: ASBESTOS (1 OF 2)
Definition
  Asbestos is the term used to describe naturally occurring silicate minerals that consist of long fibers.
Asbestos Hazards
  Asbestos exposure can cause scar tissue to form in the lungs. This condition is called asbestosis.

## Slide 27: ASBESTOS (2 OF 2)
The use of asbestos for brake linings was never abandoned completely.

## Slide 28: SEMI-METALIC FRICTION MATERIALS
Definition
  The term semi-metallic refers to brake lining material that uses metal, rather than asbestos, in its formulation.

## Slide 29: NON-ASBESTOS/CERAMIC FRICTION MATERIALS
Terminology
  Brake pads and linings that use synthetic material, such as aramid fibers, instead of steel.

## Slide 30: CARBON FIBER FRICTION MATERIALS
Terminology
  Carbon fiber material is often called CFRC (carbon fiber-reinforced carbon). It is composed of a carbon mix into which reinforcing carbon fibers are embedded.
  CFRC brakes provide constant friction coefficient whether cold or hot, low wear rates, and low noise development.

## Slide 31: BRAKE PADS AND ENVIRONMENTAL CONCERNS
Copper is used in brake pads for heat transfer, strength, and to reduce fade.
Copper is considered a pollutant.
Legislation to reduce/eliminate copper in various states.
  Washington State legislation mandates that all brake pads and shoes manufactured after January 1, 2015, are required to have a leaf mark icon indicating the level of compliance with state friction material content legislation.

## Slide 32: Figure 97.11 All boxes of brake linings and pads should be labeled with the leaf mark, which gives a visual clue as to the standard under which the brake friction materials meet certain state laws regarding the amount of copper

## Slide 33: QUESTION 3: ?
Why is copper being removed from brake pads?

## Slide 34: ANSWER 3:
It is considered a pollutant.

## Slide 35: EDGE CODES (1 OF 2)
Purpose
  Starting in 1964, brake linings have been using a standardized way to identify the brake lining materials.
Edge Code Information
  Company code
  Pad number
  Formulation code
  Vendor number
  Friction code
  Week number that the brakes were made
  Environmental code (A, B, or N)
  Year of manufacture

## Slide 36: EDGE CODES (2 OF 2)
Coefficient of Friction Edge Code

## Slide 37: Figure 97.12 The edge codes include a lot of information about the brake friction material

## Slide 38: Figure 97.13 The “edge codes” are now printed on the backing of the brake pad because there is so much required information that it often does not fit on the edge of the brake pad or shoe

## Slide 39: Figure 97.14 Typical drum brake lining edge codes, showing the coefficient of friction codes for cold and hot circled

## Slide 40: Copyright