Circuit Testing Using a Fused Jumper Wire

Meets ASE Task:  (A6-A-)  Check electrical circuits using fused jumper wire; determine the needed action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

CAUTION:  A fused jumper wire should never be used to bypass an electrical load device.  A fused jumper wire should only be used to bypass circuit control devices such as switches or relays.

_____  1.  Check service information for a diagnostic test procedure that includes the use of a

fused jumper wire.

__________________________________________________________________

__________________________________________________________________

__________________________________________________________________

_____  2.  A horn circuit is a commonly used circuit to show the use of a fused jumper wire.

a.  Locate the horn (describe the location):

_______________________________

b.  Disconnect the wire from the horn.

c.  Connect one end of the fused jumper wire

to the terminal of the horn.

d.  Touch the other end of the fused jumper

wire to the positive (+) terminal of the

battery.

e.  The horn should work.  OK ____    NOT OK ____

_____  3.  Based on the test results, what is the needed action?  ________________________

__________________________________________________________________