Inspect and Test the Relays

Meets ASE Task:  (A6-A-10)  Inspect and test switches, connectors, relays, solenoid solid state devices, and wires of electrical/electronic circuits; perform necessary action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specified procedures for inspecting and testing

relays.

__________________________________________________________________

__________________________________________________________________

_____  2.  Relays should “click” when actuated.  List all of the relays and determine if they click

by listening or feeling the relay housing.

Circuit or Relay ID				Clicks?  Yes or No

_____________________________________	            _______

_____________________________________		_______

_____________________________________	            _______

_____________________________________		_______

_____________________________________	            _______

_____________________________________		_______

_____  3.  How many four-terminal relays are used? ____________

_____  4.  How many five-terminal relays are used? ____________

_____  5.  Test a relay for proper operation using an ohmmeter:

Coil resistance (usually labeled terminals 86 and 85)

= ________ (usually between 60 and 100 ohms).

Continuity normally closed (NC) contact (usually labeled terminals 30 and 87)

= ________ (should be close to zero ohms).

_____  6.  Based on the inspections and tests, what is the necessary action? _________________

_____________________________________________________________________