Battery State-of-Charge Test

Meets ASE Task:  (A6-B-1)  Perform battery state-of-charge test; determine needed action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specified method for determining the state-of-

charge of the battery.

_____________________________________________________

_____________________________________________________

_____________________________________________________

_____  2.  A typical state-of-charge test includes the following steps:

Step 1     Select DC volts on a digital multimeter.

Step 2	Connect the red meter lead to the positive (+)

terminal of the battery.

Step 3	Connect the black meter lead to the negative (-) terminal of the battery.

Step 4	Turn on the headlights for about one minute or until the battery voltage

stops dropping to remove the surface charge.

Step 5	Turn off the headlights and observe the voltmeter display for the

highest reading and compare it to the percentage of charge.

12.6 volts or higher = 100% charged

12.4 volts                =   75% charged

12.2 volts                =   50% charged

12.0 volts                =   25% charged

10.5 volts                =   dead

_____  3.  What is the state-of-charge of the battery? _______________________

_____  4.  What is the needed action? _____________________________________________

__________________________________________________________________