Electronic Memory Saver Usage

Meets ASE Task:  (A6-B-3)  Maintain or restore electronic memory functions.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specified method and tools or equipment needed to

maintain or restore electronic memory function.

__________________________________________________________________

__________________________________________________________________

__________________________________________________________________

_____  2.  Most domestic brand vehicles can use the cigarette (auxiliary outlet) to apply voltage

when the battery of the vehicle is removed or disconnected furring service.  For this

procedure to work, the lighter or auxiliary outlet must be powered with the ignition

switch in the on position.

a.  Using a DMM set to read DC volts, check for battery voltage at the lighter

socket with the ignition off.    ____OK    ____ NOT OK

b.  Check for DC volts at the lighter socket with the ignition set to the on (run)

position.  ____ OK    ____ NOT OK

_____  3.  If the vehicle is equipped with a to-post-type battery design, a jump box can be

attached to the ends of the cables to keep the memory in the electronic components

while the battery is removed.  Is this a possible method?

____ Yes    ____ No

_____  4.  Describe the method recommended to restore lost memory.  ____________________

_________________________________________________________________

_________________________________________________________________